## Slide 1: Study of longitudinal phase space reconstruction using ART
25. 04. 11
Geunwoo Kim

## Slide 2: ART (Algebraic Reconstruction Technique)
2
Update = (|True – Estimated|) / N

## Slide 3: Transformation coordinates
3
(x, y)
How to convert coordinate?
Longitudinal phase space (z, pz)
1. Momentum:
2. Bunch length estimation (one calculation)

## Slide 4: Transformation method
4
1. Momentum:
2. Bunch length:
Reconstruction by using booster cavity
  Phase sweep of booster cavity
ASTRA simulation
Check particle loss
Momentum and energy spread
momentum chirp before cavity
momentum chirp after cavity

## Slide 5: Transformation method
5
Issues simulation w/o dipole magnet
It is difficult to observe x offset according to the phase sweep.
Cannot process tomography method w/o dipole.
Consider generating example data to verify algorithm.
Δ = ~ 0.5 μm

## Slide 6: Algorithm test
6
Generating example file
Data requirements
x center shifting w.r.t phase
Enough amount of data to reconstruct (60 sets used in paper)
256 bins, 256 pixels (256 x 256 image)
particles 50,000
# of data = 61
-90 ~ 90 deg phase sweep data generated

## Slide 7: Algorithm test
7
Test developed ART algorithm

## Slide 8: Algorithm test
8
Convergence 수식 넣기
Iteration: 11
Iteration: 151

## Slide 9: ART algorithm test
9
Well-matched original vs reconstruction

## Slide 10: ART algorithm test
10
Longitudinal emittance

## Slide 11: Algorithm test
11
Test developed ART algorithm with different angle range (-60, 60)
Not working for reduced angle range

## Slide 12: Summary & Next steps
12
Vacuum system
Verification of ART algorithm.
ASTRA Simulation approach w/o dipole
Dipole magnet implementation via elegant
ART Algorithm update
Beam diagnostics workshop & KPS