## Slide 1: Research Progress on Development of an Absolute Coordinate Calibration Device for Beam Profile Monitor
Friday, 11 April 2025
윤 주 환

## Slide 2
Scintillating Screen based BPRM
Perspective Calibration
1. Review of the Concept
BPRM Stage scheme
Device Order & Setting
Device Performance Test
2. Experiment Setup
Distorted Image Measurement
Image Transformation into 2D Plane
3. Experiment
Comparison of Original & Measured
1D (x, y axis) Intensity Graph Fitting
Fitting Error
4. Result Analysis

## Slide 3: Review of the Concept
CMOS Camera
YAG Screen
Pixel Space
Real Space
Defects of the existing BPRM
Inclined scintillating screen
Inaccurate position coordinates
Resulting in distorted beam profile
Goal of the research
Restoring original screen space
Identifying real beam profile
Method of image calibration
Obtain the relationship between pixel space and real space
Transform all coordinates

## Slide 4: Perspective Calibration
Flattening the 3D distorted image into 2D projection space.
Nominate 4 pairs of coordinate on both planes, to solve 3x3 matrix.

## Slide 5: Experimental Setup
Grid plate
Grid plate
2–axis
Motor
Camera
Lens
YAG
Laser
한 칸에 5mm
중심점(원점) 기준으로 20mm 지점까지 사용 가능
Wavelength: 532 nm
Power: 500 mW
Diameter: 6.0 mm
* 슬릿 구멍으로 빔 크기 줄이기
Ce:YAG single crystals
Size: 10x10x0.1mm
Thermal resistance: 790 W/m
Melting point: 2243 K
Polished surface with marking grid
Type: CMOS
Resolution: 1.6 Megapixels
Sensor Size (FxV): 4.97 mm × 3.73 mm
Mono (Colorless)
Fixed focal length: 25 mm (Wide Angle)
Working distance: 100mm - ∞
Maximum distortion: 0.22 %
Ethernet control
Resolution: 10000 ppr
BK Brake (Axis-mounted)
Holding torque: 1.0 Nm

## Slide 6: Order Laser Optics Equipment

## Slide 7: BPRM Stage Alignment
Active area in which two glass grids are linearly parallel.
The grid arrangement becomes more skewed towards the edge.

## Slide 8: 2-Axis Motor Repeatability
Command Position : -25000
Actual Position : -25000
Position Error : 0
Actual Velocity : 0
Command Position : 25000
Actual Position : 25000
Position Error : 0
Actual Velocity : 0
Command Position : 25000
Actual Position : 25000
Position Error : 0
Actual Velocity : 0
Command Position : -25000
Actual Position : -25000
Position Error : 0
Actual Velocity : 0
Command Position : 0
Actual Position : 0
Position Error : 0
Actual Velocity : 0
x 50 for each axis

## Slide 9: Raw Data Acquisition
. . .
N = 10
Collect motley samples of YAG screen images.
Each screen has different arrangement.

## Slide 10: Beam Profile Monitoring Method
. . .

## Slide 11: Beam Profile Monitoring Method
Real Space Image
Restored to original screen size
Projection showing transverse beam space
Pixel Space Image
Indicate the beam intensity
Can be used to plot 1D graph

## Slide 12: BPRM Measurement & Analysis
Read the raw image file
List up all pixel values of image
Sum pixel values along the axis
Plot them onto Gaussian graph
Adjust the graph fitting
Fitting Error
Offset (image noise)
Blank area (Outside of the screen)

## Slide 13: Summary & Future Plan
BPRM Method
Perspective calibration
2D motorized BPRM stage
Beam profile graph fitting
Data Acquisition & Analysis
Utilize motorized axis when collecting 4 pairs of boundary condition coordinates
Establish the method of analyzing a set of data
Fill out and submit the paper

## Slide 14: THANK YOU