## Slide 1: Theories derived from Haissinski equation and their applications to electron storage rings
Young Min Park
Division of Advanced Nuclear Engineering (DANE), POSTECH
2025-04-03, Pohang, South Korea

## Slide 2: Wake field & Impedance
2
Leading particle
Trailing particle
Structure
Wake
Electro magnetic fields induced by the beam are refereed to as wake fields due to the fact that they are left mainly behind the traveling charge. – L.Palumbo, CERN. LNF-94/041
In reality, (not a point charge)

## Slide 3: Potential well distortion
3
W/O wake
Equation of motion
Wake field term
Hamiltonian
With wake
Due to wake filed term
Centroid shift
Bunch lengthening (Or shortening)
Peak position change

## Slide 4: Vlasov-Fokker Plank equation
4
VFP
Quantum excitation
Radiation damping
In equilibrium(s-independent)
Haissinski equation
phase-space distribution
Conservative term

## Slide 5: Introduction
5
Previous theory
[1] B.W.Zotter, Potential-well bunch lengthening
Zotter’s cubic equation is not self-consistent and is valid only when a pure inductance can approximate the longitudinal total impedance of the ring.
In real machine, discrepancy between simulations and experiments was conducted.
[2] V. Smaluk, Impedance computations and beam-based measurements: A problem of discrepancy
Derive equations for center of mass, peak position, longitudinal profile, bunch length.
Show Zotter’s cubic equation is a special case of our theory.
Theory test with real machines.

## Slide 6: Theories derived from Haissinski equation
called longitudinal loss factor
Changed , and slope of change of can be measured experimentally ​
When the bunch distribution retains its original Gaussian shape with ​, and the loss factor can be calculated as:
6
Centroid shift
Difference between and gap between real part of theoretical and actual impedance

## Slide 7: Theories derived from Haissinski equation
7
Centroid shift measurement
[1] R.H.A. Farias, Oscilloscope measurement of the synchronous phase shift in an electron storage ring, PRAB01
Beam pick-up signal vs RF cavity signal
[2] T. Ieiri, Beam dynamics measurements using a gated beam-position monitor at KEKB, NIM-A (2009)

## Slide 8: Theories derived from Haissinski equation
Changed , and slope of peak position can be measured experimentally
When the bunch distribution retains its original Gaussian shape with ​, and can be calculated as:
8
Peak position
Difference between and gap between real part of theoretical and actual impedance

## Slide 9: Theories derived from Haissinski equation
9
Peak position measurement/ Bunch length measurement
Streak camera (~ps resolution)
BPM zero-crossing signal
BPM Measured Position of

## Slide 10: Theories derived from Haissinski equation
10
Bunch lengthening
Appendix
Changed , and slope of can be measured experimentally
When the bunch distribution retains its original Gaussian shape with ​, and can be calculated as:
Difference between and gap between imaginary part of theoretical and actual impedance

## Slide 11: Theories derived from Haissinski equation
11
Inverse problem
If the bunch distribution is accurately measured, the impedance can be extracted from it.
  The inverse problem(deconvolution) is ill-posed, meaning it is highly sensitive to measurement errors.
  High-frequency impedance components are difficult to obtain reliably.

## Slide 12: Explicit expressions for specific impedance
12
Equivalent impedance and Centroid shifts for specific impedance

## Slide 13: Explicit expressions for specific impedance
13
Compare with Zotter’s equation
Assume
If we assume purely inductive impedance
We can get Zotter’s cubic equation, but is is not appropriate for comparison with experimental data.

## Slide 14: Applications to real machines
14
SLC damping ring
KEKB low energy ring
Super-KEKB LER
~1998
~2010
2018~

## Slide 15: Applications to real machines
15
SLC damping ring
Original chamber
Improved chamber
[1] R. Warnock, Numerical solution of the Haissinski equation for the equilibrium state of a stored electron beam, PRAB 21.

## Slide 16: Applications to real machines
16
SLC damping ring
Suggested equation
Zotter’s equation

## Slide 17: Applications to real machines
17
KEKB low energy ring
[1] D. Zhou, Simulation of microwave instability in LER of KEKB and Super KEKB

## Slide 18: Applications to real machines
18
Suggested equation
Zotter’s equation
KEKB low energy ring

## Slide 19: Applications to real machines
19
KEKB low energy ring
Measured effective inductance =
Why those discrepancy occur?
Systematic errors in streak camera
Supplementary bunch lengthening induced by resistive impedance

## Slide 20: Applications to real machines
20
Super-KEKB
[1] D. Zhou, Simulation of microwave instability in LER of KEKB and Super KEKB

## Slide 21: Applications to real machines
21
Suggested equation
Zotter’s equation
SuperKEKB
Inductive impedance dominates bunch lengthening
Calculated by Hassinski equation

## Slide 22: Applications to real machines
22
Super-KEKB (Inverse problem of Haissinski equation)

## Slide 23: Applications to real machines
23
SuperKEKB discrepancy
[1] T. Ishibashi, Impedance modelling and single-bunch collective instability simulations for the SuperKEKB main rings
matched well with simulation and measurement( is good.)
Streak camera error?
Missing inductive impedance?
Find alternative methods to measure bunch length

## Slide 24: Conclusion
24
Using the Haïssinski equation a self-consistent stationary solution of the Vlasov–Fokker–Planck equation, we can derive analytical expressions for intensity-dependent beam observables such as centroid shift, bunch lengthening, and equivalent impedance.
The study emphasizes the importance of matching beam-based measurements with impedance calculations, highlighting the practical use of the derived formulas for interpreting experimental data.In particular, streak camera and BPM measurements can provide useful information for evaluating loss factors and extracting equivalent or frequency-dependent impedances.
This approach enables more reliable comparisons between simulations and measurements and may help identify missing impedance sources in storage ring models.

## Slide 25: Thank you for your attention!
25

## Slide 26: Appendix Bunch lengthening
26
Bunch lengthening