## Slide 1: 20250516 Group Meeting
Minseo Jeong

## Slide 2: Index
Current process of multi-objective Bayesian optimization(MOBO)
UED experiment plan(with IBS)

## Slide 3
Input parameter: Strength of solenoids, bunch charge, RF gun phase, source beam size
Objective parameter: Beam size, bunch length, normalized emittance, energy spread, q-resolution, (+energy)
Parameter | Range
Charge | [50fC, 100fC]
Source beam size | [20μm, 100μm]
RF gun phase | [-80°, -30°]
Solenoid 1 strength | [0.144T, 0.18T]
Solenoid 2 strength | [0.07664T, 0.0958T]

## Slide 4
Surrogate model: Gaussian process
Kernel: Matern function with v=5/2
Initial sample point: 16
Acquisition function: Upper confidence bound hypervolume improvement(UCB-HVI)
Number of iteration: 100~400

## Slide 5
Acquisition function: expected hypervolume improvement(EHVI)
Objective: beam size, bunch length
Mean and standard derivation of beam size and bunch length:
[48.2μm, 18.6μm], [178fs, 45.8fs]

## Slide 6: Future Plan
Comparison with other optimization method
(e.g. random process, NSGA-II)
Application to eLabs-Gun I facility
- Objective variables can be changed
R. Roussel et al. Phys. Rev. Accel. Beams 27. (2024).

## Slide 7: Future Plan(Optional)
Trust region Bayesian optimization(TuRBO): An algorithm that restricts optimization of the acquisition function to within a so-called trust region
Trust region is centered at the best previously observed measurement so far during optimization
As optimization progresses, the location and size of the trust region are continuously updated
R. Roussel et al. Phys. Rev. Accel. Beams 27. (2024).

## Slide 8: UED Experiment
Gas UED experiment(static)
Solid UED experiment(time-resolved)

## Slide 9: UED Experiment

## Slide 10
Layout
Side view
Top view
Beam

## Slide 11
XY-Stage
(Capillary)
XYZ-Stage
(Sample)
XY-Stage
(Laser mask)
320mm
400mm
Drain port
650mm
TMP
CRYO
Side view

## Slide 12: Gas UED Experiment
To maintain different vacuum condition between gun and vacuum chamber, capillary and turbo chamber is installed

## Slide 13: Gas UED Experiment
Sample delivery protocol
 | Flow cell | Slit jet
Appearance | Gas | Powder/crystalline
Temperature | Ambient | 50~300°C
Pressure | 0.5~5Torr | ~1Torr
Consumption | <100mL | <150g
Rep. rate | CW | 

## Slide 14: Gas UED Experiment
Intensity of diffraction pattern
(s is momentum transfer )
is used for analysis of data
Pair distribution function:
X.Shen et al., Struct. Dyn. 6, 054305 (2019)

## Slide 15: Appendix-MOBO Code

## Slide 16: Appendix-MOBO Code

## Slide 17: Appendix-MOBO Code

## Slide 18: Appendix-MOBO Code

## Slide 19: Appendix-MOBO Code