## Slide 1: Studies of Longitudinal feedback system (LFS)
25. 05. 16
Geunwoo Kim

## Slide 2: Introduction
2
Wakefield
Wakefield is generated when the beam passes through an arbitrary structure.
It affects the beam's movement, causing it to transition into coupled motion via higher-order mode.
 Causing Coupled Bunch Mode Instability (CMBI).
Long-range wakefield

## Slide 3: Introduction
3
Higher-Order Mode (HOM)
Higher-order mode

## Slide 4: Introduction
Coupled Bunch Mode Instability (CBMI)
where μ is mode number
4
From Y. Park
Bunch index
Longitudinal phase space
Mode 1 coupled bunch instability
Stable beam
From Y. Park

## Slide 5: Introduction
Growth rate depends on mode number μ.  Beam loss occurs
Max(Ibeam) is limited.
frev ~ 375 kHz ↔ detuning Δf ~ 300 kHz
5
From beam
From cavity
(Korea-4GSR) 24ID, 7HHC, 400 mA
Mode 1
τg-1 = 6282.331 1/s
Mode 2
τg-1 = 3946.8 1/s
Optimal detuning (~300 kHz, 24 ID, 400 mA)

## Slide 6: Longitudinal feedback system (LFS)
Overview of LFS
Bunch by Bunch feedback system
Suppression wakefield effects for each bunch
Broadband amplifier should be used.
6
Transverse feedback loop

## Slide 7: Longitudinal feedback system (LFS)
Main parameters
Central freq.
  ; corresponding freq. for μ=1.
Wider bandwidth (BW: fRF/2 = 250 MHz)
  i.e., Low Q-factor (~5)
7
From beam
μ=1 freq.

## Slide 8: Longitudinal feedback system (LFS)
Main parameters
Filling time 1.27 ns < 2 ns (less than bunch spacing)
Shunt impedance: related to costs
  Making more input/output ports
  Adding nose cone structure
8
Only 2 ports are used among 8 ports.
The others are terminated 50 Ω.
TM010
Nose cone
Korea-4GSR LFS (TDR)
Unwanted !
Notes: 기본적으로 Pillbox cavity

## Slide 9: Longitudinal feedback system (LFS)
9
Nose cone
TM010
HOM
HOM
Three types of LFS
ALS (Coaxial electrodes)
DAΦNE (Waveguide-overloaded)
Bessy II (Combined with the others)
Notes: 기본적으로 Pillbox cavity

## Slide 10: Longitudinal feedback system (LFS)
Main parameters
Filling time 1.27 ns < 2 ns (less than bunch spacing)
Shunt impedance: related to costs
  Making more input/output ports
  Adding nose cone structure
10
Only 2 ports are used among 8 ports.
The others are terminated 50 Ω.
TM010
Nose cone
Korea-4GSR LFS (TDR)
Unwanted !
Notes: 기본적으로 Pillbox cavity

## Slide 11: Longitudinal feedback system (LFS)
11
Damping rate (BESSY-II)
where .
Damping rate:
Operation verified @ w/ LFS (w/o LFS)

## Slide 12: Application to Korea-4GSR lattice
12
7 HHC and 5HHC operation
Both cases operate in brightness mode
For the 5 HHC case, It can be used w/ single LFS. (9 ID)
However, for 7 HHC case, cannot be damp far enough.
  Insert more LSF ? (X, not recommened…)
  Inject uneven filling pattern beam…

## Slide 13: Summary
13
Introduce how CMBI effect to beam motion
Understand basic knowledge of LFS.
Apply BESSY II’s LFS case to Korea-4GSR status.