## Slide 1
16th International Particle Accelerator Conference, Taipei
Comprehensive Study of Robinson Instability in Active and Passive Higher Harmonic Cavities for Bunch Lengthening
Youngmin Park, Moses Chung
POSTECH
Jimin Seok, Jaeyu Lee, Jaehyun Kim, Gyeong Su Jang
Pohang Accelerator Laboratory(PAL), POSTECH
June.2.2025

## Slide 2
Outline
Higher harmonic cavities(HHCs) in storage ring
Robinson instability derived by NC active HHCs in Korea-4GSR
Robinson instability derived by SC passive HHCs in PLS-II
Conclusion
16th International Particle Accelerator Conference, Taipei
Notes: In this talk, I will first explain the reason why we use higher harmonic cavities (HHCs) in storage rings. Then, I will briefly introduce the basic theory of Robinson instabilities.
After that, I will present a comparative analysis of Robinson instabilities that occur when using:
a normal-conducting active harmonic cavity in Korea-4GSR, and
a superconducting passive harmonic cavity in PLS-II.

## Slide 3
Touscheck lifetime in storage rings is determined by transverse beam size and bunch length.
Bunch lengthening offers:
Increase Touschek lifetime.
Lower frequent injection for Top-up operation.
Mitigate collective instability effects.
4th Generation Storage Ring:
Transverse emittance is reduced by over a factor of 100 times.
Short bunch length due to small momentum compaction factor. Higher Harmonic Cavities (HHCs) installation is necessary.
Why higher harmonic cavity?
Lifetime
Lifetime
16th International Particle Accelerator Conference, Taipei
Notes: Let me begin by explaining why higher harmonic cavities are essential.
In storage rings, maintaining a stable beam requires a sufficiently long Touschek lifetime, which is determined by the transverse beam size and the bunch length. Higher harmonic cavities are used to increase the bunch length, which in turn extends the Touschek lifetime, allowing for less frequent top-up injections. They also help mitigate several types of collective instabilities.
Especially in 4GSR, the beam emittance is reduced by more than two orders of magnitude. Combined with a smaller momentum compaction factor, this results in much shorter bunches, making the installation of HHCs indispensable.

## Slide 4
Conditions for flat potential:
Energy balance term :
Flat potential term :
Adjustable variable :
Equilibrium bunch length:
Lower Higher effectiveness of bunch lengthening.
HHC system:
Flat potential:
Decrease voltage gradient. Reduce restoring force and achieve bunch lengthening.
Bunch lengthening for HHC
16th International Particle Accelerator Conference, Taipei
Notes: Now, I’ll explain how HHCs are used to achieve bunch lengthening.
Before installing an HHC, the bunch experiences a restoring force due to the voltage gradient at the bunch center (around τ=0\tau = 0τ=0). The goal of a flat potential is to reduce this gradient, thereby weakening the restoring force and allowing the bunch to lengthen.
This condition is achieved by adjusting the relative phase and voltage ratio between the main cavity and the harmonic cavity. The equilibrium bunch length can be derived from the Hamiltonian or by solving the Vlasov equation. In general, a lower harmonic order leads to a longer bunch.

## Slide 5
NC-Active
Pros:
Freely adjust and for any currents.
LLRF feedback suppress transient effects.
No cryogenic system.
Cons:
External RF source(Generator) is required.
Generator
  DC Robinson instability
Types of higher harmonic cavity
Korea-4GSR
SC-Passive
Pros:
Simple design
No DC Robinson instability.
High Low AC Robinson instability. Low CBI.
High Can operate at low current.
Cons:
Cryogenic system
High
  Cavity mode instability (D-mode)
NC-Passive
Pros:
Simple design
No DC Robinson instability.
No cryogenic system.
Cons:
Low Can’t operate at low current. Need many cavity.
PLS-II
AC/CBI
Low
  AC Robinson instability
  Coupled Bunch Instability(CBI)
AC/CBI
can’t adjustable.
Transient effects
16th International Particle Accelerator Conference, Taipei
Notes: HHCs can be categorized into:
NC-active (Normal Conducting, powered),
NC-passive (Normal Conducting, beam-driven), and
SC-passive (Superconducting, beam-driven).
While each type has its own pros and cons, I will focus specifically on the instabilities that can arise with each configuration.
In active cavities, due to the presence of an RF generator, DC Robinson instability may occur. For normal conducting cavities, the low quality factor can also lead to AC Robinson instability and coupled-bunch instabilities (CBIs), which I will discuss next.
On the other hand, superconducting passive cavities have much higher Q values, so AC Robinson and CBI are generally suppressed. However, a different instability called the cavity mode instability, or D-mode instability, can appear. I’ll return to this later.
In this study, we analyzed two cases:
NC-active HHCs used in Korea-4GSR, and
SC-passive HHCs implemented at PLS-II.

## Slide 6
Robinson instability derived by NC active HHCs in Korea-4GSR

## Slide 7
Korea-4GSR
Korea-4GSR is a 4th generation electron storage ring currently under construction.
Phase 1: 200 mA with 9 Insertion Devices (IDs)
Final operation : 400 mA with 24 IDs
Parameter | w/o HHC | w/HHC
Circumference (m) | 799.297 | 
Momentum compaction factor |  | 
Energy (GeV) | 4 | 
Energy spread (%) | 0.0886 | 
Main RF voltage (MV) | 4.2 | 
Radiation loss (MeV) | 2.035 | 
Current (mA) | 400 | 
Harmonic number | 1332 | 
Main cavity quality factor | 29900 (5360) | 
Main cavity | 113.68 | 
HHC quality factor | X | 16000
HHC | X | 86
Minimum required HHC | X | 7
Life time (h) | 5.82 | 29.4
Bunch length | 7.5 | 37.7
Radiation damping time x/y/z | 7.21/10.48/6.78 (24 IDs) | 
Parameter | w/o HHC | w/HHC
Circumference (m) | 799.297 | 
Momentum compaction factor |  | 
Energy (GeV) | 4 | 
Energy spread (%) | 0.0886 | 
Main RF voltage (MV) | 4.2 | 
Radiation loss (MeV) | 2.035 | 
Current (mA) | 400 | 
Harmonic number | 1332 | 
Main cavity quality factor | 29900 (5360) | 
 | 113.68 | 
HHC quality factor | X | 16000
 | X | 86
Minimum required HHC | X | 7
Life time (h) | 5.82 | 29.4
 | 7.5 | 37.7
 | 7.21/10.48/6.78 (24 IDs) | 
ALBA-type NC active HHC is under consideration
Located in Ochang
16th International Particle Accelerator Conference, Taipei
Notes: Next, I will explain the case of using a normal-conducting active cavity in Korea-4GSR.
Korea-4GSR is a fourth-generation electron storage ring currently under construction and located in Ochang. The Phase 1 goal is to operate at 200 mA with 9 insertion devices, while the final target is 400 mA with 24 IDs.
In this study, we focus on the final operating condition. Since Korea-4GSR will install normal-conducting main RF cavities, the plan is to also use normal-conducting harmonic cavities, rather than superconducting ones. Specifically, an ALBA-type NC-active cavity is being considered.
To achieve a flat potential, at least 7 HHCs are required, which allows us to reach a bunch length of 37.7 ps.

## Slide 8
Stable
Unstable
AC/CBI
AC/CBI
Instability in NC active cavity
DC Robinson instability
AC Robinson instability
Coupled Bunch Instability
Multi bunch oscillation interacts with .
Causes amplitude growth of th oscillation mode.
Beam interacts with .
Causes amplitude growth of synchrotron oscillation.
Restoring force of RF cavity Beam induced voltage Loss phase stability
Beam loading term
Restoring force term
Bunch index
16th International Particle Accelerator Conference, Taipei
cavity resonant frequency
synchrotron frequency
revolution frequency
Notes: Let’s first examine the instabilities that can arise in normal conducting active cavities.
DC Robinson instability occurs when the beam-induced voltage becomes stronger than the restoring force from the cavity, causing the centroid phase to drift in one direction, breaking phase stability.
AC Robinson instability arises when the bunch oscillates at the synchrotron frequency ωs\omega_sωs​, and the spectral component at ω=ωrf+lωs\omega = \omega_{rf} + l\omega_sω=ωrf​+lωs​ interacts with impedance, leading to amplitude growth of synchrotron oscillations.
When multiple bunches are present in the ring, bunches oscillate with phase differences. These modes may interact with the impedance at specific frequencies, leading to coupled-bunch instabilities.

## Slide 9
NC active HHC
Issues with NC Active HHC
Background
To minimized generator power, optimal detuning frequency must be satisfied.
Main problem
Low revolution frequency (375 kHz) is close to optimal detuning frequency (270 kHz). This cause strong coupled-bunch Instability.
Mitigation method
Change the detuning frequency .
  Shifts the impedance peak away from .
Adjust the coupling factor .
  Reduce the impedance at the intersection with the line.
Both cases must consider feasible generator power.
16th International Particle Accelerator Conference, Taipei
Notes: As mentioned earlier, several instabilities can occur in NC-active cavities, but the most critical issue is the μ = 1 coupled-bunch instability (CBI).
In active cavities, there exists an optimal detuning frequency that minimizes generator power. Unfortunately, this optimal detuning turns out to be very close to the revolution frequency of Korea-4GSR, which is 375 kHz. This leads to severe CBI.
There are two main ways to mitigate this:
Shift the detuning frequency to move the impedance peak,
Increase the coupling factor β to broaden and suppress the impedance peak.
However, both strategies must be balanced with available generator power.

## Slide 10
4GSR Active Cavity
7 HHC, 400 mA operation, Flat Potential
DC Robinson occurs!!
CBI growth rate > LFS damping rate ()
Increasing helps to suppress CBI.
Reduce HHC beam loading DC Robinson instability
Broadened impedance CBI can occur
16th International Particle Accelerator Conference, Taipei
Notes: We performed a 2D scan of main cavity and HHC detuning frequencies with 7 HHCs installed. The color codes in the plot are:
Blue: AC Robinson instability,
Red: DC Robinson instability,
Hatched region: Coupled-bunch instability (CBI).
With β = 1, we observe both AC Robinson and strong μ = 1 CBI, with a growth rate over 5000 s⁻¹, far beyond what can be damped by LFS.
When we increase β to 3, the CBI growth rate drops to around 3000 s⁻¹, but this is still too high. Moreover, increasing β reduces beam loading effects, making DC Robinson instability appear. A broader impedance also raises the risk of higher-order CBIs, such as μ = 3 or 4.

## Slide 11
4GSR Active Cavity
7 HHC, 400 mA operation,
DC&AC Robinson Instability can be mitigated by NFP
Near Flat Potential(NFP) Leaves voltage gradient to retain restoring force.
NFP condition
16th International Particle Accelerator Conference, Taipei
CBI growth rate is still too large to be suppressed by LFS.
 Mitigation studies using bunch filling pattern are in progress.
Notes: One effective way to suppress AC and DC Robinson instabilities is to avoid making the potential completely flat. Instead, we allow a small restoring force—this is called the near-flat potential condition.
We define \xi as the ratio of harmonic to main cavity force. When ξ = 1, the potential is completely flat. Setting ξ ≈ 0.9 still gives us a 3× longer bunch, while suppressing AC and DC instabilities.
In this configuration, we indeed observe a stable region with no AC or DC Robinson instability. However, μ = 1 CBI remains strong, and further study, such as optimizing the fill pattern, is currently in progress.

## Slide 12
Robinson instability derived by SC passive HHCs in PLS-II

## Slide 13
PLS-II
Although a harmonic cavity is not currently planned, this lattice was used for comprehensive studies.
A SC passive HHC was assumed, as the cryogenic system is already in place.
SC passive niobium HHC [1]
Located in Pohang
PLS-II is a 3rd generation electron storage ring currently in operation.
[1] Hee-su Park et al., INVESTIGATION OF THE FABRICATION METHOD FOR THE 3RD HARMONIC SUPERCONDUCTING DOUBLE-CELL CAVITY, IPAC23, (2023)
Parameter | w/o HHC | w/HHC
Circumference (m) | 281.82 | 
Momentum compaction factor |  | 
Energy (GeV) | 3 | 
Energy spread (%) | 0.1 | 
Main RF voltage (MV) | 4.5 | 
Radiation loss (MeV) | 1.242 | 
Current (mA) | 400 | 
Harmonic number | 470 | 
Main cavity quality factor | ~ | 
Main cavity | 89 | 
HHC quality factor |  | 
HHC |  | 95
Minimum required HHC |  | 1
Life time (h) | ~20 | ~67
Bunch length | 16.8 | 56.1
Radiation damping time x/y/z | 2.06/2.71/1.60 | 
Parameter | w/o HHC | w/HHC
Circumference (m) | 281.82 | 
Momentum compaction factor |  | 
Energy (GeV) | 3 | 
Energy spread (%) | 0.1 | 
Main RF voltage (MV) | 4.5 | 
Radiation loss (MeV) | 1.242 | 
Current (mA) | 400 | 
Harmonic number | 470 | 
Main cavity quality factor |  | 
 | 89 | 
HHC quality factor |  | 
 |  | 95
Minimum required HHC |  | 1
Life time (h) | ~20 | ~67
 | 16.8 | 56.1
 | 2.06/2.71/1.60 | 
16th International Particle Accelerator Conference, Taipei
Notes: Now, let’s move on to the case of a superconducting passive cavity in PLS-II.
PLS-II is a third-generation storage ring, currently operational in Pohang. While no harmonic cavity is installed yet, we use this lattice for comparison.
The main cavity is already superconducting and active, so adding an SC-passive cavity is a practical assumption. We use past SC passive cavity designs as the basis for parameters in this study.

## Slide 14
Instability in SC passive cavity
Cavity mode
AC Robinson instability Weak due to
CBI Weak due to small and high
Extremely large impedance at the detuning frequency . Excites oscillation modes near . Cavity mode or D-mode instability [1]
[1] T. He et al., Mode-zero Robinson instability in the presence of passive superconducting harmonic cavities, PARB 26, (2023)
[2] A. Gamelin, Harmonic cavity studies for the SOLEIL Upgrade, IPAST Workshop, (2022)
Typically, growth rate of D-mode instability is low
When Coupling occurs between AC Robinson & D-mode. Strong instability
AC Robinson instability is negligible before coupling. Only consider D-mode instability.
[2]
16th International Particle Accelerator Conference, Taipei
Notes: Instabilities in SC cavities differ significantly from NC cavities.
Due to the high Q (~10⁶), the impedance is very low at ωRF+ωs\omega_{\text{RF}} + \omega_sωRF​+ωs​, so AC Robinson instability is weak. Also, CBI is minimal due to the narrow impedance spectrum.
However, at the detuning frequency, the impedance can reach GΩ levels, leading to a resonant interaction between the beam and cavity field. This causes a cavity mode instability, or D-mode.
This was discussed in a 2023 PRAB paper, and our simulations confirm the presence of D-mode near the detuning frequency. D-mode usually shows moderate growth rates (~10–100 s⁻¹), but if Δω\Delta\omegaΔω approaches ωs\omega_sωs​, mode coupling can lead to strong instability.

## Slide 15
PLS-II Passive Cavity
1-3 HHC, 400 mA operation,
The line defines the condition for optimal bunch lengthening as a function of .
Possible mitigation methods
Increase detuning frequency Lower bunch lengthening efficiency.
Increase number of cavity Enhance transient beam loading in the presence of gaps.
1 Cav
Fit:
Analytic:
Fit:
Analytic:
Fit:
Analytic:
3 Cav
D-mode
D-mode
D-mode
AC
AC
AC
Macroparticle simulation conduced with uniform filling & 10000 particle.
Simulation result match well with analytic prediction.
Stable
Unstable
2 Cav
16th International Particle Accelerator Conference, Taipei
Notes: This plot shows the D-mode instability regions and bunch lengthening conditions for various total shunt impedances.
With 1 or 2 HHCs, D-mode instability appears. Simulations (shown on the right) match well with the analytical predictions.
There are two main ways to suppress D-mode:
Increase detuning frequency, but this worsens bunch lengthening efficiency.
Add more cavities, increasing shunt impedance, but this enhances transient beam loading, especially in gapped fill patterns.

## Slide 16
Conclusions
This study focused on Robinson instability in both NC-active and SC-passive harmonic cavities, from Korea-4GSR and PLS-II.
NC Active Harmonic Cavity (4GSR)
  Main issue: CBI → varying coupling and adjusting can be partially mitigate.
  Other instabilities (DC Robinson, AC Robinson) occur. → can be suppressed by NFP.
SC Passive Harmonic Cavity (PLS-II)
  Cavity mode (D-mode) instability is dominant.
  D-mode arises when: Can be avoided by increasing or
Future works
  Multi-particle multi-bunch tracking simulation is required for further validation.
  Optimizing the bunch filling pattern is necessary to suppress CBI.
16th International Particle Accelerator Conference, Taipei
Notes: To summarize, this study investigated Robinson instability in both NC-active and SC-passive harmonic cavities using Korea-4GSR and PLS-II cases.
In NC-active cavities, μ = 1 CBI is the main issue, which can be partly mitigated by adjusting coupling β and detuning. DC and AC instabilities can be suppressed by applying a near-flat potential.
In SC-passive cavities, D-mode instability is dominant when Δω ≈ ωₛ, but can be avoided by increasing Δω or R/Q.
Future work includes tracking simulations and bunch fill pattern optimization for better stability.

## Slide 17
Thank you for your attention!
16th International Particle Accelerator Conference, Taipei

## Slide 18
Appendix. Generator power
In an active harmonic cavity consider both generator voltage & beam induced voltage.
The required generator power varies with tuning angle
is determined by the detuning between the cavity resonant frequency () and rf frequency ()
Main cav , HHC cav
Optimum condition
16th International Particle Accelerator Conference, Taipei

## Slide 19
Appendix. Bosch’s model
Scan parameters
Active
Main and harmonic cavity tuning angle
Harmonic cavity coupling
Passive
Main and harmonic cavity tuning angle
[1]
[1] R. A. Bosch et al., “Robinson instabilities with a higher harmonic cavity”, PRAB, (2001)
Check AC Robinson instability and mode coupling
Check DC Robinson instability (Zero frequency instability)
Check CBI
Set scan parameters
Compute RF Potential
Solve longitudinal bunch distribution
Calculate beam properties
Visualize result
Instability onset condition
AC Robinson instability
CBI
Mode coupling
Instability verification
Find stationary solution
16th International Particle Accelerator Conference, Taipei
Notes: To evaluate whether such instabilities occur, we followed an algorithm based on a method proposed in a 2001 PRAB paper.
We first scan a set of cavity parameters. At each condition, we compute the stationary longitudinal distribution. Then, we check for the presence of:
DC Robinson instability,
AC Robinson instability, and
Coupled-bunch instability.
In active cavities, both the tuning angle and coupling factor β\betaβ can be adjusted. In contrast, passive cavities operate at fixed β=0\beta = 0β=0, so only the tuning angle is adjustable.
To determine if an instability occurs:
For DC and AC Robinson, we compare the growth rate with the radiation damping rate.
For mode coupling, we check if the dipole and quadrupole modes intersect.

## Slide 20
Appendix. NFP
In a double RF system using an HHC, the total voltage is given by:
HHC reduces the voltage gradient at , where the bunch is located, leading to bunch lengthening.
The degree of bunch lengthening can be quantified using a parameter , defined as the ratio of the voltage gradient at between the harmonic cavity and the main cavity.
  Flat potential condition
  , Similar to initial bunch
Smaller leads to less bunch lengthening and requires lower HHC voltage (less number of cavities).
16th International Particle Accelerator Conference, Taipei

## Slide 21
Appendix. NFP
The bunch length can be estimated semi-analytically using the Hamiltonian approach.
From the Vlasov equation, the stationary distribution must be a function of the Hamiltonian, and assuming a Gaussian distribution in energy deviation:
We compared the bunch length variation with respect to using both:
  Semi-analytical formula
  Particle tracking simulation with 10,000 macro-particles/50000 turns w/o wake field effects
The comparison shows good agreement in the absence of wakefield effects.
Significant bunch lengthening can be achieved when .
16th International Particle Accelerator Conference, Taipei

## Slide 22
Appendix. Passive HHC self-consistency
Passive harmonic cavity Equilibrium longitudinal distribution depends on .
Self-Consistent method
Set Initialize
Calculate
Compute using Vlasov equation
Update
PLS-II with
Repeat until converges
16th International Particle Accelerator Conference, Taipei
Notes: In passive cavities, the beam determines the voltage, so the equilibrium longitudinal distribution depends on the cavity tuning angle.
We apply a self-consistent algorithm:
Set the tuning angle, and initialize form factor as 1
Calculate the cavity voltage and potential,
Solve the Vlasov equation for the bunch distribution,
Update the form factor until convergence.
Using this approach, we obtain the bunch shape for various detuning frequencies, shown on the right.

## Slide 23
Appendix. Stable operation at low current
1-3 HHC, 400 mA operation,
At low beam current, achieving bunch lengthening requires low .
This condition can trigger strong D-mode instability or coupling between AC-Robinson and D-mode instability.
The 3D surface represents the required detuning frequency as a function of and .
To operate at low current (250 mA) with bunch lengthening is required.
Projection direction
line
Stable
Unstable
16th International Particle Accelerator Conference, Taipei
Notes: At low beam current, the detuning frequency needed for bunch lengthening approaches zero. This increases the risk of D-mode instability.
The 3D plot on the left shows the required conditions for bunch lengthening. The projected 2D view on the right indicates that, to achieve stable operation with bunch lengthening at 250 mA, the total shunt impedance must exceed 320 Ω.