## Slide 1
WBPM experiment results paper work plan
  Introduction
  Image analysis
  Beam size calculation
  Beam profile comparison
Ultra-short bunch length measurement using ChDR
  Experimental target
  Bunch length measurement
  Radiator design
  Experimental set-up
Python + EPICS based DAQ monitoring system implementation
  Introduction
  EPICS
  Configuration
  Manual
  HDF5
  Summary
Contents

## Slide 2: WBPM experiment results paper work plan
2025. 07. 18.
송우진

## Slide 3
Beam position monitor
PAL-XFEL SX beamline
Beam profile monitor
PLS-II BL6C
?
Introduction

## Slide 4: Image analysis
250611_WBPM_Xe_test (Background data X)
- Exposure time 0.3 ms, 250 accumulative (75 sec), ROI: 10-15 mm (Z)

## Slide 5: Beam size calculation
Screen monitor  FHWM
WBPM  Gaussian fit (FWHM = 1sigma * 2.355)

## Slide 6: Beam profile comparison

## Slide 8: Ultra-short bunch length measurement using ChDR
2025. 07. 18.
송우진

## Slide 9
Experimental target
Before installation
Radiator design and manufacture
Set-up
Data acquisition system
Alignment test
Future plan
Installation
Alignment at e-Labs
Experiment
Radiator fabrication
Securing test facilities
Calculation of the target range
Detector (Spectrometer or power meter)
Experiment (1st test at IBS, 23.08)
Future plan
Crystal radiator modification
Experiment (2nd test at IBS, 25.08)
Beam profile monitor
Linac (e-Labs)
Bunch length measurement
LWFA (IBS 150TW laser)

## Slide 10
Bunch length measurement
What we Measure
(Coherent ChDR)
What we already know
(Incoherent / Single particle ChDR)
What we want to know
(Bunch length)
IBS 150 TW Laser, LWFA experiment
Expected e-beam parameters: 500 MeV, 1~5 fs(0.3~1.5 um), 10 pc

## Slide 11
Radiator (with capillary) design
Spectrometer
ChDR
Beam

## Slide 12
Experimental set-up
Laser
Capillary
Au Mirror
Au Mirror
ChDR
ChDR
ChDR
ChDR
Window
LWFA Experiment with IBS 150 TW Laser
The goal was to measure the length of the electron beam. (500 MeV, a few fs, 10 pC)
Measuring ChDR coming off the edge of a capillary.
Beam transported using a 3’ Au mirror.
Outside the chamber, only passes through the filter and directly into the detector.
ChDR
Window
THz filter
Detector
Capillary
ChDR
Filtered signal

## Slide 13
Experimental set-up
THz filter
THz detector (power meter, 0.1~30 THz)
Measurement Target: Regions where the trends of Incoherent ChDR and Coherent ChDR differ.
  As the bunch length increases, differences appear at lower frequencies.(1 fs  ~80 THz, 5 fs  ~ 20 THz)
Measurement Plan: Use filters up to 20 THz and replace 5 filters sequentially from the highest frequency.
  Record beam energy and, if possible, beam size for each measurement.

## Slide 14: Python + EPICS based DAQ monitoring system implementation
2025. 07. 18.
송우진

## Slide 15
High-temperature superconducting (HTS) magnet wavelength shifter (WLS)
Introduction
  The world's first application using HTS
  Basic testing has been completed, and we plan to install it in the PLS-II storage ring tunnel for experimentation.
  Data such as magnet temperature, voltage, and current must be measured to ensure stable operation.

## Slide 16
The DAQ used in the HTS experiment was SCXI-1125  However, it has been discontinued.
A new DAQ that satisfies the required performance must be selected, tested, and built into the system.
SCXI-1125
DT9824
Introduction

## Slide 17
Previously, QuickDAQ or DESYLab was used when operating DAQ (DT9824).
  Difficulties in setup and automation each time, suitable for intermittent experiments.
Python + EPICS utilization
  Stable monitoring service, automation and continuous measurement, log data DB conversion, suitable for continuous experiments and services.
QuickDAQ
DESYLab
Introduction

## Slide 18
Experimental Physics and Industrial Control System (EPICS)
Open source software framework  Large facility control system, data acquisition.
Input/Output Controller (IOC): A control process that communicates directly with device hardware.
Process Variable (PV): The basic unit of data handled by EPICS.
  Each PV represents the status of equipment (e.g., temperature, current, vacuum, etc.).
  Clients can access PVs to read, write, and monitor them.
Channel Access (CA): EPICS communication protocol (TCP-based)
  Connects clients and IOCs using PV names.
CS-Studio (Control System Studio), Phoebus, caget / caput / camonitor (terminal-based utilities)
EPICS

## Slide 19
CA Client vs Server (From Ziga Oven, COSYLAB)
EPICS

## Slide 20
EPICS

## Slide 21
Python: DAQ data acquisition, storage, and PV updates
Configuration
CS-Studio: Visualization of updated measurements in Python (real-time updates)

## Slide 22
Configuration
PC
Save file (HDF5)
(Local PC)
Database (dt_data.db)
SoftIoc (dt_softioc.bat)
Epics (Server)
DT_monitor.opi
(Client)
CS-Studio
PV update
(TCP/IP, local host)
Visualization
Python (IOC)
SN23289013
SN42949672
SN31784952
H/W
…...
Thread1
Thread2
Thread3
Buffer
Buffer
Buffer
Flush
Multiprocessing
USB
TCP/IP

## Slide 23
Run dt_softioc.bat (epics)
Run dt_softioc.py - If DT9824 operates without problems, automatic measurement starts. - Data is automatically saved in the Data folder in HDF5 format.
Run CS-Studio
DT_monitor.opi  Monitoring
Manual

## Slide 24
The measured results are always saved in HDF5 format.
계층적 데이터 형식 (Hierarchical Data Format) - A file format for storing large amounts of data. - Small file size, indexing, and fast access speed. - Can be easily used by installing HDF viewer.
HDF5 Data Access

## Slide 25
  HDF5 to CSV/Excel Convert
HDF5 Data Access
import h5py import pandas as pd h5_file = 'DT9824(00)_250708130833347981.h5' # 변환하고자 하는 HDF5 파일 with h5py.File(h5_file, 'r') as f: data = {'Time': f['Time'][:], 'CH1': f['CH1'][:], 'CH2': f['CH2'][:], 'CH3': f['CH3'][:], 'CH4': f['CH4'][:]} df = pd.DataFrame(data) # Pandas DataFrame 생성 df.to_csv(f'{h5_file}.csv', index=False) # CSV 저장 df.to_excel(f'{h5_file}.xlsx', index=False, engine='openpyxl’) # Excel 저장
  HDF5 to ASCII Convert
import h5py import numpy as np h5_file = 'DT9824(00)_250708130833347981.h5' with h5py.File(h5_file, 'r') as f: time = f['Time'][:] ch1 = f['CH1'][:] ch2 = f['CH2'][:] ch3 = f['CH3'][:] ch4 = f['CH4'][:] combined = np.column_stack((time, ch1, ch2, ch3, ch4)).astype(np.float64) np.savetxt(f'{h5_file}.txt', combined, fmt='%s', delimiter='\t', header='Time\tCH1\tCH2\tCH3\tCH4', comments='')

## Slide 26
Build an automation and monitoring system for multiple DT9824s using Python + epics.
Enable continuous measurement and logging of data to a database, as well as internal/external triggers, and utilize the maximum sampling rate.
Long-term stability testing required.
Summary

## Slide 27: Measurement of frequency response of DAQ

## Slide 28
Signal distortion due to attenuation in frequency domain. (example)
- Changes in voltage signal waveform with 4 Hz filter applied.
Signal distortion
Removal of high-frequency components with a 4 Hz LPF.
Signal distortion occurs in sections where the slope changes rapidly. - Attenuation due to the bandwidth of the equipment can cause measurement errors.
iFFT
FFT
Introduction

## Slide 29
Introduction
Bandwidth measurement experiment
  - Data : 2023.10.18-19 PAL
  - SCXI-1125, DT9824 bandwidth measurement
  - Results
Simulation of measurable signal length
- Signal distortion in special situations where short signals occur.
 | Sampling rate | Specification | Measurement
SCXI-1125 | 100 kSa/s | 10 kHz | 11.5 kHz
DT9824 | 4.8 kSa/s | 1.104 kHz | 1.105 kHz

## Slide 30
Set-up
Function generator
(Agilent 33220A)
1 uHz ~ 20 MHz
10 mV ~ 10 V (p-p)
SCXI-1125
(1ch)
Sine signal
1 Hz ~ 20 kHz (SCXI)
1 Hz ~ 10 kHz (DT)
1 V (p-p)
Control PC
(Labview)
Set frequency
measurement
Frequency response measurement results
 | Sampling rate | Specification | Measurement
SCXI-1125 | 100 kSa/s | 10 kHz | 11.5 kHz
DT9824 | 4.8 kSa/s | 1.104 kHz | 1.105 kHz
DT9824

## Slide 31
원본 신호 Rise time =
Amplitude,
……
Generate a virtual signal with a rise time of 0.1 ms to 10 ms (original signal).  Signal distortion occurs due to the frequency response characteristics of DT9824 (measured signal).  Calculate how much the amplitude and length of the measured signal have changed compared to the original input signal.
10%
90%
Time domain signal
Frequency response and signal spectrum
= 0.1~10 ms (0.1 ms step)
Δt = 5 μs
Simulation: Short rise time signal measurement

## Slide 32
Signal with Freq. Resp.
(DT9824 - 1.1 kHz BW)
Intensity and length changes depending on signal length
Intensity variation=
Length variation=
SCXI-1125 | 0.99 | 1.01
DT9824 | 0.92 | 1.08
SCXI-1125 | 0.99 | 1.01
DT9824 | 0.92 | 1.08
Simulation: Short rise time signal measurement

## Slide 33
Bandwidth measurement experiment conducted with SCXI-1125 and DT9824
SCXI-1125  DT9824
  Has sufficient bandwidth for high-speed charge/discharge measurement experiments (~ tens of Hz).
  However, in situations where short pulses (~ 1 ms) occur, attenuation correction must be applied.
Measurable range  Additional research considering resolution is necessary (noise, bit depth, …).
Frequency response
Signal distortion caused by bandwidth
Summary