## Slide 1: Current progress of LPS reconstruction
25. 07. 25
POSTECH
PhD/MS combined student
Geunwoo Kim

## Slide 2: Overview of LPS
Key factors
1D intensity distribution
Evenly spaced rotation angles
[Original beam image]
What we want to know
[Reconstructed image]
Notes: https://watkins.cs.queensu.ca/~jstewart/457/notes/ct/06/06-fbp.html

## Slide 3: Overview of LPS
How can we rotate the beam in longitudinal direction (z, pz) ?
Varying the booster cavity phase can adjust both and .
Reconstruction point
Measurement point
Parameters | Specifications
Energy | 70 MeV
Charge | 200 pC
# of particles | 100,000
Space charge | OFF
Bunch length | 1.2739 ps
 | Phase range [deg] | Increment [deg] | # of data
Booster phase Φ | 225 - 241 | 0.1 | 161

## Slide 4: Model vs Simulation
Compare equation vs simulation (obtained < 1 % error)
Find the gun phase at the maximum point (MMMG phase).
We can know the slope S from

## Slide 5: Model vs Simulation
Investigation both slope S and bunch length.
Chart: Booster phase - MMMG phase (deg)
RMSE = 0.132 MeV/c/rad
MAPE = 2.94 %

## Slide 6: Model vs simulation
Now, we can analysis phase advance
Complete preparing phase space angle data w.r.t booster phase.

## Slide 7: Sinogram (angle data w.r.t momentum)
Only pz distribution can be measured from the beamline.
  X can be converted to pz using a dipole.
  pz distribution in (z,pz) = pz distribution in (pz,y)

## Slide 8: Sinogram (angle data w.r.t momentum)
Prepared center-shifted distribution for reconstruction (give same weight).

## Slide 9: Reconstruction results
Comparison original vs reconstruction
FBP
SART
Phase advance cut
±50 deg Φ
±30 deg Φ
±50 deg Φ
±30 deg Φ
No center shift case

## Slide 10: Image analysis
FBP
  MSE: 0.0055
  Similarity for whole region: 12.39 %
  Similarity for ROI: 75.10%
SART
  MSE: 0.0060
  Similarity for whole region: 25.72 %
  Similarity for ROI: 65.46%

## Slide 11: Issues
??

## Slide 12: Issues

## Slide 13: Completed Stages and Next Steps
Procedure of tomography
1. Preprocessing
2. Analytic modeling
3-2. Weight Matrix
4. Apply algorithm
5. Verification
Done
Ongoing
3-1. Using library
4. Verification
Next plans