## Slide 1: 0725 Passive Superconducting HHC
Young Min Park
Division of Advanced Nuclear Engineering (DANE), POSTECH
2025-07-25, Pohang, South Korea

## Slide 2: Storage ring with HHC
2
[1] Pedro F. Tavares et al., Equilibrium bunch density distribution with passive harmonic cavities in a storage ring, Phys. Rev. ST Accel. Beams 17, (2014).
HHC system:
Flat potential:
Decrease voltage gradient. Reduce restoring force and achieve bunch lengthening.
Touscheck lifetime in storage rings is determined by transverse beam size and bunch length.
Bunch lengthening offers:
Increase Touschek lifetime.
Lower frequent injection for Top-up operation.
Mitigate collective instability effects.

## Slide 3: Passive SC HHC
3
[1] Pedro F. Tavares et al., Equilibrium bunch density distribution with passive harmonic cavities in a storage ring, Phys. Rev. ST Accel. Beams 17, (2014).
SSRF
NSLS-II
APS-U
K-4GSR (design)
Previous method: (scalar self consistency)
Improved method: (full self consistency)
Self consistency?
[1]

## Slide 4: Passive cavity self consistency
4
My method Initialize grid : over the range and Reset the minimum and maximum values of and Iteration refinement toward self-consistency
Paper method Initialize grid : over the range and Initial value : grid point with minimum residual Iteration refinement toward self-consistency

## Slide 5: Passive cavity self consistency
5
Name | Value
Main cavity voltage | 4.24 MV
Energy loss per turn | 2.035 MeV
Number of main cavity | 12
Initial bunch length | 7.45 ps
Main value | 113.68
HHC Quality factor | 
HHC value | 89
Beam current | 400 mA
Name | Value
Main cavity voltage | 4.24 MV
Energy loss per turn | 2.035 MeV
Number of main cavity | 12
Initial bunch length | 7.45 ps
HHC Quality factor | 
Beam current | 400 mA
37.5 ps
: 89.993
: 151.32
400 mA
300 mA
200 mA
100 mA
37.2 ps
: 89.9948
41.3 kHz
: 151.33
37.2 ps
: 89.9896
: 151.32
37.13 ps
: 89.9792
: 151.32

## Slide 6: Simulation convergence test
6
Number of macroparticles
Nturns
Nslice
The convergence test is in progress.
Macroparticle: 500
BL: 7.76 ps
Macroparticle: 5000
BL: 19.09 ps
Macroparticle: 10000
BL: 24.25 ps
Macroparticle: 30000
BL: 24.13 ps
Nslice : 20
BL: 36.2 ps
Nslice : 30
BL: 35.9 ps
Nslice : 10
BL: 35.8 ps
Cavity filling time
Revolution time
Decay turn 15900 turns Wake turn & Number of turns > 30000~50000

## Slide 7: Transient effects
7
Transient effects
Ion instability Include ion clearing gap between bunch trains Uneven filling pattern Beam loading voltage varies bunch-by-bunch Bunch length and centroid change
Semi analytic method
[1] T. Olsson, Self-consistent calculation of transient beam loading in electron storage rings with passive harmonic cavities, Phys. Rev. Accel. Beams 21, (2018).
Gap: 300
[1]

## Slide 8: Transient effects
8
Analytic result
[1] T. Olsson, Self-consistent calculation of transient beam loading in electron storage rings with passive harmonic cavities, Phys. Rev. Accel. Beams 21, (2018).
Gap: 300
Gap: 300
400 mA,
200 mA,
Long, asymmetric train stronger transient effects
Optimize filling pattern is needed
Number of Gap(determined by ion-clearing & hardware limits) > 25
Number of continuous bunch (determined by hardware) > 64
Number of bunch (Single bunch instability) ~ 1000

## Slide 9: Transient effects
9
[1] T. Olsson, Self-consistent calculation of transient beam loading in electron storage rings with passive harmonic cavities, Phys. Rev. Accel. Beams 21, (2018).
Gap: 300
400 mA,
Simulation result
Simulation vs analytic mismatch (Further studies need)

## Slide 10: Summary & Future plan
10
[1] T. Olsson, Self-consistent calculation of transient beam loading in electron storage rings with passive harmonic cavities, Phys. Rev. Accel. Beams 21, (2018).
No instability observed when applying SC passive cavities for bunch lengthening
Conducted semi-analytic, self-consistent methods to compute bunch distributions under both uniform and uneven filling patterns
Convergence tests (especially with respect to turn count and transient effects) remain to be completed due to long runtimes
Plan:
  Incorporate transient-effect analysis and begin drafting manuscript on 4GSR bunch-lengthening studies
  Arrival of new server will significantly improve simulation throughput and enable accelerated convergence testing

## Slide 11: Thank you for your attention!
11