## Slide 1: Ultrafast Electron Diffraction Facility in PAL-eLabs
Minseo Jeong

## Slide 2: Ultrafast Electron Diffraction
Pump-probe imaging technique based on optical pump-probe spectroscopy and electron diffraction caused by ultrafast electron
D. Filippetto et al. Rev. Mod. Phys. (2022).

## Slide 3: UED Facility in PAL-eLabs

## Slide 4: UED Facility in PAL-eLabs
Design of sample chamber for gas sample experiment
(with IBS)

## Slide 5: Optimization of UED parameters
Bayesian optimization: Model-based optimization algorithm using probability distribution model based on previous observations

## Slide 6: Optimization of UED parameters
Input parameter: Strength of solenoids, RF gun phase, source beam size
Objective parameter: Beam size, bunch length, q-resolution

## Slide 7: EPICS Simulator
Goal: Test of optimization algorithm of PAL UED facility by simulator
Running simulation(e.g. BMAD) by modifying process variables(PV) of PAL UED facility(e.g. solenoid current, RF phase)

## Slide 8: EPICS Simulator
Simulacrum(simulator of LCLS accelerator)

## Slide 9: Measurement of Thermal Emittance of Photogun
The normalized emittance at emission:
( electric field at the cathode)
The thermal emittance of photogun can be measured by solenoid scan
Y. WANG et al. PHYS. REV. ACCEL. BEAMS 23, 103401 (2020)

## Slide 10: Future Plan
Measurement of thermal emittance of photogun
Optimization of PAL-eLabs UED machine parameters
Participation of UED experiment (with IBS)
- static gas UED
- pump-probe experiment with solid sample