## Slide 1: Group meeting
2025/09/26
장원

## Slide 2
Content
Review - Issue for sapphire crystal
Choose material for target range
Experimental set up
Expected result

## Slide 3
Review-Transmission coefficient issue for Sapphire
  20 THz ~ 80 THz
  15um ~ 3.75um
  https://www.crystran.com/optical-materials/sapphire-al2o3
Radiation intensity can be affected by the crystal properties depending on the wavelength.(It may not be detected at all.)

## Slide 4
TPX (polymethylpentene)
High-resistivity float-zone Silicon (HRFZ-Si)
Polytetrafluoroethylene (PTFE)
THz detector
Target: 0.1 – 30 THz (=3000 – 10 um)
THz material option: – TPX (>30 THz), HRFZ-Si, ZnSe, PTFE (< 20 THz)
Gold mirror

## Slide 5
ZnSe Right-Angle Prism(600nm~16um)- Thorlabs

## Slide 7
20 THz  15 um
 ~ 3 mrad
Divergence
30 THz  10 um
 ~ 2 mrad
ZnSe기준, h=1 mm

## Slide 8
Bem path
stage
crystal
Radiation

## Slide 9
Detecting angle for Commercial product(ZnSe)
e beam
Prism
ChDR
Gold Mirror (4”)
Detector
5-axis stage
2~3 mrad
Light path < 1 m (2~3 mm spread)
By Snell’s law

## Slide 10
It's slightly off from the peak.
The peak position shifts to a lower frequency for shorter bunch lengths.

## Slide 11
Result
ZnSe exhibits a relatively constant transmission rate and refractive index over a region that significantly overlaps with the target range.
Choose material for target range
Modify the setup by moving the gold mirror instead of the radiator.
As the peak region lies slightly outside the detecting region, it remains uncertain whether the length can be reliably measured.
Because of it’s toxicity, it is advisable to obtain practical guidance from experienced users.