## Slide 1: Development of Zynq SoC-Based EPICS IOC for KOMAC remote control System
류연찬
2025/09/26

## Slide 2: 목차
The Reason of Choice
What is EPICS
  Meaning, Workflow, Example, Application
Development DAQ based on FPGA(Zynq)
  Motivation, Component, Sequence

## Slide 3: Reason of Choice
Introduce EPICS and Control
FPGA in accelerator
  Motivation of use FPGA
  Design requirement and Result

## Slide 4: What is EPICS
What is EPICS
Accelerators consist of many devices that must operate in coordination
Operator room is might be far from hardware device
EPICS is the framework that enables such coordinated operation across distributed devices
KOMAC 100 MeV Beam
KOMAC Operator Room
EPICS

## Slide 5: What is EPICS
EPICS
Client
Server
Channel Access
EPICS : Experimental Physics and Industrial Control System
  Toolkit for building distributed control system at large research facilities (such as accelerator)
Client
  ask information and use service
Server (IOC)
  provide information and service
Channel Access (CA)
  network protocol
Process Variable (PV)
  a single data unit exposed by a device
EPICS Logo and meaning
Centralized System

## Slide 6: How does EPICS work

## Slide 7: Example of EPICS IOC
EPICS IOC setup (Keysight Waveform Generator)
Proto file
  Keysight W.G. speaks SCPI protocol
  Map SCPI commands to PVs with Streamdevice (Support Module)
DB file
  Records that use the protocol files the IOC exposes PVs
Clients
  Access PVs via Channel Access
SCPI
CA
Proto file
DB file
Generator
Sever/Client
EPICS Control

## Slide 8: EPICS Application
EPICS UI Tools
Phoebus (CSS)
  Check PV status by GUI
  Communicate with CA protocol
Matlab Middle Layer
  Matlab interface
  Middle layer of EPICS PV
Pyepics
  via python
PLS-II Operation Status
CSS Tool view
ORM graph in Matlab
(E.Ahmadi, IPM)
Python control

## Slide 9: Motivation of Development DAQ
Beam Current Monitor (BCM)
Legacy workflow (problem)
  Oscilloscope exported values over Ethernet(SCPI)
  Operators viewed waveforms via VNC(Virtual Network Computing)
  Polling-based led to latency and data drop at higher repetition rates
Goal
  Build shot-synchronous DAQ and PVs to directly to EPICS
  If data is over user-set value, send stop signal
DAQ (Data Acquisition)
  Acquire the analog signal, digitize it
  Deliver snapshots and summaries via EPICS for remote operation
EPICS IOC
BCM
Legacy workflow

## Slide 10: DAQ Components
Xilinx Zynq SoC (System on Chip)
PS(Process System)
  Linux OS
  Build and run EPICS IOC
  Communicates over Ethernet using Channel Access
PL(Programmable Logic)
  Logic gate area (AND, OR, NOT)
  Connects to the ADC and stores snapshot in BRAM
AXI4 communication
  Communication protocol between PL and PS
ADC(Analog to Digital Conver)
  Converts the BCM current signal to samples
Xilinx Zynq
ADC Module
ADC Module
AXI4

## Slide 11: Design of DAQ Sequence
1. The PL continuously samples the ADC.
2. On an external trigger, the PL stores 1.3 ms sequentially in BRAM (buffer)
3. When the required count is reached, the PL asserts an interrupt
4. Interrupt signal is delivered to the PS (kernel)
5. The EPICS IOC reads BRAM and creates a waveform for PV

## Slide 12: EPICS IOC
Xilinx petalinux compiler (EPICS)
Record chain
  Record for 4 ADC channels waveform PV
  Accumulation the data
  Compared with the threshold value
  Action output to hardware
Operation view
  Beam current monitoring via CSS

## Slide 13: QnA