## Slide 1: Design and Simulation of X-ray tube for Hypersonic Vehicle Data Transmission Studies
나창선
2025. 10. 31

## Slide 2
Signal
modulation
communication
signal
X-ray detector
X-ray tube
plasma
NASA, 2019
Overview

## Slide 3
Crookes tube
Wilhelm Röntgen discovered X-rays using a Crookes tube.
1895
1913
Coolidge tube
William D. Coolidge developed the X-ray tube based on the thermionic emission principle. It used a heated filament and a high-vacuum system to emit electrons efficiently.
Modern X-ray Tubes
The Coolidge tube was later improved into various modern types of X-ray tubes, optimized for medical and industrial applications.
History of the X-ray Tube

## Slide 4
Heated tungsten cathode emits electrons by thermionic emission.
Electrons accelerate toward the anode and hit the target.
Only about 1% of the energy becomes X-rays.
The rest is converted into heat at the anode.
X-rays consist of bremsstrahlung and characteristic radiation.
Conventional X-ray Tube Operation
Rotating anodes improve cooling in medical systems.
Stationary anodes are used for compact designs.

## Slide 5
bremsstrahlung
characteristic X-ray
The X-ray spectrum consists of bremsstrahlung and characteristic X-rays.
To enhance bremsstrahlung efficiency, high-Z targets such as W (74), Mo (42), and Cu (29) are used.
X-ray Spectrum
Continuous radiation: Bremsstrahlung; Sharp peaks: Characteristic lines.

## Slide 6
Unlike filament-type tubes, CNT emitters require no heating or vacuum filament system, allowing compact and energy-efficient design.
CNT cathodes enable fast on/off switching, making pulsed X-ray emission possible.
CNT X-ray Tube
Fowler–Nordheim (F-N) equation:
𝐼: emission Current
𝑉: applied voltage
𝜙: work function
𝛽: field enhancement factor
CNT-based X-ray tubes have been commercially used in the medical since the mid-2010s.

## Slide 7
Focusing cup
Focusing electrode
A negative bias is applied to the focusing cup or focusing electrode to converge the electron beam onto a small focal spot.
Focusing

## Slide 8
The simulation was performed under 40 kV and 2 mA, less than 10 cm conditions.
Electrons emitted from the cathode are focused by the focusing electrode and accelerated toward the anode to generate X-rays.
Simulation Setup
(-)
(+)
cathode
anode
Focusing electrode
(-)

## Slide 9
Beam Size by Position
The simulated beam was successfully focused to 88.4 µm,
achieving the target beam size below 100 µm.
88.4 µm

## Slide 10
The beam focusing will be optimized based on the key parameters shown above:
Future Plan
– Cathode–focusing electrode distance (∝focusing) – Cathode–anode distance (∝defocusing) – Focusing electrode thickness (∝focusing) – Focusing aperture diameter (∝defocusing) – Focusing electrode voltage (∝focusing)

## Slide 11
Future Plan
– Dc-f fixed – Dc-a fixed – Thf : 15 (∝focusing) – df : 3 (∝defocusing) – Vf fixed
– Dc-f fixed – Dc-a fixed – Thf : 10 (∝focusing) – df : 3 (∝defocusing) – Vf fixed
– Dc-f fixed – Dc-a fixed – Thf : 10 (∝focusing) – df : 2 (∝defocusing) – Vf fixed
Thf
df

## Slide 12
This study is an X-ray tube for Data Transmission in plasma environments, where conventional radio transmission fails.
The field-emission CNT cathode enables compact, low-heat, and pulsed X-ray generation, which is essential for data transmission.
A CNT-based X-ray tube was designed and simulated under 40 kV / 2 mA conditions. The electron beam was successfully focused to 88.4 µm.
Beam focusing will be optimized by adjusting electrode geometry and bias voltage.
Summary

## Slide 13
(a)~(f) : 발산각에 따른 집속정도
(g) : Cathode(CNT)의 직경에 따른 집속정도