## Slide 1: Mode Locking in a Free-Electron Laser Amplifier

## Slide 3: Introduction
Free electron laser(FEL): a device in which an electron beam and a beam of electromagnetic wave colinearly travel through an undulator, causing an energy modulation at the periodicity of the radiation wavelength, which turns into a density modulation(microbunching) and generates amplified, coherent radiations.
Self-amplification spontaneous emission(SASE): Initial microbunching is initiated not by external seed radiation, but by the spontaneous radiation within the in the first section of undulator
- can produce hard X-ray
- poor longitudinal coherence

## Slide 4: Self-seeding FEL
Self seeding FEL: FEL seed by monochromatized SASE FEL radiation
- bandwidth can be improved more than 10 times

## Slide 5: Fresh Slice Multi-stage Amplification
Electron beam tilted by RF deflector or dechirper is used
Pulse duration can be reduced by few fs
First demonstrated at LCLS with tilted beam and 3 stages of amplification
High pulse energy deviation
A. Lutman et al, PRL 120, 264801, 2018

## Slide 6: Enhanced SASE
Enhanced SASE(E-SASE): A technique in which an electron beam is energy modulated by optical laser which overlaps only a short longitudinal section of the electron beam
Energy modulation in the wiggler is converted to density modulation in chicane
Pulse duration can be reduced by a few hundred attoseconds
Greater peak x-ray output, and gain saturation in a shorter length of undulator
A. A. Zholents, Phys. Rev. ST Accel. Beams, 8:040701 (2005).

## Slide 7: Mode-locked Laser
Mode-locked Laser: Laser whose phase between each modes is fixed

## Slide 8: Mode-locked Laser
Field of mode-locked laser:
If Am is same for all m, then the envelope of the field is
Ultrashort(fs~ps) laser pulses can be generated periodically

## Slide 9: Mode-locked Laser
Active mode locking: demonstrating mode locking by periodically modulating amplitude or phase of modes
- Frequency of modulation should be same with frequency spacing between laser modes

## Slide 10: SASE XFEL
Resonant wavelength of FEL:
For exponential growth, undulator length should be longer than gain length
FEL parameter
The temporal output power is noisy, comprising phase-uncorrelated pulses with separation 2πlc
Cooperation length : distance over which electrons interact coherently with the radiation field in one gain length
- defines coherence length
SASE spectrum bandwidth (rms)

## Slide 11: Mode-coupled/locked XFEL
By equally, periodically delaying electron bunch, spikes with frequency is integer) remains
Coherence length and cooperation length are increased due to electron delay
These modes are intrinsically coupled with the electron bunch over regions of a coherence length

## Slide 12: Mode-coupled/locked XFEL
Modes can be made to lock in phase by modulating the electron beam energy via laser with frequency same with
Phases of pulses are phase correlated over a distance

## Slide 13: Mode-coupled/locked XFEL
Maxwell’s eq:
One-dimensional case considered, slowly varying amplitude approximation() introduced
Let , and , then
By ignoring high gain FEL interaction, bunching parameter b is constant w.r.t , i.e.
Field equation for FEL :

## Slide 14: Mode-coupled/locked XFEL
Field equation for FEL :
: scaled interaction length along the undulator, : scaled electron bunch coordinate
By Fourier transform w.r.t. ,
With initial condition and adding term in the equation,
Intensity of radiation

## Slide 15: Mode-coupled/locked XFEL
Intensity of radiation ()
Number of modes: 2Ne-1
Mode separation: corresponding (Ts: time taken for radiation to travel the slippage length)
Mode width:
Se=1, N=5
Se=5, N=2
Se=5, N=7

## Slide 16: Mode-coupled/locked XFEL
Optical klystron effect: reduction of gain length due to dispersion by chicane
Chicane converts beam energy modulation into density modulation due to longitudinal energy dispersion parametrized via D=R56/2lc
The combined effects of the enhanced slippage (Se≥1) and gain length reduction (Ge<1) give a modified cooperation length
R.Coisson, Particle Accelerators, (1981)

## Slide 17: Simulation result(EUV)
Delay by chicane:
Se=5, Ge=0.65
SASE pulse duration:
Pulse width of mode-coupled FEL: (FWHM) with separation =2.48fs < coherence length
Wavelength separation 0.21nm

## Slide 18: Simulation result(EUV)
Pulse width of mode-locked FEL: with separation 2.48fs
Theoretical pulse width of homogeneously active mode-locked FEL:
: modulation frequency, N0: number of modes)
SASE noise still remains as the slowly varying envelope of mean period

## Slide 19: Simulation result(X-ray, LCLS)
Pulse width of mode-locked FEL: with separation 150as
Theoretical pulse width of homogeneously mode-locked FEL:

## Slide 20: Simulation result
Bunching parameter is affected by dispersion from chicane
A criterion for operation
if
For a 4-dipole chicane with equal magnet and drift lengths L,
For phase matching with N independently powered chicanes, should be satisfied
EUV:
X-ray:
Both systems are feasible to demonstrate

## Slide 21: Experiment result in SwissFEL
Athos(3.4GeV)
16 undulators modules, 52 periods×3.8 cm≈2 m each
- nine undulators were used for MC-SASE
Photon energy: 500~600eV
Delay by chicane: 2fs(600nm)
E. Prat et al. PRL 133, 205001 (2024)

## Slide 22: Conclusion
Mode-locking of FEL can be demonstrated by equally, periodically delaying electron bunch via chicane and modulator laser
Reduction of pulse length to tens~hundreds of attoseconds
Limitation: lower spectral brightness compared to SASE, undulator shorter than saturation length required, wavelength of modulator laser should be changed when changing electron delay