## Slide 1: Study of bunch shortening
Young Min Park
Division of Advanced Nuclear Engineering (DANE), POSTECH
2026-01-22, Pohang, South Korea

## Slide 2: Bunch shortening
2
Why bunch shortening?
Improve the probe time resolution
Cover the ~ 1 ps gray region.
To achieve Bunch shortening
Two method: Reduce / Bunch shortening with HC (Crab-cavity/Increase main voltage)
Bunch shortening with HC
Increase voltage gradient Strong restoring force Short bunch length
Bunch shortening and instability
Bunch shortening mode should be largely robust against collective effects:
A strong longitudinal restoring force
Higher synchrotron frequency tends to weaken mode coupling Operating with negative detuning satisfy the Robinson damping condition.
Consider about the effects of high-frequency impedance
Gray region

## Slide 3: Lifetime of low-alpha mode
3
Lifetime
In general, the beam lifetime depends on the bunch length and the bunch charge.
If the bunch length 1-2 ps level, a simple estimate shows that the lifetime can decrease by about of factor of ~ 8.
Typical parameter of storage rings.
K-4GSR current operation status: 0.3 mA per bunch (Brightness/400 mA) with ~ 9 ps bunch length Lifetime: 5-6 h
If the bunch length is reduced to about 3-4 ps, ~ 0.1 mA per bunch may need to maintain a Touscheck lifetime
Name | Diamond |  | Soleil |  | BESSY-II | 
Operation Mode | Standard mode ) | Timing mode | Normal mode () | Low- mode () | Standard mode | Low- mode ()
Bunch charge | 0.32 mA | 0.025 mA | 1.36/5 mA | 0.065/0.065 mA | 0.9 mA | 0.045/ 0.285 mA
Bunch length | 18 ps | 3.5 ps | 18 ps | 4.8 ps | 45 ps | 7/16 ps
Bunch lifetime | 20 h | 10 h | 18 h | 10 h | 5 h (Touschek ~ 25h) | 20/10 h
Name | Diamond |  | Soleil |  | BESSY-II | 
Operation Mode |  |  |  |  |  | 
Bunch charge | 0.32 mA | 0.025 mA | 1.36/5 mA | 0.065/0.065 mA | 0.9 mA | 0.045/ 0.285 mA
Bunch length | 18 ps | 3.5 ps | 18 ps | 4.8 ps | 45 ps | 7/16 ps
Bunch lifetime | 20 h | 10 h | 18 h | 10 h | 5 h (Touschek ~ 25h) | 20/10 h

## Slide 4: Bunch shortening setting
4
Setting:
Numerical analysis
ps
kHz
2.522 kHz
2.072 kHz
2.905 kHz
3.244 kHz

## Slide 5: Simulation result
5
I = 10 mA

## Slide 6: Simulation result
6
I = 5 mA

## Slide 7: Simulation result
7
I = 1 mA

## Slide 8: Some issues about result
8
Centroid issue
Because the bunch does not have a centroid at .
A straight mitigation method is to adjust the main cavity RF phasae.
Sensitivity of HHC detuning
At low current, even tens of Hz detuning change can produce a large change in longitudinal distribution and bunch length.
In particular, for 1 mA operation, a ~10 Hz tuning difference change from -3 to -4.
Solution
Apply short-bunch operation to brightness mode (multi-bunch).
Primary goal: Increase total current allows large detuning frequency (less sensitive). Reduce single-bunch current to improve Touscheck lifetime.
Since other facilities often run low- mmainly in multi-bunch / hybrid schemes, this approach may be practical.

## Slide 9: Bunch shortening with brightness mode
9
Setting:

## Slide 10: Bunch shortening to ~ 1 ps.
10
To achieve a reduction in bunch length from 9 ps to ~ 1 ps..
Limitation
HHC voltage has to be increased too much – By almost a factor of 80.
Detuning frequency close to 0 Hz, which is experimentally unrealistic.
Solution
Previously, we obtained and reaching may be achievable in brightness-mode operation.
Reducing by about a factor of 6 could provide ∼7× bunch shortening.
Voltage of main/harmonic cavity
Phase of main/harmonic cavity
Beam current
Amplitude of bunch form factor
Phase of bunch form factor
Shunt impedance
Tuning angle
Cavity quality factor
Detuning frequency
: rf-frequency

## Slide 11: Feasible operating Range of
11
Setting:

## Slide 12: Coherent/Incoherent frequency
12
Setting:
In principle, increase increase large synchrotron frequency .
However, the coherent frequency shows a decreasing trend as increases, indicating that a cavity mode is being excited.
Nevertheless, since this cavity mode satisfied the damping condition, the beam motion remains stable.
Cavity mode: Appears when the detuning frequency close to .
Analytic result of Coherent/Incoherent frequency and FFT result.
ELEGANT Coh. : Coherent frequency of the beam.
ELEGANT Incoh. : Single particle frequency

## Slide 13: Reducing 𝛼
13
ILMaxtrix
Setting:

## Slide 14: Thank you for your attention!
14