## Slide 1
A machine-learning based closed orbit feedback for the SSRF storage ring
JKPS (02/20)
20, FEB. 2026
류연찬
Control Group
Pohang Accelerator Laboratory, POSTECH

## Slide 2
Outline
JKPS (02/20)
2
Chosen Reason
Principle
  Orbit Feedback, Machine Learning
Experiment Research
  Environment RF Feedback / ML Feedback / SOFB / Long-term test
Discussions

## Slide 3
Introduction
JKPS (02/20)
3
Chosen Reason
  Want to study about ML/AI
  Application of Orbit Feedback
EPICS CA 통신

## Slide 4
Principle – Orbit Feedback
JKPS (02/20)
4
Closed Orbit Distortion(COD)
  In an ideal storage ring, the electron beam follow a periodic closed orbit
  Magnet field errors, misalignments, introduce new design orbit
  This deviation from ideal orbit call COD
Orbit Response Matrix
  Can be experimentally measured by correctors and BPM
ORM
IRM
Pseudo-Inverse
Relation of ORM and IRM
Closed Orbit Distortion

## Slide 5
Principle – Orbit Feedback
JKPS (02/20)
5
Pseudo Inverse & Singular Value Decomposition(SVD)
  Response Matrix is (MxN) square matrix, so it can’t solve inverse matrix directly.
  Pseudo Inverse Matrix by SVD
  SVD : decomposition by 3 matrix, which has singular value and orthogonal matrix
  ;
Limitation of Conventional SOFB
  Difficult to update the Response Matrix during beam operation
  Inversed solution obtained by SVD may not be unique
기존 역수 :

## Slide 6
Weight
bias
Principle – Machine Learning
JKPS (02/20)
6
Machine Learning
  Each layer consists of multiple nodes (neurons)
  Hidden layers are located between the input layer and the output layer
  the input values are multiplied by weights, summed together with a bias term, and then passed through an activation function
  The weights and biases are randomly initialized and optimized through backpropagation to minimize the loss function

## Slide 7
Principle – Machine Learning
JKPS (02/20)
7
Loss function
  Quantifies the difference between the predicted values and the true values
  During training, the weights and biases are iteratively updated to minimize the loss function
Backpropagation
  Optimize the weights and biases to minimize the loss function
Loss function
Backpropagation

## Slide 8
Experiment Research
JKPS (02/20)
8
Neural network model (Environment)
  Keras for learning modules and API based on TensorFlow (with Python)
  Learning rate : 0.01 (for backpropagation)
  100 nodes each at 3 hidden layers
  Activation function : Rectified Linear Unit(ReLU). f(x)=max(0,x)
Storage Ring ML Environment
  Collect data by EPICS
  Input : 138 BPM / Output : 80 Corrector and RF
  Top-up mode (201~202 mA)
  40 min for measure. 800 sets. (700 for training, 100 for test)
Rectified Linear Unit

## Slide 9
Experiment Research - RF
JKPS (02/20)
9
Result for 4 experiments
  RF Feedback / ML Feedback / SOFB / Long-term test
RF Feedback
  Reduce 30 dB. limit change 10 dB once
  After 9th seconds, RF change reduce 30 dB
  RF main freqency back to original value within 10 seconds
RF Feedback

## Slide 10
Experiment Research – ML Feedback
JKPS (02/20)
14
ML Feedback (Joint of RF and Corrector)
  5 seconds feedback at a time
  Gave random disturbance by corrector
  Increased RF freqency by 15 dB
  Can corrector orbit back near previous level
  RF also corrected back initial values
↑Horizontal
↓Vertical
RF Frequency→

## Slide 11
Experiment Research – SOFB
JKPS (02/20)
15
Slow Orbit Feedback (SOFB)
  3 seconds feedback at a time
  Beam Position seem to be match
  (Different with ML) Residual current at Corrector
  Also seen RF doesn’t meet
Reason of this happen
  SOFB use many corrector even if need one corrector
  ML can locate corrector to correct orbit
RF Frequency→
↑Horizontal
↓Vertical

## Slide 12
Compare with ML and SOFB
JKPS (02/20)
112
ML Feedback ↑
SOFB ↓
Vertical →
←Horizontal

## Slide 13
Experiment Research – Long Term
JKPS (02/20)
16
16 hours operation test
  3pm~7am(next morning)
  RF Freq. variation by environment temperature
  Fluctuation at 3rd hours supposed to be unstable of machine
RF Frequency →
 | Horizontal | Vertical
Max. Orbit Drift | 40 μm | 20 μm
RMS BPM | 15 μm | 8 μm
↑Horizontal
↓Vertical
↑3pm
7am↑

## Slide 14
Discussion
JKPS (02/20)
14
Does ML guarantee Orbit Stability?
  Mapping from BPM reading to appropriate corrector currents
  Seem like it doesn’t mean for Orbit stable
  But It’s good for prevent saturation of corrector current
  Maybe also good at capture drift-related nonlinearities