## Slide 1
Study of Virtual Pepper-Pot

## Slide 2
Introduction
What is the Virtual Pepper-Pot (VPP)?
Motivation
Pepper Pot
Virtual Pepper Pot
Full 4D phase space reconstruction
Generate pepper-pot like image using slit scan
Limitation of conventional method “Pepper-pot (PP)”
Resolution & Signal trade-off
[1]E. Cosgun et al., “Characterization and benchmarking of complete 4D transverse phase space for high-intensity ion beams using novel virtual pepper-pot technique,” Sci Rep, vol. 15, no. 1, p. 40761, Nov. 2025, doi: 10.1038/s41598-025-24550-2.
Small apertures ↔ Reduced signal (Low SNR)
Dense holes ↔ Beamlets overlap

## Slide 3
Principle of VPP
1) VPP Image Processing
Minimum Bit Principle
Pepper Pot
Virtual Pepper Pot
: Select the minimum intensity between horizontal and vertical slit scans to represent the physically overlapping beam fraction and avoid overestimation

## Slide 4
2) Reconstruction
2D Gaussian Fitting
y (mm)
y (mm)
2D Gaussian fitting determines the beamlet peak position , which is used together with slit center to compute the divergence
Using these data, the emittance and Twiss parameters at the slit position are reconstructed

## Slide 5
Coupled system
Eigen-emittance
Full 4D phase space reconstruction allows evaluation of coupling through eigen-emittance
In the presence of transverse coupling, the projected emittances are no longer conserved invariants of the system
⇒ Eigen-emittances are symplectic invariants of the 4D phase space matrix
{
Coupling factor
means that the beam is uncoupled

## Slide 6
Simulation Setting: From TraceWin to Xsuite
<KOMAC BTS layout>
Xsuite Simulation Lattice
Input Beam : After the RFQ
Proton, 1 MeV, 3σ-truncated 6D Gaussian beam
Macro particles = 100,000
No collective effects (e.g. Space charge effect)
Lattice
Particles
Parameters | Input
Parameters | Input
TraceWin Simulation Data
Parameters | output
Parameters | output
Parameters | output
Parameters | output
TraceWin Simulation Data
Xsuite Simulation Data

## Slide 7
Slit position (m): 3.2m
Screen position (m): 3.31m
Slit width (mm): 0.2mm
Ground Truth at Slit Position
Parameters | Slit position
Parameters | Slit position
Space charge effect를 꺼서 논문과 parameter 수치가 다름.
Scan index 수를 맞추기 위해 빔 사이즈 기준으로 복원 위치 선정.

## Slide 8
Virtual Pepper-Pot Image Processing
Screen Position Ground Truth
Scan Range: (-20mm, 20mm)
Screen Range: (-20mm, 20mm)
# of Bin: 516 (), 1024 ()
Slit Scan Spacing: 0.8mm, 1mm
Bins: 516
Slit Scan Spacing: 0.8mm

## Slide 9
Reconstruction Accuracy
Bins / Slit scan spacing | error | error | error
516 / 0.8 mm | 1.59 % | 8.28 % | 6.55 %
516 / 1.0 mm | 2.66 % | 8.76 % | 5.84 %
1024 / 0.8 mm | 3.37 % | 0.72 % | 4.08 %
1024 / 1.0 mm | 4.23 % | 0.65 % | 3.63 %
Bins / Slit scan spacing |  |  | 
516 / 0.8 mm | 1.59 % | 8.28 % | 6.55 %
516 / 1.0 mm | 2.66 % | 8.76 % | 5.84 %
1024 / 0.8 mm | 3.37 % | 0.72 % | 4.08 %
1024 / 1.0 mm | 4.23 % | 0.65 % | 3.63 %
Emittance
Twiss parameters & Beam size
Higher bin resolution significantly improves and accuracy
Slit spacing has relatively minor influence compared to bin number
Parameter | Error Range
 | 6-13 %
 | 11-21 %
 | 6-12 %
 | 11-22 %
 | 5-8 %
 | 5-7 %
Parameter | Error Range
 | 6-13 %
 | 11-21 %
 | 6-12 %
 | 11-22 %
 | 5-8 %
 | 5-7 %
Twiss parameters show higher sensitivity compared to emittance reconstruction due to error propagation
Twiss parameter errors are reduced by nearly half when increasing bins from 516 to 1024

## Slide 10
Slit Position Ground Truth
Recon: Assuming Gaussian distribution
Recon: Gaussian Mixture Model

## Slide 11
Ground truth
Reconstruction
Numerical precision leads to
Numerical precision leads to
임의의 coupling
Parameters | Ground Truth | Reconstruction | Error (%)
 | 7.135480 | 6.881567 | 3.56%
 | 3.523232 | 3.407003 | 3.30%
 | 7.896109 | 7.576622 | 4.05%
 | 1.603947 | 1.679069 | 4.68%
 | 12.664937 | 12.721668 | 0.45%
 | 12.664940 | 12.721671 | -
 | 0.985 | 0.843 | -
 | 3.283411 | 2.994380 | 8.80%
 | 4.753272 | 4.457140 | 6.23%
 | 5.991377 | 5.468239 | 8.73%
 | 7.073228 | 6.632064 | 6.24%
 | 4.840322 | 4.539386 | 6.22%
 | 4.092296 | 3.896856 | 4.78%
Parameters | Ground Truth | Reconstruction | Error (%)
 | 7.135480 | 6.881567 | 3.56%
 | 3.523232 | 3.407003 | 3.30%
 | 7.896109 | 7.576622 | 4.05%
 | 1.603947 | 1.679069 | 4.68%
 | 12.664937 | 12.721668 | 0.45%
 | 12.664940 | 12.721671 | -
 | 0.985 | 0.843 | -
 | 3.283411 | 2.994380 | 8.80%
 | 4.753272 | 4.457140 | 6.23%
 | 5.991377 | 5.468239 | 8.73%
 | 7.073228 | 6.632064 | 6.24%
 | 4.840322 | 4.539386 | 6.22%
 | 4.092296 | 3.896856 | 4.78%

## Slide 12
Slit Position Ground Truth
Recon: Gaussian Mixture Model

## Slide 13
Summary & Plan
Summary
Virtual Pepper-Pot technique enables full 4D transverse phase space reconstruction
Under high-resolution conditions, reconstruction errors are below 10%, and below 5% for emittance
Simulations with intentionally introduced coupling confirm that Virtual Pepper-Pot successfully reconstructs transverse coupling effects
Plan
Conduct simulations based on eLABs Gun1 data and implement the “differential slit method”
Study and simulate the solenoid scan for validation of the Virtual Pepper-Pot reconstruction and experimental comparison
Measure solenoid scan data at PAL-XFEL in March or August

## Slide 14
Parameters | Ground Truth | Reconstruction (bins = 516) (slit space: 0.8mm) | Reconstruction (bins = 516) (slit space: 1mm) | Reconstruction (bins = 1024) (slit space: 0.8mm) | Reconstruction (bins = 1024) (slit space: 1mm)
 |  | 3.421198 | 3.384118 | 3.359351 | 3.329536
 |  | 3.814789 | 3.831987 | 3.497718 | 3.546107
 |  | 13.050429 | 12.964562 | 11.748464 | 11.804704
 |  | 1.511921 | 1.464033 | 1.579179 | 1.511645
 |  | 3.748305 | 3.826055 | 4.172718 | 4.209248
 |  | 2.809510 | 2.751108 | 2.933928 | 2.843531
 |  | 5.519916 | 5.658486 | 6.188546 | 6.247286
 |  | 2.274331 | 2.225861 | 2.303262 | 2.243452
 |  | 3.781400 | 3.829020 | 3.820339 | 3.863476
Parameters | Ground Truth | Reconstruction (bins = 516) (slit space: 0.8mm) | Reconstruction (bins = 516) (slit space: 1mm) | Reconstruction (bins = 1024) (slit space: 0.8mm) | Reconstruction (bins = 1024) (slit space: 1mm)
 |  | 3.421198 | 3.384118 | 3.359351 | 3.329536
 |  | 3.814789 | 3.831987 | 3.497718 | 3.546107
 |  | 13.050429 | 12.964562 | 11.748464 | 11.804704
 |  | 1.511921 | 1.464033 | 1.579179 | 1.511645
 |  | 3.748305 | 3.826055 | 4.172718 | 4.209248
 |  | 2.809510 | 2.751108 | 2.933928 | 2.843531
 |  | 5.519916 | 5.658486 | 6.188546 | 6.247286
 |  | 2.274331 | 2.225861 | 2.303262 | 2.243452
 |  | 3.781400 | 3.829020 | 3.820339 | 3.863476
Reconstruction

## Slide 15
Parameters | Ground Truth | Recon error (%) (bins: 516) (slit space: 0.8mm) | Recon error (%) (bins: 516) (slit space: 1mm) | Recon error (%) (bins: 1024) (slit space: 0.8mm) | Recon error (%) (bins: 1024) (slit space: 1mm)
 |  | 1.59 % | 2.66 % | 3.37 % | 4.23 %
 |  | 8.28 % | 8.76 % | 0.72 % | 0.65 %
 |  | 6.55 % | 5.84 % | 4.08 % | 3.63 %
 |  | 10.60 % | 13.43 % | 6.62 % | 10.61 %
 |  | 21.14 % | 19.51 % | 12.21 % | 11.45 %
 |  | 10.33 % | 12.19 % | 6.36 % | 9.24 %
 |  | 21.96 % | 20.00 % | 12.51 % | 11.68 %
 |  | 6.20 % | 8.20 % | 5.01 % | 7.48 %
 |  | 7.60 % | 6.43 % | 6.65 % | 5.59 %
Parameters | Ground Truth | Recon error (%) (bins: 516) (slit space: 0.8mm) | Recon error (%) (bins: 516) (slit space: 1mm) | Recon error (%) (bins: 1024) (slit space: 0.8mm) | Recon error (%) (bins: 1024) (slit space: 1mm)
 |  | 1.59 % | 2.66 % | 3.37 % | 4.23 %
 |  | 8.28 % | 8.76 % | 0.72 % | 0.65 %
 |  | 6.55 % | 5.84 % | 4.08 % | 3.63 %
 |  | 10.60 % | 13.43 % | 6.62 % | 10.61 %
 |  | 21.14 % | 19.51 % | 12.21 % | 11.45 %
 |  | 10.33 % | 12.19 % | 6.36 % | 9.24 %
 |  | 21.96 % | 20.00 % | 12.51 % | 11.68 %
 |  | 6.20 % | 8.20 % | 5.01 % | 7.48 %
 |  | 7.60 % | 6.43 % | 6.65 % | 5.59 %