## Slide 1: High-power EUV free-electron laser for future lithography
Minseo Jeong

## Slide 3: Index
Energy recovery linac(ERL)
EUV lithography
Setup of EUV-ERL
Proof of concept with cERL

## Slide 4: Energy Recovery Linac
Energy recovery linac(ERL): recovers energy at linac by deceleration of used beam
Originally proposed for efficient e+/e- collider(Tigner, 1965)
Demonstrated after development of reliable SRF linac(1987)

## Slide 5: Energy Recovery Linac
Fields in a cavity. a) filling an empty cavity, b) an accelerated beam loads the cavity, c) a decelerated beam fills the cavity

## Slide 6: Advantages of Energy Recovery Linac
High current/high beam power(~100mA @ GeV)
Flexible beamline
Short bunch
High energy efficiency

## Slide 7: EUV Lithography
Photolithography: manufacturing process that involves using light to transfer a pattern onto a photoresist layer deposited on a silicon wafer
Resolution of lithography=
Numerical aperture(NA)= nsinθ<0.9
k1= process parameter(0.25<k1<1)
Notes: NA: maximum range of angles over which the optical system can accept light

## Slide 8: EUV Lithography
Current method for EUV light source: laser-produced plasma
Tin plasma generated by a CO2 drive laser and tin droplets generates EUV light
Contamination risk by tin debris

## Slide 9: EUV Lithography
Stochastic effect happens during EUV lithography due to high photon energy
High EUV power required to mitigate
(1.5 kW for the 3 nm node, 2.8 kW for the 2 nm node)

## Slide 10: EUV-ERL
Parameters | Target value
Wavelength | 13.5 nm
EUV Power | 10 kW
Bunch charge | 60 pC
Beam energy | 800 MeV
Repetition frequency | 162.5 MHz
Average current | 9.75 mA
Accelerating gradient | 12.5 MV/m
Number of cavities | 64
cERL-FEL Accelerator Parameters

## Slide 11: EUV-ERL
Injector: DC photogun(500kV) + 2 cryomodule w/ 3 2-cell SRF cavity

## Slide 12: EUV-ERL
Linac: 16 cryomodules(64 9-cell cavities w/ gradient 12.5MV/m)
Quadrupole triplet is installed between every 2 cryomodules
Cells were optimized for minimization of Epk/Eacc and Bpk/Eacc, flatness of field, and low Q factor of HOM
Cavity Parameters | KEK-EUV | TESLA
Frequency (MHz) | 1300 | 1300
Iris diameter (mm) | 70 | 70
R/Q (Ω) | 1009 | 1036
G (Ω) | 269 | 270
Ep/Eacc | 2.0 | 2.0
Hp/Eacc (mT/(MV/m)) | 4.23 | 4.26
BBU threshold(mA) | ~190 | ~80
TESLA Center Cell
End Cell A
End Cell B
HOM Damper
HOM
Φ100 mm BP
Φ110 mm BP
Notes: field emission - Epk/Eacc
thermal load/quench - Bpk/Eacc를 4.25mT/(MV/m

## Slide 13: EUV ERL
Higher order mode(HOM) in the cavity can cause increase of energy spread(longitudinal) and beam breakup(BBU) instability(transverse)
Beam line absorber was used(AlN, 100W at 80K) for broadband HOM damping
Position of absorber in the cavity was optimized
Notes: Heat load at cryomodule vs cost

## Slide 14: EUV-ERL
Arc

## Slide 15: EUV-ERL
Beam parameter after 1st arc:
- normalized horizontal/vertical emittances: 2.0/ 0.9 mm·mrad
- bunch length: 39 fs(rms)
- energy spread: 0.1%

## Slide 16: EUV-ERL
Undulator: 18 circular-polarizing (helical) undulators of 4.9m length

## Slide 17: EUV-ERL
Optical beamline

## Slide 18: Advantages of EUV-ERL
Generates high EUV power (>10 kW) without tin contamination on the Mo/Si mirror
Upgradable for shorter wavelength
Polarization controllable
Efficient(electricity and cost)

## Slide 19: EUV-ERL
EUV-ERL beamline can be converted for BEUV(6.6~6.7nm) by increasing the beam energy by a factor of
For multi-pass ERL, threshold of BBU can be decreased

## Slide 20: EUV-ERL
Polarization of EUV is important for better high NA operation
- p-pol:
- s-pol:
TE(s-polarization)
TM(p-polarization)
θ : the incident angle
n : the refractive index

## Slide 21: EUV-ERL
Electricity consumption:
-EUV-FEL : ~7.0 MW/10-kW EUV ⇒ ~0.7 MW/1-kW EUV(or scanner)
-LPP : ~1.15 MW/500-W EUV(2025) ⇒ ~2.3 MW/1-kW EUV(or scanner)
Construction cost
-EUV-FEL : ~US$400M/10-kW EUV ⇒ ~US$40M/1-kW EUV(or scanner)
-LPP : ~US$20M/500-W EUV(2025) ⇒ ~US$40M/1-kW EUV(or scanner)
Running cost
-EUV-FEL : ~US$40M/10-kW EUV ⇒ ~US$4M/1-kW EUV(or scanner)
-LPP : ~US$15M/250-W EUV(2023) ⇒ ~US$60M/1-kW EUV(or scanner)
Item | Electric power [MW]
Refrigerator System | 3.2
RF Source | 1.3
Other Components | 1.0
Infrastructure | 1.5
Total | 7.0
Notes: Infra: cooling-water system, an air-conditioning system, an illumination system, etc

## Slide 22: PoC of ERL
cERL
Notes: wl:10~20um

## Slide 23: PoC of ERL
Linearly-polarizing adjustable phase undulators (APUs) with a period of 24 mm for cost reduction
Diagnostics: MCT (HgCdTe) detector, energy meter
Dump line
Radiation monitors

## Slide 24: PoC of ERL
Burst mode for beam tuning →CW mode

## Slide 25: PoC of ERL
FEL commissioning
The FEL energy of undulator 2 was lower than simulation due to space charge force

## Slide 26: Future Plan
CW operation in 10mA
- upgrade of electron gun
Construction of cryomodule for main linac(~2027)

## Slide 27: Summary
High-power EUV-ERL was developed for more powerful EUV light source
The EUV-ERL has many advantages in high EUV power, upgradability to BEUV, polarization control, and low electricity consumption and cost.
Generation of SASE-FEL emission at the cERL IR-FEL was achieved for PoC of the EUV-ERL.