## Slide 1: Group Meeting 260313
Minseo Jeong

## Slide 2: UED Experiment Schedule
~Mar: Preparation for UED experiment
- test of vacuum chamber
Apr~May: solid state UED
Jul~Aug: gas pump-probe UED
Oct~Nov(delayed): Installation of new modulator and klystron

## Slide 3: Energy Recovery Linac
Energy recovery linac(ERL): recovers energy at linac by deceleration of used beam
Originally proposed for efficient collider(Tigner, 1965)
Demonstrated after development of reliable SRF linac
Nakamura et al., Jpn. J. Appl. Phys.(2023)

## Slide 4: EUV Lithography
Photolithography: manufacturing process that involves using light to transfer a pattern onto a photoresist layer deposited on a silicon wafer
Resolution of lithography=
Numerical aperture(NA)= nsinθ<0.9
k1= process parameter(0.25<k1<1)
Notes: NA: maximum range of angles over which the optical system can accept light

## Slide 5: EUV Lithography
Stochastic effect happens during EUV lithography due to high photon energy
High EUV power required to mitigate
(1.5 kW for the 3 nm node, 2.8 kW for the 2 nm node)

## Slide 6: EUV-ERL
Parameters | Target value
Wavelength | 13.5 nm
EUV Power | 10 kW
Bunch charge | 60 pC
Beam energy | 800 MeV
Repetition frequency | 162.5 MHz
Average current | 9.75 mA
Accelerating gradient | 12.5 MV/m
Number of cavities | 64
cERL-FEL Accelerator Parameters

## Slide 7: SRF Cavity in EUV-ERL
For storage and usage for acceleration of energy extracted by decelerated beam, SRF cavity(Q=~1010) should be used
Niobium(Nb) is used as a material for SRF cavity due to its high critical temperature(9.2K), availability of high purity
Elliptical cell to avoid field emission
More cell per one cavity increases efficiency, but makes it harder to damp higher order mode(HOM)
Aune et al., PRAB-ST(2000)

## Slide 8: SRF Cavity in EUV-ERL
Accelerating gradient
- Most of SRF cavities of ERL operates under 20MV/m, but some facilities operate in higher gradient recently (e.g. LCLS-II-HE: 23MV/m)
- Higher gradient increases efficiency, but increases dynamic RF loss, field emission
RF resistance at surface :
- Δ: gap energy of Cooper pair
- Rres: residual resistance(7nΩ for 2K Nb)
- Rs=14nΩ for 2K Nb

## Slide 9: SRF Cavity in EUV-ERL
Geometric factor
- ~270Ω for 1.3GHz SRF cavity
Quality factor: determines how well the cavity can store energy
-
Dynamic RF loss:
Shunt impedance : measure of efficiency with which an eigenmode of cavity interacts with particle beam
- R/Q=

## Slide 10: Optimization on Fundamental Mode
Cells should be optimized for minimization of Epk/Eacc and Bpk/Eacc, flatness of field
Epk/Eacc should be minimized(<2.1) to prevent field emission and X-ray radiation
Bpk/Eacc should be minimized(<4.25mT/(MV/m)) to prevent thermal load/quench
Radius of cavity: 2Req≅0.9λ (Req=103.3mm for 1.3GHz cavity)

## Slide 11: Optimization on Fundamental Mode
To flatten the acceleration field, length of end cell should be shorter than that of center cell
Guo et al., JINST(2025)
Konomi et al., PRAB(2023)

## Slide 12: Higher Order Mode Damping
When the particle passes through the cavity, higher order mode is excited
The wakefield left behind affects other bunches
- Transverse HOM increases energy spread and power dissipation ()
- Longitudinal HOM deflects beam and causes beam breakup instability(BBU)
Threshold of BBU:
-: recirculation time, ω: HOW angular freq.

## Slide 13: Higher Order Mode Damping
Coaxial HOM damper: couples HOM mode by hook coupler which works as an antenna
- The power is picked up by a TEM coaxial transmission line cable and transmitted outside the cryomodule
- Clean environment
- Narrowband, complicated, frequent vacuum leak, multipacting, field asymmetry caused by antenna

## Slide 14: Higher Order Mode Damping

## Slide 15: Higher Order Mode Damping
Waveguide HOM damper
- Provide natural cutoff filter for fundamental mode
- Damping efficiency is usually optimized for one (1st) waveguide mode
- Increasing the magnetic fields at the cavity-waveguide intersection leads to a decrease of the quench field limit

## Slide 16: Higher Order Mode Damping
Beam line absorber: absorbs HOM power by dielectric loss and emits it as heat
- Larger beam pipe radius is required to make HOM wave pass
- Broadband, symmetric damping
- Occupies additional beam line space
- Requires adequate thermal management
(e.g. position of absorber)

## Slide 17: Higher Order Mode Damping
Loss tangent() of the absorber material should be higher than 0.1
The absorption performance should be maintained at low temperature(~80K)
Ferrite is usually used as a material for absorber, but ceramic such as SiC(Cornell ERL) and AlN(KEK, LCLS-II) are used recently

## Slide 18: Multipacting
Multipacting : an electron multiplication based on resonance breakdown phenomenon inside RF cavity
- drain the energy stored in the cavity
For elliptical cell, MP occurs usually in equator region
- flat region at the equator should be eliminated

## Slide 19: Multipacting
Multipacting becomes problem in certain RF field band
(e.g. 17~24MV/m for 1.3GHz TESLA cavity)
Multipacting process(frequently quenching the cavity) can decrease the number of occurrence of MP
V. Shemelin, Phys. Rev. ST Accel. Beams (2013)

## Slide 20: Field Emission
Field emission: local electric-field enhancements caused by contamination or surface defect to enable the extraction of unwanted electrons
- causes damage inside the cavity
The impact of FE for SRF cavity is high due to its smaller surface power dissipation
FE current density increases exponentially as acceleration gradient increases
- work ftn of Nb)
Decreased by high pressure fluid rinsing

## Slide 21: Fundamental Mode Coupler
Fundamental mode coupler couples RF cavity and RF source by antenna
Antenna insertion depth, external quality factor()s and the distance from the FPC to the end cell of the superconducting cavity
Using single coupler can break symmetry
- compensation stub should be introduced on the opposite side of the main couple

## Slide 22: SRF Cavity in EUV-ERL(KEK)
Linac: 16 cryomodules(64 9-cell cavities w/ gradient 12.5MV/m)
Based of TESLA 1.3GHz cavity
Quadrupole triplet is installed between every 2 cryomodules
Cavity Parameters | KEK-EUV | TESLA
Frequency (MHz) | 1300 | 1300
Iris diameter (mm) | 70 | 70
R/Q (Ω) | 1009 | 1036
G (Ω) | 269 | 270
Ep/Eacc | 2.0 | 2.0
Hp/Eacc (mT/(MV/m)) | 4.23 | 4.26
TESLA Center Cell
End Cell A
End Cell B
HOM Damper
HOM
Φ100 mm BP
Φ110 mm BP

## Slide 23: SRF Cavity in EUV-ERL(KEK)
Different pipe radius for damping different HOM modes
Beam line absorber was used(AlN, 100W at 80K) for HOM damping
Notes: Heat load at cryomodule vs cost

## Slide 24: SRF Cavity in EUV-ERL(China)
7-cell cavity based on cavity in Cornell ERL

## Slide 25: SRF Cavity Baking
Surface process of SRF cavity:
- Electro polishing
- Annealing(800°C, 3hr, hydrogen degassing)
- High pressure water rinsing
- Assembly
- Baking(120°C, 48hr)

## Slide 26: SRF Cavity Baking
N-doping at 800 °C
- higher quality factor
- lower quench field
N-infusion at 120°C after annealing
- high cavity gradient
- challenge on reproducibility

## Slide 27: SRF Cavity Baking
Two step baking(3hr at 70~75°C before 120°C baking)
- higher gradient (up to 50MV/m)
Mid-T (furnace) baking: baking for 3hr at 300~400°C after/before assembly
- similar performance with N doping
- no electro polishing required
- for mid-T furnace baking,
contamination issue remains

## Slide 28: Nb3Sn Coating
Nb3Sn has higher critical temperature(18K) than bulk Nb
Nb3Sn coated cavity has same Q at 4K with Nb bulk cavity at 2K
Increases cryogenic efficiency by factor of 3~4
Easily brittles → vulnerable for physical stress
Low reproducibility limits maximum acceleration gradient

## Slide 29: Research Goal
Design of L-band cavity for EUV ERL
- Higher shunt impedance, lower Epk/Eacc and Bpk/Eacc
- Damping of HOM mode
- High gradient and quality factor( 2×1010 at 20MV/m)

## Slide 30: Research Plan
2026년 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
추진내용 | 월별 추진 일정 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 방법
 | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 |  | 9 |  | 10 |  | 11 |  | 12 |  | 
EUV-FEL 용 초전도 cavity 관련 조사 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 문헌 조사 및 전문가 자문
주요 이론 검증 및 시뮬레이션 재현 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 논문 연구 및 EM 시뮬레이션 tool 활용
Cavity 기본 형상 설계 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | EM 시뮬레이션 tool 및 최적화 기법 활용
HOM 커플러 물리 설계 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | EM 시뮬레이션 tool 및 최적화 기법 활용
FPC 물리 설계 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | EM 시뮬레이션 tool 및 최적화 기법 활용
설계 개선 및 최적화, 보고서 작성 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 전체 가속기 개념 설계 과제 및 업체와 협업

## Slide 31: Research Plan
Repeat of simulation of previous papers by CST(in progress)
Verification of field distribution of the FM and shunt impedance of HOM mode
- Xinghao Guo et al., RF design and optimization of a 1.3 GHz 7-cell high-current superconducing cavity, JINST (2025).
- Taro Konomi et al., Damped superconducing structure for EUV light source based on energy recovery linac, PRAB (2023).
Guo et al., JINST(2025)

## Slide 32: (Optional) Very High Frequency(VHF) Photogun
Very high frequency(VHF) gun operates at frequency lower than 300MHz
Lower gradient, but capable of stable CW operation
In operation/planned to apply in UED
Siddiqui et al., Struct. Dyn. (2023)

## Slide 33: (Optional) Very High Frequency(VHF) Photogun
VHF photogun is considered as an option for photogun in ERL, including EUV-ERL in china
Higher beam energy than using DC photogun
- reduced impact of space-charge forces
Currently stably operate at only low beam current(1mA) at ~1MHz
Zheng et al., PRAB(2023)

## Slide 34: Measurement of Pulse Length of Laser
Autocorrelation
Frequency-resolved optical gating(FROG)
Spectral interferometry

## Slide 35: Autocorrelation
Autocorrelation with second harmonic generation(SHG)
SHG
crystal
Pulse to be measured
Variable delay, t
Detector
Beam
splitter
E(t)
E(t–t)
Esig(t,t)

## Slide 36: Autocorrelation
Pulse
Autocorrelation
t
t

## Slide 37: Autocorrelation
Pulse
Autocorrelation
t
t

## Slide 38: Autocorrelation
Simple setup
Limited resolution(~30fs)
Not available for UV(<300nm) measurement due to limit of SHG of β-BBO crystal
Phase matching is required
The measurement result is always symmetric
→unable to figure out complicated shape pulse

## Slide 39: Autocorrelation
Two photon absorption(TPA): simultaneous absorption of two photons to excite an atom or molecule (e.g. semiconductor of photodiode)
are one/two photon absorption coefficient)
Photon energy should be higher than half of the bandgap

## Slide 40: Autocorrelation
TPA autocorrelation measures the transmission after TPA
-
-
Commonly used for UV autocorrelation
- diamond photodiode is used as a material
High background signal

## Slide 41: Autocorrelation
Optical Kerr effect: change in the refractive index of a material in response to intensity of light
- n=n0+n2I
When the response time is short, then the signal is
Transmittance:
(for small value of phase lag )
Low intensity:
High intensity:
Large n2
Large n2
Large n2

## Slide 42: Autocorrelation
Kerr gate autocorrelation
Pump and probe beam usually has different wavelength
Since Kerr effect is third order effect, relationship between width of AC and pulse is different
(e.g. factor of 1.29 for sech2)
Low background signal

## Slide 43: Autocorrelation
Experiment: measurement of pulse length of UV(266nm) laser
Requirement of material
- polarization independent(isotropic or amorphous)
- fast response time
- not too low signal

## Slide 44: Autocorrelation
Candidate for material for Kerr lens: fused silica
- fast response time
- low transmittance

## Slide 45: Autocorrelation
Material for TPA autocorrelation: Glass or Ge-doped fused silica
- high TPA coefficient at UV

## Slide 46: Appendix - Phase matching
If ksig ≠ kpol:
If ksig = kpol:
Generated light is in phase with previously generated light.
Generated light is out of phase with previously generated light.
NLO medium
NLO medium
z
Coherent destructive interference
Coherent destructive interference

## Slide 47: Appendix - Phase matching of SHG
But:
So the phase-matching condition becomes:
z
x
y
y
SHG crystal
w
2w
w
This condition restricts the allowable beam angles and crystals because n(w) tends to be less than n(2w) to begin with, and cos(q) only reduces it further. The birefringence must be large for this to work.