## Slide 1
2026-04-24, Pohang, South Korea
2026 JKPS(Journal Klub of Pohang Scientist)
(과학관, JKPS)
DAON LEE

## Slide 2
Outline
Ⅰ. Introduction
Ⅱ. Transient Beam Loading
Ⅲ. Simulation
Ⅵ. Compensation
Ⅴ. Summary
Ⅵ. Follow-up Study

## Slide 3
Introduction
3
● Bunch lengthening is effective to achieve mitigation of the intra-beam scattering(IBS) and sufficient Touschek lifetime.
Transient Beam Loading(TBL) effect in the ultra-low emittance ring
● The TBL affects the performance of the bunch lengthening.
● They estimated the TBL effect using a semi-analytical method with compensation.

## Slide 4
Beam Loading
4
Beam loading
• The Beam Loading :
- When a beam passes through an RF cavity, it excites the electromagnetic fields inside the cavity, much like a klystron or other RF source does. This excitation of the cavity by the beam is referred to as beam loading.

## Slide 5
Equivalent Circuit
5
Energy conservation / Superposition principle
in Fermilab
Very high in SC cavity
-> crucial beam loading effect

## Slide 6
Transient Beam Loading
6
Transient beam loading / from transient to steady-state
• The Transient Beam Loading :
- Due to bunch spacing, cavity filling time, detuning, and loaded Q, the cavity voltage seen by each bunch can vary.

## Slide 7
Double RF System
7
Five main RF cavity & five passive harmonic cavity(PHC)
• The TM020-mode cavity(PHC) :
- TM020 mode is advantageous for harmonic cavities because its low reduces transient beam loading, and its magnetic field node enables compact HOM(Higher-Order Mode) damping, thereby preserving bunch-lengthening performance.

## Slide 8
Double RF System
8
Five main RF cavity & five passive harmonic cavity(PHC)
• Operation :
- If the main RF slope is canceled by a third-harmonic cavity to achieve bunch lengthening, the longitudinal focusing force around the synchronous phase becomes very weak or nearly vanishes. As a result, even small fluctuations in the harmonic cavity voltage caused by bunch gaps can lead to significant changes in both the bunch position and the bunch length.

## Slide 9
Simulation
9
1. Tracking simulation
• Tracking simulation : (1,000 macro-particles per bunch/total 10e+6 macros)
- These simulations demonstrated that the TM020-mode cavities are very effective for lengthening bunches when the bunch gaps are introduced.

## Slide 10
Simulation
10
Evaluation of bunch lengthening : 2. Semi-analytical calculation simulation
• Semi-analytical calculation simulation :
- This approach also allows us to estimate the bunch lengths quickly while the tracking simulation takes a long time.

## Slide 11
Simulation
11
Estimation of the transient rf voltage
• The voltage fluctuation :
- By applying the semi-analytical method, they estimated the voltage fluctuations due to bunch gaps in various harmonic cavities.

## Slide 12
Compensation
12
The feed-forward Low-level rf(LLRF) compensation
• The feed-forward LLRF compensation :
- The half bandwidth of the compensation was chosen to be 1.1 MHz, which was approximately the same as the repetition frequency of the bunch trains.
①
②
③

## Slide 13
⒝ Feed-forward 2.1MHz :
- we need to determine the bandwidth considering the required power and the performance.
Compensation
13
The feed-forward LLRF compensation on Main & Harmonic cavities
-> All well good
⒜ Feed-forward 1.1MHz :

## Slide 14
Compensation
14
The feed-forward LLRF compensation on separate rf cavities
• Feed-forward 3.MHz :
- The cavity voltage required for this compensation was ∼45 kV, while the peak generator power was ∼50 kW. Both of them are technically feasible.

## Slide 15
Discussion
15
The superconducting cavities
• Two KEKB-type SC cavities :
- With these cavities, the voltage fluctuation was estimated to be 0.4% p-p.
-

## Slide 16
Summary
16
• For next-generation light sources, we investigated the transient beam loading effect, which affects bunch lengthening, using semi-analytical simulations.
• They proposed a normal-conducting double RF system based on a 1.5 GHz TM020-mode harmonic cavity with feed-forward LLRF compensation using a separate RF cavity, and the simulation results demonstrated improved performance.

## Slide 17
17
Follow-up Study

## Slide 18
18
Follow-up Study
•
•
With = −52.5°, variation in the bunch phase was mitigated from ±1.5° to ±0.4°
RMS of bunch phase within
40 and 150 buckets

## Slide 19
Thank you !

## Slide 20
Appendix A
20
Robinson instability criteria
The Robinson instability is a longitudinal coupled-bunch instability driven by the interaction of the beam with the impedance of accelerating cavities
• In low intensity : (beam loading voltage의 perturbation을 무시 가능한 경우)
(rf voltage phasor 가 거의 변하지 않음)
- 이 경우 보통의 phase stability condition으로 돌아감.
• In high intensity :
- beam loading voltage phasor가 추가로 생겨 원래의 rf voltage가 섭동. 이때 안정되지 위해서는 추가 가속성분이 restoring force를 깨지 않아야함.
• Robinson’s damping :
- below transition에서, (왼쪽 그림 : )
1. 인 번치는 가 더 커짐
2. bunch 가 높은 임피던스를 보게 됨
3. 인 입자들보다 더 많은 에너지를 잃게 됨
4. 번치의 coherent synchrotron oscillation 감소.
Robinson instability는 번치의 주파수 변동이 어느쪽 slope에 걸리느냐로 결정