## Slide 1: Lab meeting
2026. 05. 08 –
나창선

## Slide 2: Background – Image charge
Forck et al., Beam Position Monitors.

## Slide 3: Background – Impedance Matching, Reconstruction
wikipedia:Impedance_matching
Mismatched case
Matched case
Impedance matching
Minimize reflection and waveform distortion
Impedance matching
The pick-up signal is transmitted through a coaxial line.
Impedance mismatch causes signal reflection.
Reflected signals can produce ringing and waveform distortion.
Match the characteristic impedance of the pick-up structure.
Reconstruction algorithm
Low-β beams have longitudinal electric-field spread.
The measured signal can be broader than the original bunch shape.
Reconstruction is required to recover the bunch profile.
Forck et al., Beam Position Monitors.

## Slide 4: Impedance Matching
Signal Transmission Structure of CPU-BSM
Main signal path: Pick-up ring → coaxial line → oscilloscope
Coaxial line: conventional coaxial geometry
Pick-up ring: curved microstrip-like structure
RF design house

## Slide 5: Reference vs Basic
Reference
Basic
Distribution | Gaussian
 | 0.1, 0.2, 0.3
Distribution | Gaussian
 | 0.1, 0.2, 0.3
Basic model includes: - pick-up ring - coaxial line - cavity
Matching structures were not included in the basic model.
The basic model was compared with the reference response.

## Slide 6: 30 mm vs 60 mm
D=30 mm
D=60 mm
w | 12.6 mm
t | 3 mm
h | 10 mm
Distribution | Gaussian
 | 0.1, 0.2, 0.3
Distribution | Gaussian
 | 0.1, 0.2, 0.3
As the aperture increased, the distance between the beam and pick-up ring increased.
The current signal amplitude decreased for the larger aperture.
The normalized waveform became slightly broader.

## Slide 7: Impedance Matching - Beam Guard
Beam guard is required to protect the pick-up ring from direct beam loss.
With beam guard, the pick-up ring is no longer a simple microstrip geometry.
Standard microstrip formulas are not directly applicable.

## Slide 8: Impedance Matching – Aperture
Straight
Aperture Effect on Characteristic Impedance
The pick-up ring is a curved microstrip-like structure.
Larger aperture  different curvature
In a curved ring, the inner and outer edges have different path lengths.
Characteristic impedance changes with aperture

## Slide 9: Summary
In the basic model, only the pick-up ring, coaxial line, and cavity were included. → Without matching structures, ringing was observed.
As the aperture increased:
  Current intensity decreased.
  The normalized signal became broader.
Beam guard was added for pick-up ring protection, and characteristic impedance optimization was performed.
In the curved pick-up ring simulation, characteristic impedance changed with aperture. → Straight microstrip estimation should be corrected by aperture-dependent CST simulation.

## Slide 10: Future Work
Impedance Matching
  Design pick-up ring and coax matching structure
  Perform full assembly simulation
Reconstruction Algorithm
  Apply reconstruction algorithm to large-aperture CPU-BSM
  Evaluate applicability to proton accelerator.
Tomography

## Slide 11: Appendix

## Slide 12: Reference vs basic vs beamguard
Basic v1
Beamguard v1
Reference
w | 12.6 mm
t | 2
h | 11
h_wall | 15
gap | 12.7
Distribution | Gaussian
 | 0.1, 0.2, 0.3
Distribution | Gaussian
 | 0.1, 0.2, 0.3

## Slide 13: v1(w=12.645,h=10) 과 비교 v2(D=70mm,w=15,h=11.5)
Sigma_t = 0.2 ns
Beta = 0.2
Sigma_t = 0.1 ns
Beta = 0.3
Pick-up ring의 폭을 늘리고 임피던스 매칭을 진행함.
Current의 Intensity가 증가했음.

## Slide 14: Appendix - Parameter
전체
정면
상단
측면
coax_in
coax_out
t
w
h
ring_in
ring_out
pipe_in

## Slide 15: Appendix - Parameter
h
w
gap
t
h_wall
t_wall

## Slide 16
Analytical estimate: 100.151 Ω
CST simulation: 111.546 Ω