## Slide 1: Group Meeting 260522
Minseo Jeong

## Slide 2: UED Experiment & Laser Cross-correlation experiment
Solenoid align(completed)
UV laser align (in progress)
Purchase for laser cross correlation experiment (arrival in July)

## Slide 3: SRF Cavity for EUV-ERL

## Slide 4: Research Plan
2026년 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
추진내용 | 월별 추진 일정 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 방법
 | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 |  | 9 |  | 10 |  | 11 |  | 12 |  | 
EUV-FEL 용 초전도 cavity 관련 조사 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 문헌 조사 및 전문가 자문
주요 이론 검증 및 시뮬레이션 재현 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 논문 연구 및 EM 시뮬레이션 tool 활용
Cavity 기본 형상 설계 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | EM 시뮬레이션 tool 및 최적화 기법 활용
HOM 커플러 물리 설계 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | EM 시뮬레이션 tool 및 최적화 기법 활용
FPC 물리 설계 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | EM 시뮬레이션 tool 및 최적화 기법 활용
설계 개선 및 최적화, 보고서 작성 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 전체 가속기 개념 설계 과제 및 업체와 협업

## Slide 5: SRF Cavity in EUV-ERL(KEK)
Based on TESLA 1.3GHz cavity
Cavity Parameters | KEK-EUV | TESLA
Frequency (MHz) | 1300 | 1300
R/Q (Ω) | 1009 | 1020
Ep/Eacc | 2.0 | 2.06
Hp/Eacc (mT/(MV/m)) | 4.23 | 4.26
TESLA Center Cell
End Cell A
End Cell B
HOM Damper
HOM
Φ100 mm BP
Φ110 mm BP

## Slide 6: SRF Cavity in EUV-ERL(China)
7-cell cavity based on cavity in TESLA 1.3GHz cavity
Cavity Parameters | KEK-EUV | TESLA
Frequency (MHz) | 1300 | 1300
R/Q (Ω) | 784.8 | 790
Ep/Eacc | 2.03 | 2.16
Hp/Eacc (mT/(MV/m)) | 4.23 | 4.27

## Slide 7: SRF Cavity in EUV-ERL(China)

## Slide 8: SRF Cavity in EUV-ERL(China)

## Slide 9: SRF Cavity in EUV-ERL(China)
7-cell cavity based on cavity in TESLA 1.3GHz cavity
X. Guo, J. Instrum. (2025)
Field flatness : 98.04%
Field flatness : 98.33%

## Slide 10: Higher Order Mode Damping
Calculation of external Q factor of HOM is required

## Slide 11: Fundamental Power Coupler
Goal: setting external quality factor by
Position, injection length, and tip geometry of antenna should be optimized
X. Guo, J. Instrum. (2025)

## Slide 12: Fundamental Mode Coupler
Using single coupler can break symmetry
- compensation stub should be introduced on the opposite side of the main couple

## Slide 13: Multipacting
Multipacting : an electron multiplication based on resonance breakdown phenomenon inside RF cavity
- drain the energy stored in the cavity
For elliptical cell, MP occurs usually in equator region

## Slide 14: Multipacting Simulation (TESLA center cell)
Primary emission energy: 3eV
Emission angle: 45°
X. Guo, J. Instrum. (2025)

## Slide 15: Dual axis cavity
Allows energy recovery of parallel beams, accelerating/decelerating along different axes
It can shorten length of linac

## Slide 16: Research Plan
Design of cavity
- minimization of Epk/Eacc and Bpk/Eacc, maximization of flatness of field, and lower HOM impedance
- by optimization algorithm(MOGA, MOBO)