## Slide 1: SLS-IPAC Organize
Young Min Park
Division of Advanced Nuclear Engineering (DANE), POSTECH
2026-05-29, Pohang, South Korea

## Slide 2: Schedule
2
SLS-II (2026-05-02 ~ 2026-05-14)
  Machine study at SLS-II
  ADTS measurement with low chromaticity (Mon.)
  Apple-X ID characterization (Tue.)
  Round beam and dissonance injection (Thu/Sun.)
  RF noise level measurement (Mon/Thu.)
  SLS-II Ring tour (Wed.)
  Bunch length with HHC measurement (Thu.)
  Booster emittance exchange (Fri.)
CERN (2026-05-14)
  CERN Tour
  SC(Synchronous Cyclotron)
  ATLAS (A Toroidal LHC ApparatuS)
  Control room (PS,SPS,LHC)
  LEIR (Low Energy Ion Ring)
ESRF-EBS (2026-05-15)
  ESRF Tour
  Control room & Injection
  Ring tour
IPAC (2026-05-15 ~ 2026-05-22)

## Slide 3: SLS Tour
3
SSA generate 150 kW/500 MHz rf for storage ring main cavity.
Much stable than general Klystron & modulator.
The SSA is built from many individual amplifier modules, almost like a “Christmas tree”.
One advantage of this modular design is that a faulty module can be hot-swapped and replaced individually.
SSA
SSA

## Slide 4: SLS Tour
4
Simple FODO cell/ 160 ms ramp/ 3 Hz injection
Bending ramp = Quad ramp = Sextupole ramp (Same mps)
Additional Quad/Sext to match tune/chromaticity
Bend with trimmed
Quad/Sext
Booster Ring
Extraction septum

## Slide 5: SLS Tour
5
BRTL (Booster to Ring Transfer Line)
Screen monitor : Uses for measurements
Closed horizontal dispersion
Injected by 3-mm thick septum from booster to SR
Emittance measurement
Without and with emittance exchange (EE)
Energy spread measurement
Dispersion at SCRM-2 = 1.2 m
Measured
Quad scan to measure emittance

## Slide 6: SLS Tour
6
Ring injection
Thick septum : 2-Permanant magnet / Center electromagnet (3 mm width)
Thin septum : In vacuum septum magnet with 1 mm width
Injection scheme : 4-kicker bump alter to longitudinal injection (plan)
Quad near septum Make large beta function () to increase DA a factor of 2.
1mm thin septum
3mm thick septum

## Slide 7: SLS Tour
7
2 T superbend magnet in operation
Purple: combined-function magnets (dipole + quadrupole)
Blue center magnet: pure dipole
LGB applied → maximum magnetic field at the center
A superconducting superbend magnet with a field of up to 5 T is currently under testing.
It is planned to replace the existing 2 T superbend magnet after the test campaign.
Superbend magnet (Current)
(Plan to install - Superconducting)

## Slide 8: SLS Tour
8
Bunch by Bunch Feedback
Transverse kicker :
Longitudinal kicker :
In real commissioning No CBI are observed until 400 mA operation
Transverse kickers
Longitudinal kickers

## Slide 9: SLS Tour
9
Harmonic Cavity
Main cavity : (Connected by SSA)
Super – 3HC : (Pick-up to get cavity voltage)
Main HOM-damped cavity
Super – 3HC

## Slide 10: SLS Tour
10
Harmonic Cavity Tuner
Parameter | Value
Tuning range | 
Tuning resolution | 
Parameter | Value

## Slide 11: SLS Tour
11
Others
Undulators
Booster cavity
Diagnostic beamline

## Slide 12: Bunch lengthening with HHC
12
Measure bunch lengthening with various current
Date) 2026-05-08 10:00 – 16:00
Goal : Measure the bunch length with various current and transient effects
Participant : Jonas Kallestrup, Lukas Stingelin, Alessandro Citterio, Junha Kim, Youngmin Park
Measurement method: streak camera Bunch length and transient effects BPM and RF modulation coherent synchrotron frequency
Main steps:
  Single bunch scan with 0.07, 0.5, 2 mA
  Find initial setup with 50 filled + 0.1 mA bunch train
  High current scan with 450 filled + 30 gap bunch train at [100,200,300,350,400] mA
Cavity setteing
  Main cavity :
  Higher harmonic cavity: (Optimal for 400 mA operation)

## Slide 13: Bunch lengthening with HHC
13
Single bunch scan
Control pulse delay to find 0th bunch position
Filling pattern monitor
Streak camera (Unit )
Current | Bunch length
Current | Bunch length
Theorical value = 8.97 ps
Bunch length increased with single-bunch current.
This effect is likely due to potential-well distortion induced by wake field, rather than HHC bunch lengthening.

## Slide 14: Bunch lengthening with HHC
Bunch length
Transient
For the 50-filled-bucket case, the single-bunch current was about 0.1 mA.
Bunch-by-bunch measurements were performed every 8 buckets.
The measured bunch length was approximately 9.4 ps, similar to the 0.07 mA single-bunch case.
This indicates that the total current of 5 mA was too low to produce a noticeable HHC-induced bunch lengthening.
14
50 Filled bunch measure(Total 5 mA)
0th
1st
Change delay
2nd

## Slide 15: Bunch lengthening with HHC
15
Coherent frequency measurement (50 filled bunch mode – 5 mA)
Main RF voltage and phase modulations were applied to excite the beam response. The beam response was monitored in the horizontal plane using BPM signals. Then large FFT amplitude was interpreted as a resonant oscillation response.
The modulation amplitudes were selected below the LLRF interlock limits:
Interlock limits:
Applied modulation gains:
= 2e-4, = 5e-4
The modulation frequency was swept from 0.5 kHz to 5 kHz, and he scan was performed separately for RF voltage and RF phase modulation.
Theory value =

## Slide 16: Bunch lengthening with HHC
At 350 mA, the expected bunch length was about 18–20 ps.
However, the measured bunch length was significantly longer and became comparable to the 400 mA case.
This additional lengthening is likely due to potential-well distortion, since the single-bunch current is about 0.78 mA.
At 400 mA, the operating point was close to the flat-potential condition.
A strong transient effect was observed along the bunch train under this condition.
16
High current scan with 450 filled + 30 gap bunch train at [100,200,300,350,400] mA
Some error

## Slide 17: Bunch lengthening with HHC
17
Compare with theory
The measured bunch lengths were slightly longer than the theoretical prediction.
However, the overall transient trend was reproduced reasonably well.
In particular, the similar bunch length level observed at 350–400 mA was also consistent with the theoretical tendency.
The systematic increase in the measured bunch length is likely due to additional potential-well distortion.
As discussed earlier, the single-bunch current is already high enough to induce wake-field-driven bunch lengthening.

## Slide 18: Bunch lengthening with HHC
18
Compare with theory
The measured centroid transient showed a similar trend to the theoretical prediction.
The transient amplitude was also comparable between measurement and theory.
At 400 mA, the measured centroid shift was about 160 ps, and he theoretical result showed about 150 ps
At 350 mA, the measured centroid shift was about 85 ps and the theoretical result showed about 75 ps
The measured centroid transient is reasonably consistent with the theoretical prediction.

## Slide 19: Bunch lengthening with HHC
19
6th order Characteristic equation & Measurement of synchrotron frequency
HHC Voltage (kV)
Current (mA)
6th-order characteristic function including main cavity and HHC impedances
HHC voltage calculated self-consistently at each beam current
Good overall agreement with measured vlaues
Small frequency deviation appears at low current, but similar values are reproduced

## Slide 20: Booster Emittance Exchange
20
Booster emittance exchange optimization
Date) 2026-05-08 16:00 – 21:00
Goal : Decrease , Optimize timing of coupling
Participant : Jonas Kallestrup, Junha Kim, Youngmin Park
Changed knob :
Ramp-down starting point
QF current min/max
Each step : 88 turn (79.2 )
Total step : 4000 ()
Initial / reduced by .
Extraction timing scan (change extraction kicker delay) Set the reference extraction timing at the minimum point.
QF ramp-down timing scan Shift the ramp-down start point to optimize the resonance-crossing timing. (But no feasible improvements)
Extraction timing scan Change value away from the coupling points Some Issue occurs
Coupling minimized
Extraction
Exchange occurs due to ramp-down
Emittance recover due to radiation properties

## Slide 21: Booster Emittance Exchange
21
Booster emittance exchange optimization
Date) 2025-05-08 17:00 – 21:00
Beam loss by septum
Beam loss occurred at several QF settings clipped beam profiles suggested possible septum/aperture scraping.
The likely cause was a change in the extraction optics due to the tune shift induced by the QF variation.
Extraction kicker and BRTL quadrupoles were adjusted to recover beam centering and injection.
Stable injection was not recovered, and the experiment was stopped.

## Slide 22: CERN Tour
22
Date) 2026-05-14 11:00 – 18:00
SynchroCyclotron(SC)
Operate 1957 – 1990’s, 600 MeV circular accelerator
After 1964: SC mainly used for nuclear physics due to PS (Proton Synchrotron)

## Slide 23: CERN Tour
23
Date) 2026-05-14 11:00 – 18:00
ATLAS (A Toroidal LHC ApparatuS)
Purpose
Study particles produced in high-energy proton–proton collisions
Test the Standard Model and search for new physics
Structure
Large cylindrical detector surrounding the collision point
Built with several layers, each measuring different particle properties
Detectors
Inner Detector: tracks charged particles
Calorimeters: measure particle energy
Muon Spectrometer: detects muons
Magnets: bend charged particles to measure momentum
Achievements
Played a key role in the Higgs boson discovery in 2012
Continues precision measurements and searches for new particles

## Slide 24: CERN Tour
24
Date) 2026-05-14 11:00 – 18:00
CERN control room
Central control room for CERN’s accelerator complex
Organized into four main operation panels:
  PS and injector chain
  SPS
  LHC
  Cryogenic system
Operators monitor and control beam operation, machine status, and cryogenic conditions from this room

## Slide 25: CERN Tour
25
Date) 2026-05-14 11:00 – 18:00
LEIR (Low Energy Ion Ring)
Accumulates low-energy ion beams from Linac 3
Converts long ion pulses into short, dense bunches
Accelerates the ions before transfer to the PS
Used as part of the ion injector chain:
Linac 3 → LEIR → PS → SPS → LHC
Operation history
Converted from the LEAR (Low Energy Antiproton Ring)
LEAR operation ended in 1996
First beam observed in October 2005
Injection
Extraction

## Slide 26: IPAC SSMB
26
Date) 2026-05-15 ~ 2026-05-22
Dr. Deng !!

## Slide 27: IPAC SSMB
27
Date) 2026-05-15 ~ 2026-05-22
Longitudinal Weak Focusing
Longitudinal Strong Focusing
Don’t need Isochronous condition!!

## Slide 28: Thank you for your attention!
28

## Slide 29: 6th Order characteristic equation
29
Beam-cavity coupled motion
Main cav
HHC