## Slide 1: Europe business trip (PSI, CERN, ESRF, IPAC26)
2026-05-29
Junha Kim

## Slide 2: Paul Scherrer Institute
SLS2.0
Swiss Spallation Neutron Source
SwissFEL
Paul Scherrer Institute (PSI)
취리히 공항에서 기차로 약 1시간 20분 떨어진 곳에 위치
강을 기준으로 동편과 서편으로 나뉨
동편 : SwissFEL, 식당, Visitor center ...
서편 : SLS2.0, SINQ, Guesthouse...
Control room 건물은 SLS2.0 옆 건물, 3개의 가속기를 한 곳에서 운전함

## Slide 3: Control panel
Current
Injection Efficiency
Lifetime
Vacuum level
Bucket status
Current
Lifetime
Injection rate mA/min
Transition rate BR to SR
BEAM LOSS
Vacuum Level
Tune
(Qx,Qy)
Bucket status
Beam profile monitor (Beam diagnostics beamline 1)
Beam disgnostics beamline2

## Slide 4: ADTS measurement
Machine study : Jesus , Junha, Young-min (MAY 4th, 20:00 ~ 24:00)
Experiment method
Beam bump : 400mA -> 0 mA
Injection to 20mA, bucket : 20/450
Initial tune : (Qx, Qy) = (0.352, 0.21) ; Lifetime : 3.3 hours
Tune setting change to nominal working point : (Qx, Qy) = (0.37, 0.22) ; Lifetime : 6.0 hours
5) Chromaticity correction to (0, 0) – using 9 sextupole families
  () = (0.96, 1.32) -> (0.1769, 0.2175)
6) Measurement ADTS :
  Varying Kicker strength in 8 steps (Hor, Ver), measured x, y (60 turns)
  Measure tune based on x,y (NAFF)
  Calculate Jx, Jy : , ,

## Slide 5: ADTS measurement
Chromaticity measurement & setting tool
Result of Jx along the ring
Result of Jy along the ring
Summary of the result :
has fluctuation along the ring, but is stable
As increase kicker strength, the results has more unstable.
One possible reason of Jx are BPM noise.

## Slide 6: 2nd order chromaticity measurement
Motivation : we want to know function of
Varying octupole strength (5 families / 8 families)
  OCX1, OCY1, OCX2, OCY2, OCXm, OXX, OXY, OYY
  Because of OXX, OXY, OYY placed at dispersion free region, there are no change if varied these strength
  직접 EPICS로 octupole strength 값 변경, 5 step
Measure chromaticity varying (-350 kHz ~ 350 kHz)
  in 9 steps , 2 samples each step
  fitting 3rd order polynomial
  Getting the coefficient.
Jesus’s IPAC26 proceeding

## Slide 7: 2nd order chromaticity measurement
Experiment method
Stored a 20 mA beam with 20/450 bunch buckets filled.
Varied the octupole magnet strength
Scanned from -350Hz ~ 350Hz in 9 steps, corresponding to
Tune measurement at each steps
3rd order polynomial fitting
6) Repeat 1~5 across 5 octupole families

## Slide 8: 2nd order chromaticity measurement
Results :

## Slide 9: Effect of ID gap on tune measurements
Machine study : Simona Bettoni, Jonas, Junha, Young-min (May 5th)
Installation & Setup: 2nd APPLE-X ID is installed in April
Goal : Identify the dominant field components affecting the beam within the ID.
Beam Conditions: 30 mA / 450 bunches
Operating Modes: Three polarization modes (LH, LV, and Circular)
Gap Settings: Measurements performed for open (30.5 mm) and closed (11.5 mm) gaps in each mode
Tune Shifts: Measured as a function of horizontal ID displacement from

## Slide 10: Effect of ID gap on tune measurements
Calculate sextupole strength and octupole strength by polynomial fitting

## Slide 11: Effect of ID gap on tune measurements
2025-12 of 1st APPLE-X ID
2026-05-05 FOFB 25kHz of 2nd APPLE-X ID
2026-05-05 FOFB 10Hz of 2nd APPLE-X ID
Summary of the result :
Measured tune has different shape on vertical side compared with 1st APPLE-X ID
Guessing 2nd Apple-X ID has misalignment or broken?

## Slide 12
Machine Study Log
Data Acquisition : Fast orbit horizontal position (74.36kHz) , Turn-by-Turn (8000 turn)
MAY 5th
  Conditions : 400 mA, top-up injection, SOFB on, FOFB on
  Instrumentation : 115 synchronized BPMs
  Measurement scale1 : 8k turn data for each 115 BPMs, measured 5 times
  Fast orbit mode : 8000 samples acquired with 74.36kHz; Correspond to approximately on sample every 14 turn, measured 5 time
MAY 8th
  Conditions : 100~400 mA, top-up, SOFB on, FOFB on
  Instrumentation : 115 synchronized BPMs
  Measurement scale1 : 8k turn data for each 115 BPMs, measured 5 times
  Fast orbit mode : 8000 samples acquired with 74.36kHz; Correspond to approximately on sample every 14 turn, measured 5 time
SLS2.0

## Slide 13
Measurement result of SLS2.0 – Fast orbit mode (74.36kHz)
SLS2.0
RMS energy oscillation is .
Low frequency rf error is dominant.
RMS phase error : 0.0015°
400mA / SOFB, FOFB on

## Slide 14
Measurement result of SLS2.0 – TbT (8000 turns)
SLS2.0
RMS energy oscillation is .
Analysis of low frequency region is limited because of number of turns are small
RMS phase error : 0.044°
400mA / SOFB, FOFB on

## Slide 15
Measurement result of SLS2.0 – Fast orbit mode
SLS2.0
Data | RMS | RMS phase error ()
1 | . | 0.0015
2 | . | 0.0051
3 | . | 0.0016
4 | . | 0.0026
5 | . | 0.0024
Average | . | 0.0026
Data |  | 
1 |  | 0.0015
2 |  | 0.0051
3 |  | 0.0016
4 |  | 0.0026
5 |  | 0.0024
Average |  | 0.0026
From the PSI RF Logbook
Phase noise with LLRF feedback :

## Slide 16
Measurement result of SLS2.0 – average result
12
SLS2.0
Results :
Synchrotron tune decrease from 3HC effect.
Because of limited acquired turn number, TbT mode is not accurate measuring RF noise.
Based on Fast orbit mode (74.36 kHz), RF noise level is 0.0026
Based on PSI RF logbook, RF noise level is 0.0024

## Slide 17: CERN tour
MAY 15th : 11:00 ~ 17:00
CERN Synchrocyclotron(SC) tour
ATLAS tour
Lunch with Frank and Jacqueline
CERN Control Center tour
LEIR tour
SC
ATLAS
LHC Control area
LEIR

## Slide 18: ESRF tour
MAY 15th : 9:30 ~ 14:00
Beam status of ESRF-EBS
Beam Injection
Outside of the Tunnel

## Slide 19: ESRF tour
MAY 15th : 9:30 ~ 14:00
SSA for ESRF Main cavity
Vacuum chamber of ESRF
Nonlinear Kicker
4 Kicker current monitor
When we visited, ESRF is operating for user.
We can tour the outside of the Tunnel

## Slide 20
IPAC26
IPAC26’ : MAY 17th ~ 22th
SOLEIL-II, HEPS, BESSYIII, SLS2.0, MAX4U...
Many institutes present their commissioning progress and plans to upgrade their machines.

## Slide 21
IPAC26
Diamond-II Magnet Crosstalk effect
Diamond-II Booster ramping simulation

## Slide 22: Discussion & Question
Q) What is your tools for control the element?
  Own development tool, Not use MML or python ML. Mocha(?)
Q) How do you generate vertical dispersion for emittance coupling?
  Using skew quad at only arc section, response matrix.
Q) Booster ramping curves?

## Slide 23: Booster Ramping Curves
QF : Horizontal Tune
QD : Vertical Tune
Defocusing Sextupole
Focusing Sextupole
Small gaps for Emittance Exchange
Booster ramping curve: Half-sine
Combined-function magnets (dipole, quadrupole, sextupole) : Half-sine curves
Separate sextupoles: Follow bending curves and correct chromaticity to (1, 1)
Correctors are not considered for the booster.

## Slide 24: Booster Ramping Curves
RF ramping curve is not half-sine curve.
Original RF ramping curve (Blue)
New RF ramping curve (Orange)
SLS2.0 team implement a new booster RF ramp shape for reducing power consumption.
The beam quality seems to be equally good as previous RF ramp.
They found new RF ramping curve just manually

## Slide 25: Discussion & Question
Q) On Booster Interference with Storage ring orbit.
    During the early commissioning stage, 3Hz orbit oscillation was observed in the storage ring.
    Since the booster injection system was also 3Hz, this was identified as crosstalk from the booster injection system.
    After the FOFB in the storage ring, the effect was well suppressed and was not a significant issue.
Q) Vacuum conditioning

## Slide 26: Thank you