## Slide 1
2026-06-12, Pohang, South Korea
Reconstruction from VPP with MENT
& Study of Transient Beam Loading
DAON LEE
2026 The Beam Diagnostics and Dynamics Study
(Room 310)

## Slide 2
Outline
Ⅰ. Tomography
- Overview of the Tomography
- The single-optics based reconstruction
- RMS envelope equation
Ⅱ. Transient Beam Loading
- Overview of the transient beam loading
- Comparison of rms bunch lengths : Theoretical vs. Tracking
Ⅲ. Summary

## Slide 3
Overview of the Tomography
3
KOMAC BTS(Beam Test Stand) implementation in x-suite
Beam parameters
Energy
1 MeV
N total, macro
3,000,000 -> 3e+8 / 300,000 -> 50,000
0.16 [π mm·mrad]
rms bunch length
1.141820 mm
(Δp/p)
0.507123 %
Simulation set-up
Slit width, Slit step(continuous scan)
0.2mm
Distance L
0.11m
Screen resolution
30
Recon. method
Numerical / +Analytic
Framework
X-suite
(slit)
(screen)

## Slide 4
Reconstruction
4
Space-charge / Analytic reconstruction / Coupling
• Phase space distribution
Previous Numerical method
- total time : 3m 33.48s
Analytic method
- total time : 3m 10.99s
TVDs are same.
• Phase space distribution
Coupling factor(t) : 0.25
Analytic method
- total time : 4m 44.12s
0.113
0.128
0.123
0.147
0.129
0.118

## Slide 5
Previous Discussion
5
Single-optics / Space charge & emittance -dominated
1
Multi-optics
2
Space charge-dominated(beamlets)
Single-optics-based reconstruction
rms envelope equation

## Slide 6
Single-optics-based Reconstruction
6
Diagonal scan / Multi-screen scan
• Additional diagonal scan
• Multiple screen distance
RECON.
L1
L2
Progress made, but resolving a coordinate alignment issue(coding) in the iterative density update.
In my view, this is easier than adding mechanical angle scans and simplifies data processing as no coordinate transformation is needed.
fixed
fixed
(slit)
(screen1)
(screen2)
Time-consuming issue
Additional longitudinal space needed

## Slide 7
7
Single-optics
Unknown :
It is possible to solve.
Multi-screen Scan
RECON.
L1
L2

## Slide 8
8
Single-optics
Unknown :
It is possible to solve.
& It does not work at 45 degree.
Diagonal Scan
In diagonal scan

## Slide 9
• RMS Envelope equation(kapchincky-Vladimirsky eq.)
Space-charge ratio comparison
Measurement Distortions
9
Space-charge/emittance
* Generalized perveance
Bunch peak current
Characteristic current
Charge-Neutralization factor
For gaussian bunch:
focusing
space-charge
emittance
Characteristic current:
Classical particle radius:
Supposes ,
– relativistic factor
Emittance dominated:
Space-charge dominated:
1
SC/focusing ratio(at 7th quadrupole; the lowest magnetic field strength)
2
SC/emit. ratio(just before slit, original bunch)
3
SC/emit. ratio(just after slit, beamlets)
Number of particles for bunch
For proton : 1.535e-18m

## Slide 10
3
SC/emit. ratio(just after slit, beamlets)
SC/Emittance-dominated
10
Beamlets
For a center beamlet
1-i) Horizontal
1-ii) Vertical
1) Horizontal Scan
Chosen a center scan
X=0
For a center beamlet
2-i) Horizontal
2-ii) Vertical
2) Vertical Scan
y=0
Chosen a center scan

## Slide 11
Overview of the Transient Beam Loading
11
PLS-Ⅱ
Beam parameters
Energy, Total current
3 GeV, 300 mA
Bunch N, macro
300 / 10,000
5.8/0.058 [nm·rad]
rms bunch length
22 ps
(Δp/p),
0.105 %, 0.0013
Simulation set-up
Circumference
281.82 m
RF frequency
499.9732 MHz
Harmonic number
470
, R/Q
145,000 / 89 Ω
Framework
mbtrack2

## Slide 12
Uniform Fill Pattern
12
Without camshaft bunch
Theoretical rms bunch length
- 14.26ps
Analytic method
- 21.94ps

## Slide 13
Comparison of RMS Bunch Lengths
13
Uniform fill pattern
• The bunch length can be calculated from the energy spread.
The angular frequency of incoherent synchrotron oscillation
Use of the first derivative at for calculation
By beam loading
-> Reduction in bunch length
-> Increased bunch length
Theoretical rms bunch length
- 14.26ps
Analytic method
- 21.94ps

## Slide 14
Uniform Fill Pattern
14
With camshaft bunch

## Slide 15
Summary
15
1) The issue with multi-optics was addressed by introducing single-optics-based reconstruction methods: diagonal scan and multi-screen scan.
2) Based on the RMS envelope equation, the beam after passing through the slit is emittance-dominated, so this is not expected to cause a significant problem for reconstruction in the BTS.
3) For the whole bunch ensemble, large-amplitude particles spread more than expected, making the RMS bunch length larger than the theoretical value

## Slide 16
Thank you !