## Slide 1: Group Meeting 260626
Minseo Jeong

## Slide 2: UED Experiment
Restoration of beamline after blackout
Alignment of irises of UED beamline

## Slide 3: Laser Cross-correlation experiment
Initiation of cross-correlation experiment: end of July
Coding Labview program for experiment

## Slide 4: Design of SRF cavity
Optimization of FM performance
- Maximization of R/Q and field flatness
- Minimization of Epk/Eacc and Bpk/Eacc

## Slide 5: Optimization of Cavity by BO
Input parameter: dimensions of end cell and beam pipe
Constraint: L>A+a, B+b<Req-Ri, AU+aU<LU, BU+bU<Rtube-Ri, a2/b>6, frequency of FM=1300±1MHz

## Slide 6: Optimization of Cavity by BO
Challenge: Typical acquisition function of MOBO is not suitable for equality constraint
Solution: Two-stage acquisition strategy

## Slide 7: Optimization of Cavity by BO
1) Vector acquisition function with constraint
2) Finding Pareto front of vector acquisition function by MOGA
3) Calculation of scalar acquisition function for PF

## Slide 8: Optimization of Cavity by BO

## Slide 9: Current Status
Code for running CST with python(completed)
- Error occurred when running CST macro by python
Coding for constrained BO (in progress)

## Slide 10: Higher Order Mode Damping
When the particle passes through the cavity, higher order mode is excited
The wakefield left behind affects other bunches
- Transverse HOM increases energy spread and power dissipation ()
- Longitudinal HOM deflects beam and causes beam breakup instability(BBU)

## Slide 11: Higher Order Mode Damping
Threshold of BBU:
-
Goal: minimization of
Threshold of depends on
- Calculation of transfer matrix is required

## Slide 12: Research Plan
Optimization of cavity
- coding for constrained MOBO algorithm (by next week)
Completion of Labview code for cross-correlation experiment (by July)
UED simulation with high charge (~100pC)