## Slide 1: Emittance blow-up study via white noise for the Korea Light Source (KLS) storage ring
Junha Kim

## Slide 2
Vertical emittance blow-up methods
 | Excite betatron coupling | White noise | Vertical dispersion bump
 | 53.4 , 15 | 62 , 15 | 62, 15
Pros | Emittance sum is preserved ( = const.) | No coupled dynamics No local vertical dispersion | No coupled dynamics Easy to simulate Little impact on DA and MA
Cons | Complicated coupled dynamics need to be small | Need shaker (or kicker) Emittance sum is increased ( Complicated to simulate: need to add time-varying kicker before assessing BD performance (e.g., DA, MA, RF dump, …) | Vertical dispersion increased locally (~ 5.5 mm at CENT) Degraded beam quality for CENT source Emittance sum is increased ( So far investigation, vertical centroid motion can be increased by worst energy oscillation.
 | Excite betatron coupling | White noise | Vertical dispersion bump
 | 53.4 , 15 | 62 , 15 | 62, 15
Pros |  | No coupled dynamics No local vertical dispersion | No coupled dynamics Easy to simulate Little impact on DA and MA
Cons |  |  | 

## Slide 3
White noise setup
Noise frequency range : )
Tracking setup
Number of turns : 100k
Number of particles : 10k
Using one-turn matrix
Initial beam distribution : matching with lattice
Korea-4GSR emittance blow up simulation setting
Define white noise with a random phase (Amplitude : )
The noise spectrum ranges from 100Hz to 0.1875MHz in increasement of 100Hz
Tracking one-turn matrix tracking with radiation effects

## Slide 4
Vertical emittance vs. turn number
Horizontal emittance vs. turn number
Vertical emittance vs. vertical chromaticty
Simulation results
We aim to set the vertical emittance to around 15pm (25% of the horizontal emittance).
The simulation shows that the vertical emittance dose not increase at low chromaticity.
Hor. Emittance is independent of vertical chromaticity changes and white noise.
Based on right figure, an amplitude range of 0.1 – 0.2 is suitable for generating a 15pm vertical emittance.

## Slide 5
Korea-4GSR emittance blow up simulation settings and results
Define white noise with a random phase and an amplitude of
Noise frequency range : ) to avoid the synchrotron tune.
, = .
Tracking simulation settings are the same as before.
The tracking results are similar to the previous ones, but the horizontal emittance fluctuation over the turns is reduced.

## Slide 6
Korea-4GSR emittance blow up simulation settings and results
Noise frequency range : ) to avoid the synchrotron tune and horizontal tune.
Tracking simulation settings are the same as before.
The vertical emittance increases significantly at an amplitude of 0.2because the PSD is stronger than in the previous two cases
The horizontal emittance fluctuation over turns is not reduced compared with Case 2.

## Slide 7
Korea-4GSR emittance blow up simulation settings and results
Results at middle of ID straight section ( ,Amp = 0.2)
Define white noise with a random phase and an amplitude of
Noise frequency range : )
The rms vertical orbit centroid motion become larger than 10% of beam size at middle of ID straight

## Slide 8
Korea-4GSR emittance blow up simulation settings and results
Results at middle of ID straight section ( ,Amp = 0.2)
Define white noise with a random phase and an amplitude of
Noise frequency range : )
The rms vertical orbit centroid motion become larger than 10% of beam size at middle of ID straight

## Slide 9
Discussion with Jonas

## Slide 10
White noise setup
Noise frequency range : )
, =
Tracking setup
Number of turns : 35k
Number of particles :10k
Using one-turn matrix
Initial beam distribution : matching with lattice
ESRF-EBS emittance blow up simulation settings
To validate our simulation results, we reproduced the ESRF-EBS simulation study following IPAC24 proceeding by N. Carmignani (“Emittance blow-up with a magnetic shaker at different chromaticities”).
The noise spectrum ranges from 100 Hz to 0.1776 MHz in increments of 100 Hz, consistent with the proceeding.
The tracking simulation settings are based on the proceeding paper.
The EBS.mat file from the AT website was used.

## Slide 11
ESRF-EBS emittance blow up simulation results
We aim to achieve a vertical emittance blow-up similar to the values in the proceeding paper.
Consistent Trends:
  Vertical emittance dose not increase at low chromaticity
  Horizontal emittance remains independent of vertical chromaticity changes and white noise
Discrepancy in Amplitude:
  Proceeding : 4 – 6 required to generate 2-18 pm vertical emittance.
  Our simulation : Only 0.1 – 0.3 is required to achieve the same emittance level

## Slide 12
ESRF-EBS emittance blow up simulation results
Our simulation result
The proceeding result
The eurizon report result
Comparison of required amplitude strengths to achieve a vertical emittance of 0 – 18 pm.
Our simulation : 0.1 – 0.3 is required
IPAC proceeding : 4 – 6 is required
  ~30 times larger than our results
Eurizon report : 0.04 – 0.06 is required
  3 to 4 times smaller than our results

## Slide 13
Summary
The vertical emittance blow up with white noise is studied for the Korea-4GSR storage ring.
Optimal parameter settings identified so far :
  (Step size : 100Hz) to reduce horizontal emittance fluctuations
  Required shaker amplitude : 0.1 ~ 0.2 .
  Vertical chromaticity : is effective to achieve the target 15pm vertical emittance.
However, the vertical beam orbit stability become larger than 10% of beam size.

## Slide 14: Thank you

## Slide 15
Vertical emittance vs. turn number
Horizontal emittance vs. turn number
Vertical emittance vs. vertical chrom

## Slide 16
Results at middle of ID straight section
Results at middle of High beta straight sectioin

## Slide 17
White noise setup
Noise frequency range : )
, =
Tracking setup
Number of turns : 35k
Number of particles :10k
Using one-turn matrix
Initial beam distribution : matching with lattice
ESRF-EBS emittance blow up simulation settings
To validate our simulation results, we reproduced the ESRF-EBS simulation study following IPAC24 proceeding by N. Carmignani (“Emittance blow-up with a magnetic shaker at different chromaticities”).
The noise spectrum ranges from 100 Hz to 0.1776 MHz in increments of 100 Hz, consistent with the proceeding.
The tracking simulation settings are based on the proceeding paper.
The EBS.mat file from the AT website was used.

## Slide 18
ESRF-EBS emittance blow up simulation results
We aim to achieve a vertical emittance blow-up similar to the values in the proceeding paper.
Consistent Trends:
  Vertical emittance dose not increase at low chromaticity
  Horizontal emittance remains independent of vertical chromaticity changes and white noise
Discrepancy in Amplitude:
  Proceeding : 4 – 6 required to generate 2-18 pm vertical emittance.
  Our simulation : Only 0.1 – 0.3 is required to achieve the same emittance level

## Slide 19
ESRF-EBS emittance blow up simulation results
Our simulation result
The proceeding result
The eurizon report result
Comparison of required amplitude strengths to achieve a vertical emittance of 0 – 18 pm.
Our simulation : 0.1 – 0.3 is required
IPAC proceeding : 4 – 6 is required
  ~30 times larger than our results
Eurizon report : 0.04 – 0.06 is required
  3 to 4 times smaller than our results