## Slide 1
Status Report
July 24, 2026
CONTACT
Department of Physics
4th Natural Science Building 108
https://physics.unist.ac.kr/
Soyeon Kim

## Slide 2
Contents
2
Active energy compression
Injection into PLS-II storage ring
Future plans

## Slide 3
3
Active energy compression

## Slide 4
Active energy compression of a laser-plasma electron beam
4
After LPA
Nominal energy : 257 MeV
Charge : 41 pC
Energy spread : 1.8%
Energy jitter : 3.5%
Bunch length : 2
Peak current: 2.5 kA
(b) After chicane (
Nominal energy : 257 MeV
Bunch length : 1
(c) RF cavity parameter
S-band cavity (2.998 GHz), 5-m long structure
Klystron generates 20 MV peak RF power
RF pulse is compressed by a SLED cavity -> Final RF power: 80 MV
Used RF Voltage: 45.4 MV

## Slide 5
Active energy compression of a laser-plasma electron beam
5
Phase Scan & Change of Energy Spread
Phase scan between electron bunch and RF fields in step of
Averaging 50 shots each.
Energy spread : 1.8 % -> 0.097%
Theoretical value
After Decompression Chicane
After RF cavity
Optimal phase/voltage of cavity

## Slide 6
Change of energy jitter & Spectral density
6
RF OFF
Energy jitter: 3.5%
Beam median energy: 257 MeV
RF ON
Energy jitter: 0.048%
Beam median energy: 275 MeV
Why did the beam energy increase from 257 MeV to 275 MeV?
The RF cavity was used primarily for energy compression, but operating at the optimal phase for minimum energy spread resulted in additional net acceleration of the beam centroid.

## Slide 7
Summary
7
Conclusions
Reduced the energy spread and energy jitter of LPA-generated electron beams to a level previously achievable only with large RF-based accelerators.
This technology enables practical application as a compact particle storage ring injector or for other industrial and medical applications.
Suggests that adopting X-band RF technology could enable scaling to GeV-level beam energies without significantly increasing the system footprint.

## Slide 8
PETRA IV in DESY
8

## Slide 9
9
Injection for PLS-II storage ring

## Slide 10
Injection for PLS-II Storage Ring
10
parameter | value
Distance btw B2 ~ B3 | 20 cm
Drift | 10 cm
The length of quadrupoles | 50 cm
The length of dipoles in Main Chicane | 1.5 m
The length of Rf cavities | 5m
RF frequency | 12 GHz
The length of dipoles in BTL | 50 cm
Fixed parameters
Storage Ring (long straight line)
parameter | value
Beam energy | 3 GeV
Energy spread | < 0.1 %
Energy jitter | < 0.12 %
Horizontal emittance | 5.8 nmrad
Vertical emittance | 0.058 nmrad
Horizontal beam size | 317
Vertical beam size | 16
Horizontal angular spread | 30
Vertical angular spread | 3.6
 | 6.50
 | 4.39
 | 0
 | 0
 | 0.25
 | 0.0
parameter | value
Beam energy | 3 GeV
Energy spread | < 0.1 %
Energy jitter | < 0.12 %
Horizontal emittance | 5.8 nmrad
Vertical emittance | 0.058 nmrad
Horizontal beam size | 
Vertical beam size | 
Horizontal angular spread | 
Vertical angular spread | 
 | 6.50
 | 4.39
 | 0
 | 0
 | 0.25
 | 0.0
Variables
The strength of Dipoles & Quads. , Distance btw magnets, Distance btw B1~B2 & B3~B4, The bending angle of dipoles in main chicane, RF phase

## Slide 11
Injection for PLS-II Storage Ring
11
Element | Length | Strength
Quadrupole Triplet | 50 cm | G 50 T/m
Main chicane dips. | 150 cm | B = 0.98 T
X-band cavity | 500 cm | V = 119.225 MV
Dips. For BTL | 70 cm | B = 1.26 T
Quads. for BTL | 50 cm | G 8 T/m
Element | Length | Strength
Quadrupole Triplet | 50 cm | 
Main chicane dips. | 150 cm | B = 0.98 T
X-band cavity | 500 cm | V = 119.225 MV
Dips. For BTL | 70 cm | B = 1.26 T
Quads. for BTL | 50 cm | 
Initial Beam State | 
Beam energy | 2.995 GeV
Energy spread | 1.0 %
Energy jitter | 1.0 %
Beam charge | 
Beam length | 
Initial Beam State | 
Beam energy | 2.995 GeV
Energy spread | 1.0 %
Energy jitter | 1.0 %
Beam charge | 
Beam length | 
Parameters of key beamline elements
LPA
QF1
QD1
Drift: 0.1m
WATCH
WATCH
QF2
B1
B2
B3
B4
WATCH
RF Cavity
Using X-band cavity, <5m
RF frequency: 12 GHz
WATCH
WATCH
To minimize angular spread
To stretch the bunch length
To eliminate the energy chirp
To injection into storage ring DA
QF3
QD3
QF4
QD4
B5
B6
B7

## Slide 12
Initial Beam State (After LPA)
12
LPA
Drift: 0.1m
WATCH
Beam energy | 2.995 GeV | Horizontal emittance | 4.478 nmrad |  | 0.145 m
Energy spread | 1.0 % | Vertical emittance | 0.045 nmrad |  | 0.058 m
Energy jitter | 1.0 % | Horizontal beam size | 25.481 |  | 8.375e-8
Beam charge |  | Vertical beam size | 1.615 |  | -3.35e-8
Bunch length | 2 | Horizontal angular spread | 175.729 |  | 1.367776e-19 m
 |  | Vertical angular spread | 27.849 |  | 1.641530e-20
Beam energy | 2.995 GeV | Horizontal emittance | 4.478 nmrad |  | 0.145 m
Energy spread | 1.0 % | Vertical emittance | 0.045 nmrad |  | 0.058 m
Energy jitter | 1.0 % | Horizontal beam size |  |  | 8.375e-8
Beam charge |  | Vertical beam size |  |  | -3.35e-8
Bunch length |  | Horizontal angular spread |  |  | 1.367776e-19 m
 |  | Vertical angular spread |  |  | 1.641530e-20

## Slide 13
Quad. Doublet for minimizing angular spread
13
LPA
QF1
QD1
Drift: 0.1m
WATCH
WATCH
WATCH
Length | 50 cm
DQ | 42 cm
QF1 | K 1= 5.3, G = 53 T/m
QD1 | K1 = -2.1, G = 21 T/m
Parameters of Quad. doublet

## Slide 14
After first quadrupoles (Quad doublet)
14
After first quadrupoles (Quad doublet)
parameter | value
Horizontal emittance | 4.482 nmrad
Vertical emittance | 0.048 nmrad
Horizontal beam size | 184.350
Vertical beam size | 55.700
Horizontal angular spread | 223.375
Vertical angular spread | 0.943
 | 7.58 m
 | 64 m
 | -9.13
 | -0.42
 | 0.0
 | 0.0
parameter | value
Horizontal emittance | 4.482 nmrad
Vertical emittance | 0.048 nmrad
Horizontal beam size | 
Vertical beam size | 
Horizontal angular spread | 
Vertical angular spread | 
 | 7.58 m
 | 64 m
 | -9.13
 | -0.42
 | 0.0
 | 0.0
After LPA
parameter | value
Horizontal emittance | 4.478 nmrad
Vertical emittance | 0.045 nmrad
Horizontal beam size | 25.481
Vertical beam size | 1.615
Horizontal angular spread | 175.729
Vertical angular spread | 27.849
 | 0.145 m
 | 0.058 m
 | 8.375e-8
 | -3.35e-8
 | 0
 | 0
parameter | value
Horizontal emittance | 4.478 nmrad
Vertical emittance | 0.045 nmrad
Horizontal beam size | 
Vertical beam size | 
Horizontal angular spread | 
Vertical angular spread | 
 | 0.145 m
 | 0.058 m
 | 8.375e-8
 | -3.35e-8
 | 0
 | 0

## Slide 15
Quad. Triplet for minimizing angular spread
15
LPA
QF1
QD1
Drift: 0.1m
WATCH
WATCH
WATCH
QF2
Length | 50 cm
D12 | 30 cm
D23 | 30 cm
QF1 | K1= 4.0, G = 40 T/m
QD1 | K1 = -5.0, G = 50 T/m
QF2 | K1 = 2.1, G = 21 T/m
Parameters of Quad. triplet

## Slide 16
After first quadrupoles (Quad triplet)
16
After first quadrupoles (Quad triplet)
parameter | value
Horizontal emittance | 4.588 nmrad
Vertical emittance | 0.045 nmrad
Horizontal beam size | 451.891
Vertical beam size | 24.318
Horizontal angular spread | 10.155
Vertical angular spread | 1.863
 | 44.5 m
 | 13 m
 | 0.016
 | 0.1
 | -6.616678e-08 m
 | 1.312809e-07
parameter | value
Horizontal emittance | 4.588 nmrad
Vertical emittance | 0.045 nmrad
Horizontal beam size | 
Vertical beam size | 
Horizontal angular spread | 
Vertical angular spread | 
 | 44.5 m
 | 13 m
 | 0.016
 | 0.1
 | -6.616678e-08 m
 | 1.312809e-07
After LPA
parameter | value
Horizontal emittance | 4.478 nmrad
Vertical emittance | 0.045 nmrad
Horizontal beam size | 25.481
Vertical beam size | 1.615
Horizontal angular spread | 175.729
Vertical angular spread | 27.849
 | 0.145 m
 | 0.058 m
 | 8.375e-8
 | -3.35e-8
 | 0
 | 0
parameter | value
Horizontal emittance | 4.478 nmrad
Vertical emittance | 0.045 nmrad
Horizontal beam size | 
Vertical beam size | 
Horizontal angular spread | 
Vertical angular spread | 
 | 0.145 m
 | 0.058 m
 | 8.375e-8
 | -3.35e-8
 | 0
 | 0

## Slide 17
Magnetic Chicane for bunch lengthening
17
Magnet length | 150 cm
Strength | B = 0.98 T
Bending angle [] | 8.41
[mm] | 100.7205
[mm] | -152.3553
Bunch length [mm] | 0.886
B1 ~ B2, B3 ~ B4 | 1.33 m
B2 ~ B3 | 0.1 m
Magnet length | 150 cm
Strength | B = 0.98 T
 | 8.41
 | 100.7205
 | -152.3553
Bunch length [mm] | 0.886
B1 ~ B2, B3 ~ B4 | 1.33 m
B2 ~ B3 | 0.1 m
Parameters of Main Chicane
LPA
QF1
QD1
Drift: 0.1m
WATCH
WATCH
QF2
B1
B2
B3
B4
WATCH

## Slide 18
After Main Chicane
18
After Main Chicane
parameter | value
Beam length | 0.886 mm ( ~ 3ps)
Horizontal emittance | 4.669 nmrad
Vertical emittance | 0.045 nmrad
Horizontal beam size | 477.034
Vertical beam size | 22.525
Horizontal angular spread | 10.535
Vertical angular spread | 2.003
 | 49 m
 | 11.2 m
 | -0.4
 | 0.065
 | -3.945518e-04 m
 | 1.063173e-05
parameter | value
Beam length | 0.886 mm ( ~ 3ps)
Horizontal emittance | 4.669 nmrad
Vertical emittance | 0.045 nmrad
Horizontal beam size | 
Vertical beam size | 
Horizontal angular spread | 
Vertical angular spread | 
 | 49 m
 | 11.2 m
 | -0.4
 | 0.065
 | -3.945518e-04 m
 | 1.063173e-05
After first quadrupoles (Quad triplet)
parameter | value
Beam length | 2
Horizontal emittance | 4.588 nmrad
Vertical emittance | 0.045 nmrad
Horizontal beam size | 451.891
Vertical beam size | 24.318
Horizontal angular spread | 10.155
Vertical angular spread | 1.863
 | 44.5 m
 | 13 m
 | 0.016
 | 0.1
 | -6.616678e-08 m
 | 1.312809e-07
parameter | value
Beam length | 
Horizontal emittance | 4.588 nmrad
Vertical emittance | 0.045 nmrad
Horizontal beam size | 
Vertical beam size | 
Horizontal angular spread | 
Vertical angular spread | 
 | 44.5 m
 | 13 m
 | 0.016
 | 0.1
 | -6.616678e-08 m
 | 1.312809e-07

## Slide 19
RF cavity for minimizing energy spread
19
RF cavity | 
RF voltage | 119.225 MV
RF frequency | 12 GHz
Cavity length | 5.0 m
LPA
QF1
QD1
Drift: 0.1m
WATCH
WATCH
QF2
B1
B2
B3
B4
WATCH
RF Cavity
Using X-band cavity, <5m
RF frequency: 12 GHz
WATCH

## Slide 20
RF cavity for minimizing energy spread
18
Theoretical value
After Decompression Chicane
After RF cavity
Optimal phase/voltage of cavity
RF voltage | 119.225 MV
RF phase | 2.714
RF frequency | 12 GHz
Cavity length | 5.0 m
RF voltage | 119.225 MV
RF phase | 
RF frequency | 12 GHz
Cavity length | 5.0 m
Optimal RF phase scan

## Slide 21
Graphs for each steps
20
(a) LPA Output |  |  | (b) After Chicane |  | 
Beam Energy [GeV] | 60 | 2.995 | Bunch Length [mm] | 0.8861 | 
Bunch Length [] |  |  | [mm] | 100.7205 | 
Energy Spread [%] |  | 1.0 | [mm] | -152.3553 | 
Energy Jitter [%] | 3.5 % | 1.0 | (d) Energy Spectrum |  | 
(c) After RF cavity |  |  | Before RF Cavity [GeV] |  | 2.995
Energy Spread [%] | 0.0162 |  | After RF Cavity [GeV] |  | 3
(a) LPA Output |  |  | (b) After Chicane |  | 
Beam Energy [GeV] | 60 | 2.995 | Bunch Length [mm] | 0.8861 | 
 |  |  |  | 100.7205 | 
Energy Spread [%] |  | 1.0 |  | -152.3553 | 
Energy Jitter [%] | 3.5 % | 1.0 | (d) Energy Spectrum |  | 
(c) After RF cavity |  |  | Before RF Cavity [GeV] |  | 2.995
Energy Spread [%] | 0.0162 |  | After RF Cavity [GeV] |  | 3
Bending angle [] | 8.41
Magnetic Field [T] | 0.98
 | 8.41
Magnetic Field [T] | 0.98
* Residual energy spread

## Slide 22
The change of energy jitter
21
RF OFF | 1.0 % | 2.71 pC/MeV
RF ON | 0.048 % | 31.19 pC/MeV

## Slide 23
After RF cavity
22
After Main Chicane
parameter | value
Beam energy | 2.995 GeV
Energy spread | 1 %
Energy jitter | 1 %
Horizontal emittance | 4.669 nmrad
Vertical emittance | 0.045 nmrad
Horizontal beam size | 477.034
Vertical beam size | 22.525
Horizontal angular spread | 10.535
Vertical angular spread | 2.003
 | 49 m
 | 11.2 m
 | -0.4
 | 0.065
 | -3.945518e-04 m
 | 1.063173e-05
parameter | value
Beam energy | 2.995 GeV
Energy spread | 1 %
Energy jitter | 1 %
Horizontal emittance | 4.669 nmrad
Vertical emittance | 0.045 nmrad
Horizontal beam size | 
Vertical beam size | 
Horizontal angular spread | 
Vertical angular spread | 
 | 49 m
 | 11.2 m
 | -0.4
 | 0.065
 | -3.945518e-04 m
 | 1.063173e-05
After RF cavity
parameter | value
Beam energy | 3 GeV
Energy spread | 0.0162 %
Energy jitter | 0.048 %
Horizontal emittance | 4.733 nmrad
Vertical emittance | 0.049 nmrad
Horizontal beam size | 1250.519
Vertical beam size | 189.498
Horizontal angular spread | 68.820
Vertical angular spread | 12.623
 | 330 m
 | 736 m
 | -18
 | -5.0
 | -6.004942e-02 m
 | -2.795973e-03
parameter | value
Beam energy | 3 GeV
Energy spread | 0.0162 %
Energy jitter | 0.048 %
Horizontal emittance | 4.733 nmrad
Vertical emittance | 0.049 nmrad
Horizontal beam size | 
Vertical beam size | 
Horizontal angular spread | 
Vertical angular spread | 
 | 330 m
 | 736 m
 | -18
 | -5.0
 | -6.004942e-02 m
 | -2.795973e-03

## Slide 24
BTL for injection into the Dynamic Aperture
22
length | 50 cm
QF3 | K 1= 0.2, G = 2 T/m
QD3 | K 1= -0.8, G = 8 T/m
QF4 | K 1= 0.6, G = 6 T/m
QD4 | K 1= -0.1, G = 1 T/m
Parameters of Quadrupoles
QF3
QD3
LPA
QF1
QD1
Drift: 0.1m
WATCH
WATCH
QF2
B1
B2
B3
B4
WATCH
RF Cavity
Using X-band cavity, <5m
RF frequency: 12 GHz
WATCH
QF4
QD4
WATCH
B5
B6
B7
length | 50 cm
B5 | Angle = 0.032, B = 0.01T
B6 | Angle = 3.6, B = 1.26T
B7 | Angle = 3.5, B = 1.21T
length | 50 cm
B5 | 
B6 | 
B7 | 
Parameters of Dipoles
28.46 m

## Slide 25
23
After BTL
parameter | value
Beam energy | 3 GeV
Energy spread | 0.0171 %
Energy jitter | 0.048 %
Horizontal emittance | 12.940 nmrad
Vertical emittance | 0.045 nmrad
Horizontal beam size | 307.210
Vertical beam size | 65.045
Horizontal angular spread | 111.441
Vertical angular spread | 11.432
 | 19.4 m
 | 94 m
 | 7.0
 | -16
 | 0.35 m
 | 0.1
parameter | value
Beam energy | 3 GeV
Energy spread | 0.0171 %
Energy jitter | 0.048 %
Horizontal emittance | 12.940 nmrad
Vertical emittance | 0.045 nmrad
Horizontal beam size | 
Vertical beam size | 
Horizontal angular spread | 
Vertical angular spread | 
 | 19.4 m
 | 94 m
 | 7.0
 | -16
 | 0.35 m
 | 0.1
After RF cavity
parameter | value
Beam energy | 3 GeV
Energy spread | 0.0162 %
Energy jitter | 0.048 %
Horizontal emittance | 4.733 nmrad
Vertical emittance | 0.049 nmrad
Horizontal beam size | 1250.519
Vertical beam size | 189.498
Horizontal angular spread | 68.820
Vertical angular spread | 12.623
 | 330 m
 | 736 m
 | -18
 | -5.0
 | -6.004942e-02 m
 | -2.795973e-03
parameter | value
Beam energy | 3 GeV
Energy spread | 0.0162 %
Energy jitter | 0.048 %
Horizontal emittance | 4.733 nmrad
Vertical emittance | 0.049 nmrad
Horizontal beam size | 
Vertical beam size | 
Horizontal angular spread | 
Vertical angular spread | 
 | 330 m
 | 736 m
 | -18
 | -5.0
 | -6.004942e-02 m
 | -2.795973e-03

## Slide 26
Dynamic Aperture at Injection point
24

## Slide 27
24

## Slide 28
Future Plan..
25
2. Multi-turn tracking -> Injection efficiency

## Slide 29
THANK YOU

## Slide 30
Appendix - Calculation

## Slide 31
Optimization for 1st quadrupoles (Quadrupole Doublet)
WATCH
최적화 변수
범위
LPA initial beam angular spread
After first quadrupoles
Loss function

## Slide 32
Optimization for 1st quadrupoles (Quad. Triplet)
WATCH
최적화 변수
범위
LPA initial beam angular spread
After first quadrupoles
Loss function

## Slide 33
Optimization for Main Chicane
WATCH
최적화 변수
범위
Objective function

## Slide 34
Calculation of energy spread and jitter (RMS)
Energy jitter
Where M is the number of shots
Energy spread
Where N is the number of macro-particles
After Chicane