## Slide 1: Operational Scenario for Enhancing the Touschek Lifetime of the PAL-EUV Storage Ring
Young Min Park
Division of Advanced Nuclear Engineering (DANE), POSTECH
2026-10-16, Pohang, South Korea

## Slide 2: Introduction
2
PAL-EUV
Compact 400 MeV storage designed as a high-power EUV source.
Skew quadrupoles (RS1) enable control of transverse coupling.
Active higher harmonic cavity (HHC) provides bunch lengthening.
Challenge
Short touschek lifetime : ~ 0.1 h
Skew : Dissonance injection / Transverse coherence
HHC : Robinson Instability

## Slide 3: Skew quadrupole
3
Skew quadrupole
A total of 48 skew quadrupoles are installed with RS1 sextupoles.
These skew quadrupoles induce transverse (x–y) coupling, increasing the vertical emittance.
Parameter | Value | Description
 |  | Circumference
 |  | Energy
 |  | Horizontal emittance
 |  | Beam current
 |  | Hor/Ver. tune
 |  | Harmonic number
 |  | Energy spread
 |  | Momentum compaction factor
 |  | Hor/Ver/Long. damping time
 |  | Damping partition number
Parameter | Value | Description
 |  | Circumference
 |  | Energy
 |  | Horizontal emittance
 |  | Beam current
 |  | Hor/Ver. tune
 |  | Harmonic number
 |  | Energy spread
 |  | Momentum compaction factor
 |  | Hor/Ver/Long. damping time
 |  | Damping partition number

## Slide 4: Coupling ratio
4
Transverse coherence
(For EUV undulator)
Increasing coupling → lower horizontal emittance, higher vertical emittance
Vertical coherence loss exceeds horizontal coherence gain → reduced total transverse coherence
Initial coupling target: 25% to maintain total transverse coherence above 40%
Beam size at 25% coupling: 4.95× the initial value

## Slide 5: Coupling constant
5
Relation between coupling constant & tune difference
Relation between the coupling constant and tune difference is fixed.
Then how can the coupling constant be determined?
  Injection particle : Minimize coupling to suppress the transfer of horizontal off-axis oscillation to the vertical plane.
  Stored beam : Maintain consistent coupling over the tune variation within the beam’s momentum spread.

## Slide 6: Coupling constant
6
Dissonance injection
No coupling for injected particles .
Amplitude dependent tune difference of an injected particles
: Amplitude transfer rate
Set the maximum vertical oscillation amplitude at the ID location : 0.75 mm
Stored beam coupling
Maintain an coupling ratio of at least 15% over the stored-beam momentum range
Operating point :

## Slide 7: Results for x-y coupling
7

## Slide 8: Harmonic cavity
8
Double-rf system
Higher harmonic cavity reduce voltage gradient and increase bunch length
Longitudinal stability
Parameter | Value | Description
 |  | Circumference
 |  | Energy
 |  | Horizontal emittance
 |  | Beam current
 |  | Harmonic number
 |  | Energy loss per turn
 |  | Main cavity voltage
 | 29000, 16162 | Main & HHC quality factor
 | 3.4, 1.45 | Main & HHC shunt impedance
Parameter | Value | Description
 |  | Circumference
 |  | Energy
 |  | Horizontal emittance
 |  | Beam current
 |  | Harmonic number
 |  | Energy loss per turn
 |  | Main cavity voltage
 | 29000, 16162 | Main & HHC quality factor
 |  | Main & HHC shunt impedance

## Slide 9: Harmonic cavity
9

## Slide 10: Longitudinal stability
10
Longitudinal stability
DC Robinson instability was the primary limitation on longitudinal stability
Operating point :

## Slide 11: Results for both coupling & HHC
11

## Slide 12: Summary and Future work
12
Results & Conclusions
Compared with the reference condition (1% coupling, without HHC), the proposed operating conditions increase the longitudinal bunch length and effective transverse beam area by factors of approximately 2.2 and 4.5, respectively.
These improvements suggest a potential tenfold enhancement in the Touschek lifetime, based on the reduction in beam density.
This study provides a basis for defining practical operating conditions to improve the beam lifetime and support stable operation of the PAL-EUV storage ring.
Future Work
Vertical dispersion correction: Optimize the lattice to compensate for vertical dispersion introduced by skew quadrupole magnets, targeting zero vertical dispersion at the insertion device (ID).
RF voltage optimization: Extend the optimization beyond the present fixed main cavity voltage of 100 kV, exploring operation up to the design maximum of 250 kV.

## Slide 13: Thank you for your attention!
13