## Slide 1: Present Status of J-PARC Linac LLRF System
Kenta Futatsukawa(A), Cicek Ersin(A), Zhigao Fang(A), Yuji Fukui(A), Satoshi Mizobata(A),
Yoshikatsu Sato(B), Shinichi Shinozaki(c)
(A): High Energy Accelerator Research Organization (KEK) in Japan
(B): NAT in Japan
(c): Japan Atomic Energy Agency (JAEA) in Japan
LLRF2023 - Sep. 23, 2023 -

## Slide 2
Outlook
Introduction of J-PARC and J-PARC LINAC
Replacing digital feedback and feedforward system：
  1st step: digitizer box for 324-MHz stations
  mTCA.4 system at MEBT1
Beam loading compensation system
  novel and superior adaptive beam loading compensation system calculated in the frequency domain
  demonstration of beam loading compensation system for discrete beam with comb-like structure
Phase drift compensation system to suppress the variation of output momentum
Summary

## Slide 3
J-PARC & J-PARC LINAC
J-PARC (Japan Proton Accelerator Research Complex)
J-PARC LINAC beam parameter
  particles: H- (negative hydrogen)
  kinematic energy: 400 MeV
  peak beam current: 50 mA
  acceleration frequencies: 324 MHz / 972 MHz
  pulse width: 500 ms (beam), ~650 ms (RF)
  repetition: 25 Hz (except of ADS)
The beam load on the field gradient is large due to the acceleration of high-current beams. For the J-PARC LINAC, the performance of the beam load compensation contributes greatly to the stability of the field gradient.
IS: H- Ion Source
RFQ: Radio Frequency Quadrupole Linac
DTL: Drift Tube Linac (3 cavity modules)
SDTL: Separate-type Drift Tube Linac (16 cavity stations)
ACS: Annual Coupled Structure Linac (21 cavity stations)
※ all normal conducting cavities
macro-pulse structure
intermediate-pulse structure
repetition：
25 Hz
frequency：
~1.23 MHz
required gradient stability :
    ±1% in amplitude,
    ±1 deg. in phase
comb-like structure

## Slide 4
J-PARC LINAC LLRF system
Jan. 2020 @ SDTL12
May 2020 @ SDTL02
summer shutdown of 2020 @ DTL2, SDTL01-16
summer shutdown of 2021
@ RFQ, DTL1-2
summer shutdown of 2021
@ MEBT1
old DFB&DFF system (cPCI)
updated only digitizer
mTCA.4 system
mTCA.4 system
chopper controller
digitizer box
cPCI analog module
PC + display with the touch panel function
mTCA.4 system
updated only digitizer
for MEBT1 B1-2, C1-2
@ RFQ, DTL1-3, SDTL01-16
NIM P.S.
The digital system of the 324-MHz LLRF system was completely updated until the summer shutdown of 2021. We are planning to replace the 324-MHz analog part to mRTM and eRTM boards of mTCA.4 and to develop the mTCA.4 system of 972-MHz stations.

## Slide 5
324-MHz DFB&DFF system: digitizer box
5
mRTM board
AMC board
Comparison with cPCI system
increasing number of elements: 1024 → 4096 (or 8192)
increasing monitor points: before/after the PI controller, before rotation matrix
increasing flexibility in table inputs: FB_REF/FF_BASE/PI_GAIN/FF_BEAM/rotation matrix
4 ch: 12-MHz IF sampling (utilizing downconverter of cPCI), 4 ch: direct sampling
The AMC board in digitizer box is same as the AMC board for 324-MHz mTCA.4 system to use the shelf.

## Slide 6
324-MHz DFB&DFF system: mTCA.4 system
6
eRTM board ： generating 312 MHz (LO), 324 MHz (RF), 12 MHz (reference), 120 MHz (FPGA clock), 240 MHz (ADC clock)
mRTM board ： implementing 8 ch down converter, 1 ch IQ modulator
→ 8 ch 12 MHz IF signals input to an AMC board
(digitizer box ： 4 ch 12 MHz IF, 4 ch 324 MHz RF(direct sampling)

## Slide 7
The time delay amount of the impulse response for DTL3 was clearly larger than that for SDTL01.
→ For actual measurement, the estimated transfer function includes not only general RF device but also circuits in digital board.
zoom
zoom
delay：~3 ms
delay：~1.5 ms
Beam loading compensation 1: transfer function
7
Firstly, we calculated the transfer function of our system to use the “actual time-domain measurement”.
DTL3
SDTL01
post coupler modes
The transfer function of DTL3 has a larger phase variation than that of SDTL01 at first measurement. → the time delay() is larger
transfer function
transfer function
→ impulse response
→ impulse response
※ It is a problem of setting the delay amount of ADC on the digital board, and this issue has now been fixed.

## Slide 8
Beam loading compensation 1: field stability and iteration
8
calculating optimal parameters in a few iterations. (The reason why not once is due to the nonlinearity of the klystron)
stability vs iterations [1]
intermediate-pulse structure
1.23-MHz components
±0.23% @50-mA beam
±0.036 deg. @50-mA beam
amplitude
phase
RF waveform (MLF operation)
The optimal parameters of beam loading correction (FF_BEAM) using the frequency-domain calculations are estimated
amplitude
phase
amplitude
phase
[1] K. Futatsukawa, et al., J. Instrum., 17 (11) (2022), p. T11002
[2] S. Li, et al., Nucl. Instrum. Meth. A 945 (2019) 162612

## Slide 9
Beam loading compensation 1: accumulation of errors
9
FF_BEAM：I
FF_BEAM：Q
There is no accumulation of errors in the FF_BEAM parameters after 3000 iterations.
expecting no divergence even after infinite iterations
no limit on number of iterations
Black：number of iterations = 10
Red：number of iterations = 500
For example) if 𝑥′(𝑡) has noise 𝜎 that cannot be removed by the LPF, √𝑛 𝜎 of noise will be accumulated in the FF_BEAM parameters in 𝑛 iterations.
→ divergence after finite iterations
→ need to limit the number of iterations
effect of brick-wall filter
[1] K. Futatsukawa, et al., J. Instrum., 17 (11) (2022), p. T11002
FF_BEAM parameters [1]
Example of accumulation of errors

## Slide 10
Beam loading compensation 2: discrete beam structure
10
[3] K. Futatsukawa, et al., Nucl. Instrum. Meth. A 1047 (2023) 167778
intermediate pulse structure
thinning
normal
1 bunch
thinning
The preset beam loading compensation system does not support the special intermediate pulse structure:
  normally 2-bunch operation in RCS, but 1-bunch operation in RCS
  certain intermediate pulses may be "thinned out" to adjust beam intensity
  sometimes the intermediate pulse width is adjusted in order to adjust the beam intensity.
→ In particular, the thinning operation can significantly worsen the field stability of the cavity field.
→ High-frequent changes in the beam tests require automatic adapted beam loading compensation..
amplitude
phase
present FF_BEAM
worsen in thinning timing
demonstrated FF_BEAM [3]
→ suppressing worse
DAC output
FF_BEAM with comb-like
adapted to beam structure

## Slide 11
Beam loading compensation 2: field stability
11
amplitude
phase
present FF_BEAM
demonstrated FF_BEAM [3]
In the present beam loading compensation system, the stability of amplitude and phase (±0.5% and ±0.6 deg.) has deteriorated worse when the discrete beam parameters were changed. The demonstrated beam loading compensation system for discrete beam structure can significantly suppress the deterioration and achieve the stability of less than ±0.2% in amplitude and less than ±0.15 deg. in phase.
[3] K. Futatsukawa, et al., Nucl. Instrum. Meth. A 1047 (2023) 167778
beam current: 25 mA

## Slide 12
Phase drift correction: reference
12
We installed the four precision air conditioners and airtight 19” racks as the reference no having the phase drift.
PAU-A1400-S-HC
- MEBT1: 1 rack
  airflow (m3/min) 4.8
  cooling capacity (W) 1400
  heating capacity (W) 2000
PAP05A1-K
- MEBT1C: 1 rack
- SDTL16/MEBT2B1: 2 racks / station
  rated airflow (m3/min) 3~5
  cooling & hearing capacity (W) 2300
  cooling capacity (W) 1600
precision air conditioner
PAP05A1-K
precision air conditioner
PAU-A1400-S-HC
airtight 19-inch rack
airtight 19-inch rack
pure water manufacturing device
wastewater evaporator
four racks:
  RF reference distribution system
  mTCA.4 system: MEBT1
  downstream 324-MHz: SDTL16
  upstream 972-MHz: MEBT2B1
reference
We estimates the amount of phase drift by comparing the phase of the reference and neighboring cavities

## Slide 13
Phase drift correction: results
13
raw data
data after LPF(IIR)
correction values
0.1 deg. ~ 2.3E-10 s
Phase Drift Correction
The all LLRF systems in the klystron galley environment are assumed to have the same amount of the phase drift, and the phase drift compensations are done when they vary by more than 0.075 deg. (0.1 deg. in figure) from the reference.
2018 (first time long-term measurement) [before correction]
Dp/p=0.07%
As the results of the phase drift compensation, the stability of the output momentum has improved enormously.
Long term stability of output momentum
humidity
atmospheric
pressure
center momentum
2023/02/01-03/01
2023/02/01~2023/03/01
momentum correction was done
Dp/p=0.07%
The output momentum correction is carried out about 1 or 2 times per month. (the program is always on work.)

## Slide 14
Summary
14
We are replacing the next generation digital feedback and feedforward system.
  MEBT1: installed and operated mTCA.4 system
  other 324-MHz stations: installed digitizer boxes and plan to replace with mTCA.4 system
  972-MHz stations: developing new mTCA.4 system
We developed the beam loading compensation system.
  adaptive beam loading compensation system calculated in the frequency domain
    Calculate optimal parameters in a few iterations
    no accumulation of errors in the FF_BEAM parameters
  beam loading compensation system for discrete beam with comb-like structure
    suppressing the deterioration when the beam condition such as thinning operation was changed
We developed the phase drift compensation system.
  enormously improving the stability of the output momentum from LINAC.

## Slide 15: Thank you for your attention

## Slide 16: BACKUP