## Slide 1: SSRF Lab talk
Yubin Zhao
2023-10-23
Shanghai advanced research institute. CAS
LLRF workshop 2023 in Gyeongju Korea

## Slide 2: content
SSRF and update
Soft X FEL
SHINE
summary
LLRF workshop 2023 in Gyeongju Korea

## Slide 3: Three facilities
SSRF 2004~
Soft X FEL 2014~
SHINE 2018~
LLRF workshop 2023 in Gyeongju Korea

## Slide 4: SSRF

## Slide 5: Layout of the SSRF complex
BOOSTER
Full energy booster ,optimized for top-up injection;
Beam emittance about 100 nm-rad @3.5 GeV for clean top-up operation;
A circumference of 180m and a injection energy of 150MeV;
Repeat rates up to 2Hz;
Storage ring
Energy：3.5 GeV；
Circumference：432m；
Current：5/300 mA (S/M bunch)；
emittance：3.9 mm-mrad；
RF voltage：4-6 MV
LLRF workshop 2023 in Gyeongju Korea
LINAC
Output Energy is upto 150MeV

## Slide 6
499.654MHz MO
magnet
A1
Beam measurement
A2
A3
A4
Accelerator tube
Storage ring
Booster
Attenuator
Phase shifter
LINAC
buncher
High power phase shifter
SSA
Harmonic buncher
GUN
modulator
SSA
45MWKlystron
6dB power splitter
X6
SSA
45MWKlystron
Phase control system
Phase control system
Phase shifter
3dB Power splitter
3dB Power splitter
modulator
WCM1
WCM2
WCM3
WCM4
LINAC RF
LINAC tunnel
LLRF workshop 2023 in Gyeongju Korea

## Slide 7
There are only six channels ADC, but the signal sampled are 11. so we use two second generation LLRF controller to deal with those signals, one is used to control the amplitude and phase, another is used to control the field flat and tuning control。
Architecture of booster RF system
Booster RF
LLRF workshop 2023 in Gyeongju Korea

## Slide 8: Update of Booster LLRF
Update reasons:
Accel did not provide the hardware
PXI controller and software update
When ramping mode, there happen stopping ramping
Communication complex（LabView+Sharememory）
Maintenance cost （power supply ，motor driver）
Analog LLRF from ACCEL
DLLRF
ALLRF GUI
DLLRF GUI
LLRF workshop 2023 in Gyeongju Korea

## Slide 9: LLRF controller in storage ring
Board with CPCI package，
4 Channel ADC.125MSPS
2 Channel DAC，275MSPS
4 down-converter and one up-converter channel
Linear is better than 60dB, isolate is better than 80dB
CPCI communication.
EPICS interface
Front-end board
DSP board
Controller Box
To motor driver
1
2
3
LLRF workshop 2023 in Gyeongju Korea
LLRF Interface

## Slide 10: Three harmonic SC cavity
Increase the Beam life time by lengthen the bunch
Passive mode
parameters | value
Times of beam length | ≥2
Times of beam Life time | ≥2
Harmonic frequency / MHz | 1498.96
Harmonic voltage / MV | 1.4 ~ 1.8
Temperature / K | 4.0
Static loss of thermostat/ W | ≤10
dynamic power consumption/ W | ≤5 @ Vh=1.8 MV
Q0 | ≥1E10 @ Vh=1.8 MV (Vertical test)
Adjust frequency bandwidth / kHz | +/- 500
Power of high order mode absorber / W | ≥ 400
Harmonic voltage stability % | ≤ +/- 1%
Specification
LLRF workshop 2023 in Gyeongju Korea

## Slide 11: Harmonic cavity operation
Two filling pattern ：1）four short bunch trains with ion-clearing gaps；2）mixed filling pattern
Mode 1: beam length longer 2.24 times
Mode 2: beam length longer 2.98 times
LLRF workshop 2023 in Gyeongju Korea

## Slide 12: SSRF--SXFEL
LLRF workshop 2023 in Gyeongju Korea

## Slide 13: SXFEL layout
Shanghai soft X ray FEL length is 532. It includes injector, LINAC, two undulator line (seeding + SASE), two beam line and 5 experiment station. the energy is 1.5GeV
2014 start，2022 to user stage
LLRF workshop 2023 in Gyeongju Korea

## Slide 14: SXFEL LINAC RF
C6
C4
C5
C9
C7
C8
C10
C11
L0-1
L0-2
L1-1
L1-2
LX
BC1
TDS2
TDS1
Gun
L2-1
L2-2
L2-3
L2-4
L2-5
L2-6
C3
C1
C2
S4
S5
S3
S1
S2
KX
BC2
L3-1
L3-2
L3-3
L3-4
L3-5
L3-7
L3-8
L3-9
L3-10
L3-11
L3-13
L3-14
cTDS
L3-6
L3-12
5 S-band klystron drive 4 accelerator structure and one transverse deflecting structure
11 C-band klystron drive 20 C-band accelerator structure and one transverse deflecting structure
1 X-band klystron drive one linear X-band structure
LLRF workshop 2023 in Gyeongju Korea

## Slide 15: SXFEL LLRF
parameters | value | value | value | units
Operation frequency | 2856 | 5712 | 11424 | MHz
repetition | 10 | 10 | 10 | Hz
Energy gain（2） | ≥108 | ≥126 | 20(1) | MeV
Amplitude (RMS) | ≤0.04* | ≤0.04 | ≤0.15% | %
Phase (RMS) | ≤0.09* | ≤0.18 | ≤0.15 | °
Table: LLRF specification
Typical RF station
Micro TCA chassis
LLRF workshop 2023 in Gyeongju Korea

## Slide 16: SXFEL Photos
EXPERIENCE HALL
LINAC TUNNEL
UNDULATOR TUNNEL
LLRF workshop 2023 in Gyeongju Korea

## Slide 17: SHINE
LLRF workshop 2023 in Gyeongju Korea

## Slide 18
SHINE
0 m 1400 m 1900 m 2300 m 3100 m
SC linac
undulator
beamline
Exp. Hall
Long beamline
Far Hall
Switchyard
dumps
Gun
LLRF workshop 2023 in Gyeongju Korea

## Slide 19: SHINE LINAC Layout
Injector：VHF GUN，buncher，single cavity cryomodule with two coupler，ABBA cryomodule，S-band transverse deflecting structure(0.5m)
LINAC：75 cryomodule (8 9-cell cavities) of 1.3GHz， S-band transverse deflecting structure (one meter)，16 X-band Deflecting structure ，two cryomodule of 3.9GHz（ 8 9-cell cavities ）
1.3GHz cavities basic requirement：At 2K: Q0≥2.7E+10 @ Eacc= 16 MV/m, max Eacc>19 MV/m
3.9GHz cavities basic requirement ： Q0≥2E+9@13.1MV/m
X-band: LLRF + 1 X-band Klystron + 4 X-band deflecting structure
Other: LLRF + high power + cavity
VHF gun
L0
L1
HL
BC1
L2
BC2
L3
LH
L4
2 CM
Dechirper
Ebeam=100MeV
2 CMH
18 CM
24 CM
30 CM
LLRF workshop 2023 in Gyeongju Korea

## Slide 20: SHINE Tunnel Layout
LLRF workshop 2023 in Gyeongju Korea
Inside diameter：6.3m

## Slide 21: Injector status
VHF gun : SEL，CW 70kW
Buncher: Pulse duty 50% 8kW
VHF gun and buncher had been installed before August 31.
LLRF workshop 2023 in Gyeongju Korea

## Slide 22
CMs development
CM1 prototype in horizontal test stand
3.E+10
2.E+10
2K vertical test results of the twin-FPC cavity
Two complete CM prototypes with 8 cavities were assembled, tested and studied in the past two years
CM1 Prototype：standard 8-cavities (BCP refurbished), tested in June 2022, reached its basic goal (Vtot>128 MV, average Q0>1.0E+10, Idark<1 nA).
CM2 Prototype：standard 8-cavities, including 6 midT-baked, 1 N-doped prototype cavities and 1 LG cavity, preliminary tested in Jan 2023.
  Max voltage in CW > 136 MV;
  High Q0 are preserved in HT;
Two special CMs for injector are under preparation.
LLRF workshop 2023 in Gyeongju Korea

## Slide 23
5.E+10
MP quenches
After the development of prototype cavities, 264 cavities for SHINE project have been ordered from both domestic and international manufactures (~ half half)
High-Q recipes: N-doping and mid-T baking
High-Q are stably achieved on the upcoming 1st batch cavities (8 per manufacture)
Key components – High-Q Cavities
N-doped cavities of the 1st small batch
<Eacc> = 26.3 MV/m
<Q0>= 3.2 E+10
<Eacc> = 27.9 MV/m
<Q0> = 3.3 E+10
Mid-T baked cavities of the 1st small batch
MP quenches
(Under he-tank welding)
LLRF workshop 2023 in Gyeongju Korea

## Slide 24: High power
Finished high power
4 1.3GHz/5.2kW prototypes
68 1.3GHz/5.2kW SSAs
1 1.3GHz/15kWSSA for Buncher
2 216MHz/60kW SSA for gun
1 3.9GHz/2kW prototype
2 S-band45MW klystron and 1 X-band 10MWklystron
Other high power hardware
VHF gun SSA
Beam current test platform
Injector SSA
1.3GHz SSA phase noise 37fs（10Hz~5MHz）
spur：-70dBc
Cavity horizontal test SSA
LLRF workshop 2023 in Gyeongju Korea

## Slide 25
LLRF requirement
VHF gun LLRF requirement |  | 
Parameters | value | Units
Frequency | 216.67 | MHz
Amplitude(RMS) | 0.02 | %
Phase(RMS) | 0.02 | Deg
Operation mode | CW | 
Buncher LLRF requirement |  | 
Parameters | value | Units
Frequency | 1300 | MHz
Amplitude(RMS) | 0.02 | %
Phase(RMS) | 0.02 | Deg
Operation mode | CW | 
1.3GHz cryomodule LLRF requirement |  | 
Parameters | value | Units
Frequency | 1300 | MHz
Amplitude(RMS) | 0.02 | %
Phase(RMS) | 0.02 | Deg
Detuning (RMS) | 5 | Hz
Detuning (peak) | 10 | Hz
Gradient | 16 | MV/m
Operation mode | CW | 
3.9GHz cryomodule LLRF requirement |  | 
Parameters | value | Units
Frequency | 3900 | MHz
Amplitude(RMS) | 0.02 | %
Phase(RMS) | 0.02 | Deg
Detuning (RMS) | 5 | Hz
Detuning peak | 30 | Hz
Gradient | 13 | MV/m
Operation mode | CW | 
S-band LLRF requirement |  | 
Parameters | value | Units
Frequency | 2997.22 | MHz
Amplitude(RMS) | 0.04 | %
Phase(RMS) | 0.1 | Deg
Operation mode | 50 | Hz
X-band LLRF requirement |  | 
Parameters | value | Units
Frequency | 11988.889 | MHz
Amplitude(RMS) | 0.15 | %
Phase(RMS) | 0.15 | Deg
Operation mode | 50 | Hz
LLRF workshop 2023 in Gyeongju Korea

## Slide 26
RF Front-end
Types | Ref in/MHz) | frequency/MHz | LO/MHz | IF/MHz | Ref out/MHz)
VHF gun | 1300 | 216.67 | 236.4 | 19.7 | 1300
Buncher | 1300 | 1300 | 1319.70 | 19.7 | 1300
S TDS | 1300 | 2997.2 | 3016.9 | 19.7 | 1300
X TDS | 1300 | 11988.9 | 11700+308 | 19.7 | 1300
1.3GHz | 1300 | 1300 | 1319.70 | 19.7 | 1300
3.9GHz | 1300 | 3900 | 3919.7 | 19.7 | 1300
1.3GHz LLRF front-end signa flow
X-band LO, up and down converter
LLRF workshop 2023 in Gyeongju Korea
X-band RF front-end
L,S-band RF front-end

## Slide 27
6U Compact-PCI package
4 ADC channels ，2 DAC channels
  ADC：forward、reflected、pick-up
  DAC：SSA(high power)
One trigger in port
ZYNQ
  FPGA(PL): algrithme
    4Gb DDR3，save ADCs data
  ARM(PS):
    OS：LINUX
    4Gb DDR3
  Inner communication：AXI4
1000M ethernet：to center room
64G MMC Memory：save data
Two SPIs： control ATT of RF front-end
LLRF DSP
Standard 1.3GHz DSP X-band DSP (10 channel ADC’s)
LLRF workshop 2023 in Gyeongju Korea

## Slide 28
Amplitude and phase loop：
  1、PI
  2、SEL
  3、Pulse
Slow tuning：
  1、PI
  2、monitor
Fast tuning：
  1、PI
  2、microphonic suppresion
others：
  1、QL measure online
  2、interlock
LLRF algorithm
LLRF workshop 2023 in Gyeongju Korea

## Slide 29: summary
SSRF RF system work well and three harmonic cavity have been used in storage ring
SXFEL had been finished. Now it is open to user.
SHINE is under construction. development and manufactory of RF cavity, cryomodule, high power and LLRF is in progress.
LLRF workshop 2023 in Gyeongju Korea

## Slide 30: Thanks
LLRF workshop 2023 in Gyeongju Korea