## Slide 1: Unleashing the Full Potential of LLRF Algorithms: Enhancing Stability, Reliability, and Accuracy in RF Systems —— IQ Award Presentation (LLRF2023)
Feng Qiu, on behalf of LLRF grp of KEK & IMP
Institute of Modern Physics (IMP), Chinese Academy of Science
Notes: I'm really excited to have won the IQ Award, and it's a big honor for both myself and my Institute. Now, I'll start my award presentation at first

## Slide 2
Research Activities
Sum. & Acknowledgment
Self-Introduction
01
02
03
CONTENTS

## Slide 3: Self Introduction
F. Qiu, Senior Staff Scientist, 1985/07/05, Affiliation: Institute of Modern Physics (IMP), China
  PhD degree @ IHEP (Beijing), Assistant Prof. @ KEK (previous affiliation)
2007-2012，IHEP, PhD
2012-2020，KEK, RF grp.， Assistant Prof.（Permanent）
2020/12 @ IMP, Staff Scientist
2020/11, from KEK to IMP
Research Direction
LLRF algorithm
Application of AI-technique in ACCLs
From 2024
China initiative ADS （CiADS）
Notes: I obtained my PhD degree from the IHEP in 2012. Afterward, I came to Japan and worked as a postdoctoral researcher at KEK. In 2014, I was promoted to the position of Assistant Professor. In 2020, I transitioned from KEK to work at the IMP. Currently, I hold the position of staff at IMP. In the next year, we will move to the southern China to attend the China initiative ADS project.

## Slide 4: Self Introduction (cont’d)
Mont. Tsukuba
STF（Superconducting test-facility）
cERL (compact ERL)
SRF
SRF
Cav | QL | RF Source
Bun | 1.1e5 | 8 kW SSA
Inj1 | 1.2e6 | 25 kW Kly.
Inj2 | 5.8e5 | 300 kW Kly.
Inj3 | 4.8e5 | 
ML1 | 1.3e7 | 8 kW SSA
ML2 | 1.0e7 | 16 kW SSA
KEK
CiADS
@Huizhou
@Tsukuba
SRF
CiADS
CAFe (Chinese ADS Front-end), 162.5 MHz, CW
cERL 1.3 GHz, CW
HWR010 (β=0.1)
HWR015 (β=0.1)
RFQ
~20 MeV, 10 mA
1 RFQ+ 23 SC
QL: 5e5~1e6
10 kW SSA
Aerial View
Architectural Rendering
Linac Prototype
HIAF (High Intensity heavy-ion Accl. Facility)
Main project involved: cERL and STF @ KEK; CiADS (& its prototype facility: CAFe) @ IMP
Sep. 2023
KEKB-LINAC
~20 MeV
Notes: In KEK, I was

## Slide 5: LLRF Algorithms (Achievements in the last 3 years)
LLRF
RF & linac
Beam
LLRF
Algorithm
RF Stability
Reliability
Beam Quality
Ctrl. Algorithm
RF/Beam
Commissioning
Signal Cali. / Meas.
& Sys. Identification
Disturbance Observer-based Ctrl.
Active Noise Control
Modified Iterative Learning Ctrl.
FF-based Rapid Phase Tuning
Channel Crosstalk Calibration
LFD Transfer Function Meas.
Burst-noise Mitigation
Novel RF Pulse Shaping Scheme
Loaded Q and Detuning Cali.
PRAB, 24:012804, 2021
NST, 32:56, 2021
NIM-A, 955:163820, 2020
NIM-A, 1026: 166237, 2022
IEEE-TNS, 70:2, 2023
NIM-A, 985: 164660, 2021
NST, 32:140, 2022
NIM-A, 1034: 166769, 2022
NST, 33:4, 2022
NST, 34:123, 2023
NIMA, 1012:165633, 2021
KEK Work
IMP Work
Academic Achievements
Advanced LLRF algorithms are crucial for improving the beam quality
Notes: Advanced LLRF algorithms are essential for improving RF stability and reliability, as well as the beam quality. I focus on the LLRF algorithms from three aspects: advanced control algorithms, Algorithms in RF/Beam commissioning, and signal calibration algorithm. Here are the academic achievements I have made in the last three years. The orange color indicates my works in KEK and the blue colors represent my IMP work

## Slide 6: LLRF Algorithms (Achievements in the last 3 years)
LLRF
RF & linac
Beam
RF Stability
Reliability
Beam Quality
Ctrl. Algorithm
RF/Beam
Commissioning
Signal Cali. / Meas.
& Sys. Identification
Disturbance Observer-based Ctrl.
Active Noise Control
Modified Iterative Learning Ctrl.
FF-based Rapid Phase Tuning
Channel Crosstalk Calibration
LFD Transfer Function Meas.
Burst-noise Mitigation
Novel RF Pulse Shaping Scheme
Loaded Q and Detuning Cali.
LLRF
Algorithm
KEK Work
IMP Work
PRAB, 24:012804, 2021
NST, 32:56, 2021
NIM-A, 955:163820, 2020
NIM-A, 1026: 166237, 2022
IEEE-TNS, 70:2, 2023
NIM-A, 985: 164660, 2021
NST, 32:140, 2022
NIM-A, 1034: 166769, 2022
NST, 33:4, 2022
NST, 34:123, 2023
NIMA, 1012:165633, 2021
Academic Achievements
Advanced LLRF algorithms are crucial for improving the beam quality
Notes: Today, because of the time limitation, I only focus on these four topics.

## Slide 7
Research Activities
Self-Introduction
01
02
CONTENTS
Disturbance Observer-based Ctrl.
Modified Iterative Learning Ctrl.
Channel Crosstalk Calibration
Burst-noise Mitigation

## Slide 8
Pulse Mode Operation @ cERL
Operated cERL in pulse mode to increase the beam energy (for isotope production)
Encountered poor pulse-to-pulse stability under PI ctrl (Intra-pulse stability looks good)
Observed fluctuations in the measured beam energy
Pulse-to-pulse
RF Stability (Pulse-to-pulse)
Beam Energy Stability
Pulse shape
Amp
Phase
Detuning
F. Qiu*, et al., Application of disturbance observer-based control on pulsed superconducting radio frequency cavities Phy. Rev. Accel Beam 21, 032003 (2018)
Notes: During the pulsed mode beam operation at cERL, we have encountered poor pulse-to-pulse stability under the traditional PI ctrl, the intra-pulse stability seems not bad. From one hour of beam energy data, it can be observed that there is a significant fluctuation in beam energy, and this fluctuation is closely related to the pulse-to-pulse RF stabilities.

## Slide 9
d
y
Disturbance Observer-based (DOB) Control
Disturbance Observer (DOB) ctrl.: Reconstruct disturbance estimation ( ), then cancel d with from the LLRF control loop
PI
Cav
y
Re-construct
Notes: Assuming that external disturbances, such as the beam, is 'd,' and the cavity's output is 'y,' we can then reconstruct the disturbance signal 'dhat’ from y using the inverse cavity model. Subsequently, we can eliminate 'dhat' from the control loop. Please note that a low-pass 'Q' filter is required to remove high-frequency components

## Slide 10
F. Qiu*, et al., Application of disturbance observer-based control on pulsed superconducting radio frequency cavities Phy. Rev. Accel Beam 21, 032003 (2021)
F. Qiu*, et al., Combined disturbance-observer-based control and iterative learning control design for pulsed superconducting radio frequency cavities, Nucl. Sci. Tech. 32:56 (2021)
DOB Control (cont’d)
PI+DOB
PI
RF stabilities (Pulse-to-pulse)
PI+DOB
PI
RF stabilities (intra-pulse)
Beam
Beam Energy
(NO fluc.)
PI+DOB
PI
High RF stabilities and beam energy stability have been achieved
Notes: We have applied the PI+DOB control in cERL LLRF systems. Here is the results of the intra-pulse in the presence of a approximately 1 mA beam. As you see that the beam induced RF transient is well compensated by the proposed DOB control. Here is the result of the pulse-to-pulse RF stabilities. As is shown The DOB control can significantly improve pulse-to-pulse stability. Meanwhile the fluctuation in the beam-energy was removed.

## Slide 11
Research Activities
Self-Introduction
01
02
CONTENTS
Disturbance Observer-based Ctrl.
Modified Iterative Learning Ctrl.
Channel Crosstalk Calibration
Burst-noise Mitigation

## Slide 12
SRF cavities
CAFe
CERN-COURIER evaluates this achievement as an outstanding accomplishment and a milestone breakthrough in the field of ADS
The transient loading of a 10 mA beam is the most critical technical challenge!!
10 mA
0 mA
10 mA
Operation
Self-recovery
Pulse
CW Operation
Fault
Recovery within second-level
Time [μs]
ΔA/A ~ 3%
Transient beam-loading @10 mA
Pha. [deg]
Amp. [a. u.]
Δθ ~ 3 deg
Transient Loading of 10 mA Beam @ CAFe
CAFe → Stable operation of 10 mA proton beam
  In March 2021，CAFe achieved stable operation at hundreds of kW for 100 hours, confirming the feasibility 10 mA beam operation. The average beam current set new world records for proton linear SRF accelerators
Notes: In this achievement, one of the challenge issue is the transient loading of a 10mA beam. As a complex system, faults cannot be avoided in CAFe. When a fault occurs, we have to stop the beam, wait for the fault to be recovered, and then reload the pulsed beam. The transient load of the 10mA beam may cause RF instability.

## Slide 13
The main ILC algorithm is usually implemented outside FPGA
A matrix or a zero-phase filter
A matrix or a plant-inversion-model or PID
Step1： Calibrate the error between the reference signal (r) and cavity pick-up signal (y)
Step2： Update the current feedforward (FF) output (uj+1) using the previous FF (uj) and error (ej)
ej (k)=rj (k)-yj (k)
uj+1 (k)=QILC [uj + L(ej )]
E.g. Norm Optimal ILC
Complicated
Iterative Learning Control（ILC）
Iterative Learning Control (ILC) →widely used for beam-loading compensation
—— D. H. Owens, Springer, 2015
Notes: The traditional ILC algorithm is usually implemented outside of FPGA due to the high computational cost, which may reduce its real-time capabilities.

## Slide 14
uj+1 (k) = QILC [uj + L(ej )]
uj+1 (k) = εj + Fj , εj = L(ej)
Fj+1 = Fj + Ej
Beam profile @ CAFe
Constant Value (only a register inside FPGA)
FF
“quasi-rectangular”
In most cases, a beam pulse can be considered quasi-rectangular, which means the FF could also be rectangular pulse. This assumption may significantly simplify the update law
FPGA-based ILC (Basic Idea)
Notes: In most cases, a beam pulse can be considered a quasi-rectangular, which means the FF could also be rectangular pulse. This assumption may significantly simplify the update law

## Slide 15
C. Xu，Z. Zhu，F. Qiu* et al., Application of a modified iterative learning control algorithm for superconducting radio-frequency cavities, Nucl. Instrum. Methods. A . 955,166237 (2022)
RF waveforms during iter. proc.
Convergence curve
Cav. Field
FF
Cav. Field
FF
Field Amp.
Field Pha.
FPGA-based ILC (Confirmation)
The new ILC algorithm was demonstrated during the CAFe beam-commissioning
  High rep. rate: works in 1 kHz ~ 1 MH; High bandwidth (NO Q-filter)
Implementation
20 μs beam

## Slide 16
Research Activities
Self-Introduction
01
02
CONTENTS
Disturbance Observer-based Ctrl.
Modified Iterative Learning Ctrl.
Crosstalk Cali. & φb Cali.
Burst-noise Mitigation

## Slide 17
The burst noise can lead to an unexpected LLRF response, eventually causing a cavity fault
Burst-noise and its implication
Two types of burst noise signals induced by field emission
  Flashover & (Partial) E-quench
2 μs
Pick-up
Pick-up
6 μs
E-quench
FE
Amp [norm. units]
Flashover
Amp [norm. units]
Flashover: Discharge at pick-up antenna, the actual field remains unchanged
(Partial) E-quench: Discharge at cavity inner conductor, the actual field rapidly decreases
burst noise
burst noise
burst noise
Partial E-quench
Total E-quench
Flashover
Vc Amp [norm. units]
Time [ms]
Range
>15 MV/m
>25 MV/m
>35 MV/m
Item
Flashover
Partial E-quench
Total E-quench
Duration
< 5 μs
5 ~ 7 μs
~ 1 μs
Eacc loss
None
2% ~ 30%
100%
Vc
Pick-up
Notes: During CAFe commissioning, we have observed many FE-induced cavity faults. Generally, there are two types of faults with different mechanisms: flashover and E-quench. In both of these two cases, a burst noise signal appears in the cavity pick-up. This burst noise signal can lead to an unexpected LLRF response, eventually causing a cavity fault.

## Slide 18
∆T
udelay is the reasonable PI output
0.8 μs
uPI
udelay
reset
PI output
Pick-up
Burst-noise Processing Algorithm (Basic Idea)
When the LLRF system detects the burst-noise events, a burst-noise trigger is immediately emitted and is held for a time interval of ∆T (>15 μs)
The PI output (uPI ) is overwritten by udelay which retains the data from uPI 0.8 μs prior to burst-noise trigger; then the uPI is maintained until the trigger is over
Implementation

## Slide 19
Burst-noise trigger
Field amp.
Field pha.
Burst-noise Processing Algorithm (Results)
The unexpected LLRF response can be eliminated
The effectiveness of the proposed algorithm was confirmed during the long-term operation
Beam
W/o proposed algorithm
With proposed algorithm
24 hours
Cavity pick-up
Cavity forward
Beam

## Slide 20
CM2-5
“dark-current”-induced transient (I/Q)
Statistical Distribution
The “partial E-quench” caused dark-current can be seen as a kind of beam-loading. It is possible to characterize the dark current using the “beam (dark-current)”-induced RF transient
Partial E-quench
F. Qiu* et al., In-situ mitigation strategies of field emission induced cavity fault using low-level radio-frequency system, Nucl. Sci. Tech. 33:140, 2022
“dark-current”-induced RF transient
The “partial E-quench” is accompanied by dark-current which can be seen as a kind of beam-loading. It is possible to characterize the dark current using the “beam induced RF transient”
Dark-current induced gradient loss [MV/m]
Phase of dark-current [deg]
Real part [norm. units]
Imag. Part [norm. units]
Dark-current Characteristic
Notes: It is evident that the intensity and phase of the dark current conform to a specific distribution, it is very interesting even the mechanism remains unclear

## Slide 21
Research Activities
Self-Introduction
01
02
CONTENTS
Disturbance Observer-based Ctrl.
Modified Iterative Learning Ctrl.
Channel Crosstalk Calibration
Burst-noise Mitigation

## Slide 22
Issues impacting RF Signal Measurements
Measurement accuracy of RF signals is mainly affected by two factors:
  Crosstalk between the meas. channels (e.g., dir. coupler)
  Impedance mismatch of high-power RF components (RF source or Circulator) → See J. Y. Ma’s Poster （ID: 09）
May impact the field decay process and cause the inaccurate meas. of QL [1]
[1] J. Y. Ma, …F. Qiu* et al., Measurement of the cavity‑loaded quality factor in superconducting radio‑frequency systems with mismatched source impedance, Nucl. Sci. Tech. 33:123, 2023
[2] A. Brandt, PhD thesis, Universitt Hamburg, 2007
May impact the measurement of Vf signal
The coefficients a b c d can be calibrated using the cav. diff. equation under pulse mode op.[2]
DESY’s
Method
Real part [norm. units]
Imag. part [norm. units]

## Slide 23
Novel Signal Calibration Algorithm
We proposed a novel signal calibration algorithm more suitable for CW mode machine
Condition 1:
Vectors Identity
Condition 2:
Detuning Continuity
We can’t locate the opt. coef. (using DESY’s method)
For CW machine, we have:
Ellipse→strip
Notes: For a CW machine, the cavity voltage Vc is constant, thus its derivative is approximately equal to 0. In this case, it is difficult to locate the optimal coefficient using DESY’s method. Here, we propose a new signal calibration algorithm that is more suitable for a CW mode machine. There are three conditions that must be satisfied:
Condition 1: The real part of 2Vf in the steady-state should be the same as the real part of Vc. Condition 2: The detuning just before and after RF is turned off should be identical

## Slide 24
J. Y. Ma, F. Qiu* et al., Precise calibration of cavity forward and reflected signal using low-level radio-frequency system, Nucl. Sci. Tech. 33:4, 2022
F. Qiu* et al., Approach to calibrate actual cavity forward and reflected signals for continuous wave-operated cavities, Nucl. Instrum. Methods. A . 955,166237 (2022)
The proposed algorithm was confirmed at CAFe
Cond. 1
Cond. 2
Proposed Algorithm (CW)
DESY’s Algorithm (Pulse)
Novel Signal Calibration Algorithm (Results)
Notes: Using the RF-off data, we have applied the proposed algorithm to our cavities. Firstly, we apply the first condition, resulting in a blue straight line. In the next step, we apply the second condition, resulting in a green straight line. The crossing point is then the optimal calibration coefficient. We have compared our method with DESY's method, and they are in good consistency with each other.

## Slide 25: Beam Phase Calibration (application)
BPM Meas.
Beam Phase using RF
With cali.
W/o cali.
φb
Ib
Within the calibrated optimal coefficients, it is possible to accurately calculate the RF vectors, as well as the beam phase
Cross-talk was considered
Real part [norm. units]
Imaginary part [norm. units]

## Slide 26
Research Activities
Sum. & Acknowledgment
Self-Introduction
02
03
CONTENTS
01

## Slide 27
Summary
26
Innovatively applying DOB control in the LLRF community, achieving precise beam energy spread control with remarkable results at cERL
Leveraging prior knowledge of the beam profile to develop a FPGA-based real-time ILC control, successfully suppressing RF transient instabilities caused by the10 mA CW proton beam at CAFe
Developing a real-time digital filter with robustness to FE-induced burst noise, resolving RF instability and improving machine reliability of CAFe
Proposing a novel cross-talk calibration algorithm for SRF cavities operated in CW mode

## Slide 28
Acknowledgments
27
I would like to express my gratitude to LLRF SPC & LOC for this incredible honor. I would also like to thank the members of the Selection Committee for their diligence and hard work in choosing me for this award. Special thanks to generous Dimtel Inc. for their invaluable support
I want to acknowledge the unwavering support of RF group and Beam-commissioning team in KEK and IMP
  KEK: S. Michizono (Supervisor, Division Head), T. Matsumoto, T. Miura, K. Furukawa, Z. Fang, H. Sakai, M. Omet, D. Arakawa, S. Matsumoto, E. Kako, K. Umemori, H. Katagiri, S. Fukuda, T. Furuya, T. Miyajima, T. Obina…
  IMP: Y. He (Division Head), Z. J. Wang, G. R. Huang, L. P. Sun, Z. Gao, T. C. Jiang, Z. L. Zhu, Q. Chen, L. B. Xu, Z. H. Xue, J. Y. Ma, L. J. Yang, C. Y. Xu, Z. L. Zhang, T. Tan, M. X. Xu, Z. Q. Yang, A. D. Wu, C. Y. J. Wong, D. D. Luo…
I owe a debt of gratitude to my family, colleagues, and friends
Finally, thanks again for this incredible honor. I am deeply moved and inspired to continue my work with renewed passion and dedication
Notes: I would like to express my heartfelt gratitude to LLRF SPC & LOC for this incredible honor. I would also like to thank the members of the selection committee for their diligence and hard work in choosing me for this award.
I want to acknowledge the unwavering support of RF group and Beam-commissioning team in KEK and IMP, If there is no good team and research platform, it is impossible to achieve good results
I owe a debt of gratitude to my family, colleagues, and friends. Thank you for their companionship when I encountered difficulties
I would like to every colleges in the LLRF community. Engaging in discussions with all of you has provided me with many new ideas.
Finally, thank you for this incredible honor. I am deeply moved and inspired to continue my work with renewed passion and dedication

## Slide 29
Thanks for your attention
감사합니다

## Slide 30
Back-up Slides

## Slide 31
SRF faults account for most beam trips (Eu-XFEL/CEBAF/ELBE/CAFe)
Problem: Minimize cavity faults to enhance beam availability, reliability, and stability
Solution: Gain a deep understanding of the unstable mechanisms behind cavity faults
Chart: 
| RF | IS | Control | Diag | Vac | PS
销售额 | 73 | 9 | 8 | 7 | 2 | 1
SRF: 73%
IS: 9%
Ctrl: 8%
Diag: 7%
Vac: 2% PS: 1%
Chart: 
| RF | IS | Ctrl | Human | Radiation | Cryomodule | PS | Diag
Percent | 64 | 21 | 6 | 5 | 3 | 2 | 2 | 2
SRF: 64%
IS: 21%
Ctrl: 6%
Human: 5%
CAFe @ 2.5 mA, 45 kW
CAFe @ 10 mA, 200 kW
Rad: 3%
Cry: 2% PS: 2%
RF Trips
He Fluc.
Quench
Cav. FE
…
SRF faults contribute to the dominant beam trips
Availability
Reliability
Stability
Requirements
SRF faults at CAFe
Notes: During the long-term operation of accelerators, various types of faults can occur. Based on the experience of major international laboratories, superconducting cavity malfunctions constitute a significant portion of the total faults. Common issues include the complexity and diversity of superconducting cavity faults. Addressing the challenge of reducing superconducting cavity faults to enhance beam reliability is an international issue. Resolving this problem requires an in-depth study of the unstable physical mechanisms and fault patterns of superconducting cavities.

## Slide 32
Thermal quench
Helium fluc.
QL
Δf
Δf
QL
Vc phase (LLRF trip)
Vc phase (Ponderomotive)
Spectrum
Spectrum
闪断
E-Quench
LLRF trip & Ponderomotive
Digtial low-level RF
Capture fault waveform
Analyze fault patterns & mechanisms
Features of the DAQ：
  10 kHz ~ 100 kHz rates
  0.5 s ~ 5 s waveforms
  8 ADC channels
Flashover & E-quench
SRF faults at CAFe (cont’d)
Notes: During this beam tuning process, we also observed a significant number of superconducting cavity faults. Before and after each fault occurrence, the LLRF system records a amount of fault data. Through data analysis, we can further identify fault patterns and study the physical mechanisms behind these faults

## Slide 33
Qid
Eid
Fmax
Efmax
Std_A1
Std_A2
Mean_Pdiff
Max_ Pdiff
Diff_Pf
…
SVM (support vector machine)
Radom Forest
K-means
…
Raw fault signals
Signal Preprocessing
Feature Extraction
ML classification
Statistical Features
FFT & Wavelet
Model-based
QL
Detuning
Confusion matrix
PCA plot
Phase
Amp.
Principal Component Analysis
ML-based SRF faults Classification

## Slide 34: ML-based SRF faults Classification (cont’d)
Predicted Patterns
PCA1
PCA2
True Patterns
Features
Importance
Precision: Roughly > 90% (compared with expert predictions), seems promising
PCA analysis: Which patterns are prone to confusion?
Feature importance analysis: Which features have the greatest impact on the results?

## Slide 35: Beam Phase Calibration
The cavity forward power would be different in the case of with and w/o beam
Characterize the beam vectors Vb using Vf signal with beam (Uwb) and w/o beam (Unb)
Vector Plots (in steady-state)
ALL the RF signals reaches steady-state (Ib , Vc , Vf )
Good measurement accuracy (cross-talk cali.)
Waveform Plots
Vb= Unb- Uwb
φb= ∠Vb
Ib = |Vb|

## Slide 36: Beam Phase Calibration (@ IMP-CAFe)
BPM
Proposed Method
With cali.
W/o cali.
The preliminary experiment was confirmed at IMP
F. Qiu* et al., Approach to calibrate actual cavity forward and reflected signals for continuous wave-operated cavities, Nucl. Instrum. Methods. A . 955,166237 (2022)
steady-state
φb
Ib
steady-state