## Slide 1: Round Table 1
Reliability and Anomaly Detection
Julien Branlard, for DESY Gyeangju, Republic of Korea, 23.10.2023

## Slide 2: Examples of anomalies
FW corruption
Traces are jumping back and forth between 2 values
 often indication of FW corruption

## Slide 3: Examples of anomalies
HW: cavity events
 Time constants can give an hint if the anomaly takes place inside the cavity or at the drive level.
Transient ringing
Instantaneous “plasma” discharge

## Slide 4: Examples of anomalies
SW / FW : DMA access during write
RF pulse “compression”
or
corrupted data transfer
Software bugs can appear when the CPU load is high (i.e. cron job at Sunday 00:00)
 Time stamp can be a hint towards a SW bug

## Slide 5: Examples of anomalies
HW : external components, detection chain
Faulty piezo driver corrupting the RF pulse
Loose N-type connector
Contact between capacitor and shielding
Hardware bugs usually have very distinct signatures, but can be intermittent depending on ambient temperature for example
 Divide and conquer, swapping components

## Slide 6: Types of system anomalies
  HW failure
      i.e. power supply, waveguide sparks, cavity event
  FW failure
      i.e. bit stream corruption because of SEU, write during read
  SW failure
      i.e. delayed interrupts due to CPU load
  High-level algorithms
      i.e. race condition / run away situation between diverse feedback SW algorithms
  Human factor
      i.e. wrong config, safety bypass left enabled by mistake, etc...
Non-exhaustive list

## Slide 7: Anomaly detection
“Traditional” approach
  Threshold (or envelope) monitoring
  2-level zones : warning and alarm
  Typically implemented on the control system (i.e. actually routinely used in accelerators)
“Modern” approach
  Data driven, machine learning
  Problem is often getting nominal data, tagged data
  Still on an R&D level : few examples of deployed ML-based anomaly detection routinely used in accelerator
    This is my impression, maybe this is NOT true  discussion

## Slide 8: Possible discussion points
Q1: Is anomaly detection a hot topic in your lab ?
  because of impact of faults on machine availability ?
  because of interest for promising results using machine learning techniques ?
Q2: What kind of architecture is in place to support ML-based anomaly categorization ?
  database ?
  integrated to control system ?
Q3: How is data labeled for ML-based anomaly detection ?
  Expert reviews trips and tags them
  First define catalogue then data is automatically tagged (“walks like a duck, quacks like a duck”…)
  Make use of additional knowledge (for example time constants, or additional interlock info) to best guess category and have expert confirm
Q4: What about predictive maintenance ?
  Often presented as the Holy Grail of anomaly detection, any experience ?
  “Don’t run touch a running system”  Is anyone actually doing preventive maintenance ?
Q5: anomaly detection is the first step towards reliability, what’s the next step?
  IMO, to really increase reliability, a careful review of every trip is necessary, followed by implementation of countermeasures
  How is this topic approached in your lab ?
Suggestions