## Slide 1: Controlling fusion plasmas with deep reinforcement learning
Jaemin Seo
Physics, Chung-Ang University

## Slide 2: Contents
Introduction
  Tokamak operation design
  Reinforcement learning (RL)
Surrogate model for the KSTAR tokamak
Tokamak operation design and control with RL
  Tokamak operation design with RL
  Tokamak operation control with RL
Summary

## Slide 3: Introduction – Tokamak vs Accelerator
Tokamak
Bulk fluids (Plasma)
keV-MeV
For nuclear fusion
Localized particles
~TeV
For collision
Accelerator
Both need control & optimization

## Slide 4: Introduction – Tokamak operation design
How have we achieved high performance in a tokamak?
Human trials and errors in tokamak experiments
Map
Guided by physics modeling
However,
Some phenomena are unpredictable by conventional modeling.
Hard to manually find the operation trajectory for every desired targets.
Therefore, let’s use AI to …
Predict a realistic plasma response in a tokamak.
Design operation trajectories for given physics objectives.
Data-driven simulator
AI operation design algorithm

## Slide 5: Introduction – Reinforcement learning (RL)
Deep reinforcement learning (RL) [1]
Environment
AI (RL agent)
Action
Observation,
Reward
Action | Bad | Good | Bad | Good | Good
Reward | -1 | +1 | -1 | +1 | +1
The AI takes actions that yield higher rewards.
It gradually learns the optimal decision-making policy.
Time
“Finding the best decision-making policy”
Difficulties of RL application in nuclear fusion research
RL requires a reliable training environment.
But we don’t have a perfect tokamak simulator.
RL typically needs simulation iterations to train.
But reliable theory-based simulation takes minutes to hours for a single step.
[1] V Mnih et al, Nature 518 (2015) 519

## Slide 6: Introduction – Spoiler
[1] J Seo et al, Nucl. Fusion 61 (2021) 106010
[2] J Seo et al, Nucl. Fusion 62 (2022) 086049
Make a fast surrogate environment
  We have 10-year exp data in KSTAR.
  So, let’s build a data-driven simulator!
Then, use RL for tokamak operation design/control
  On the simulator above, we trained an AI that controls the tokamak actuators to achieve given targets.
In this work,

## Slide 7: Contents
Introduction
  Tokamak operation design
  Reinforcement learning (RL)
Surrogate model for the KSTAR tokamak
Tokamak operation design and control with RL
  Tokamak operation design with RL
  Tokamak operation control with RL
Summary

## Slide 8: Surrogate model for the KSTAR tokamak
The need for data-driven simulator
In order for AI to explore the tokamak operation, we need a simulation environment.
Integrated modeling
Predict with integrated physics models
Physically interpretable
Limited by the model’s validity
Computationally costly and slow
vs
Data-driven model with DNN
Predict from patterns of the data
Black box
Experimentally relevant
Fast enough
The RL training needs simulation steps. → Fast data-driven model is adopted!
In this work, neural net models are trained with KSTAR experimental data.

## Slide 9: Surrogate model for the KSTAR tokamak
Idea
We have experimental data of both tokamak actuators and plasma responses.
Then, we can train the neural network that mimics the plasma response.
Plasma current, heating power, boundary shape, …
Plasma pressure (), safety factor (), internal inductance ()…
What we want to make: Predicting plasma states from actuators
Input
Output
Input
Output

## Slide 10: Surrogate model for the KSTAR tokamak
Prediction of plasma states
0.4 | 0.5 | 0.6 | 0.6
0.0 | 0.0 | 0.0 | 1.5
1.1 | 1.2 | 1.3
6.5 | 5.5 | 4.5
Plasma current,
Heating power,
Norm. beta,
Edge safety factor,
Tokamak control
Plasma states
?
Time
100 ms
We want a model that predicts the plasma responses by learning the pattern of the experimental data.
Plasma response is time-dependent. → RNN or LSTM (or Transformer soon)
0.4 | 0.5 | 0.6 | 0.6
0.0 | 0.0 | 0.0 | 1.5
?
0.6
1.5
1.7
4.3
0.4 | 0.5 | 0.6 | 0.6
0.0 | 0.0 | 0.0 | 1.5
?
0.6
1.5
0.6
0.0
1.1 | 1.2 | 1.3
6.5 | 5.5 | 4.5
1.7
4.3
1.9
4.3

## Slide 11: Surrogate model for the KSTAR tokamak
Neural network architecture
Geometry
Heating
Field variable
Previous state
Regression plot for testset

## Slide 12: Surrogate model for the KSTAR tokamak
Predictive simulation in KSTAR with the trained model
From the initial condition, the entire discharge can be sequentially predicted from the given actuator scenario.
The model successfully predicts the plasma evolution in different scenarios.
Given
Predict
True & Prediction

## Slide 13: Surrogate model for the KSTAR tokamak
Interactive GUI for predictive modeling
We can perform a virtual experiment in real-time.
Also can be used for the RL training environment.
https://github.com/jaem-seo/KSTAR_tokamak_simulator

## Slide 14: Contents
Introduction
  Tokamak operation design
  Reinforcement learning (RL)
Surrogate model for the KSTAR tokamak
Tokamak operation design and control with RL
  Tokamak operation design with RL
  Tokamak operation control with RL
Summary

## Slide 15: Tokamak operation design with RL
Idea
Now, we have a training environment for RL.
Then, we want an AI that designs a probable operation trajectory to achieve a target plasma state.
Ex) How do we operate a tokamak to achieve
at a given available heating condition ()?
Plasma current: 0.6 MA
Plasma boundary shape:
Goal
Constraints

## Slide 16: Tokamak operation design with RL
RL training for operation design
For the AI to interact with the simulator, we need to wrap it into a standard format, OpenAI Gym environment [1].
The AI was trained by TD3 [2] implementation from Stable Baselines [3].
Action
Observation
Reward
Action:
Observation: Previous action, , ,
Reward:
The closer to the target, the higher the reward is.
[1] G Brockman et al, ArXiv preprint, ArXiv1606.01540 (2016)
[2] S Fujimoto et al, 35th ICML (2018)
[3] A Hill et al, https://github.com/hill-a/stable-baselines (2018)

## Slide 17: Tokamak operation design with RL
Validation in the simulation
After enough training, the AI determines reasonable solution of and the boundary shape to reach the target of multiple parameters.
Reward
Before training
After training
https://github.com/jaem-seo/AI_tokamak_control

## Slide 18: Tokamak operation design with RL
Validation in the KSTAR experiment
The plasma response followed the preset targets.
However, actual shape controls were not perfect.
→ Control/diagnostics uncertainty should be reflected later.
Target setting

## Slide 19: Tokamak operation control with RL
Now, let’s try real-time control
After RL training, the AI can control the command signals for {shape} to track the time-varying targets.
It seems reasonable ( vs NBI / q95 vs shape).
Will be tested with different RL settings and constraints.
AI-determined plasma shape
AI-determined command signals
Target & plasma response
Target setting
https://github.com/jaem-seo/AI_tokamak_control

## Slide 20: Contents
Introduction
  Tokamak operation design
  Reinforcement learning (RL)
Surrogate model for the KSTAR tokamak
Tokamak operation design and control with RL
  Tokamak operation design with RL
  Tokamak operation control with RL
Summary

## Slide 21: Summary
1. Data-driven KSTAR simulator was developed, which is fast and experiment-relevant.
2. AI operation design algorithm was developed with RL, that provides an operation trajectory to achieve given targets.
3. RT feedback controller is being developed.
[1] J Seo et al, Nucl. Fusion 61 (2021) 106010
[2] J Seo et al, Nucl. Fusion 62 (2022) 086049
Before training
After training

## Slide 22: Thank you for your attention!