## Slide 1: Fast 6-Dimensional Phase Space Reconstructions using Generative Beam Distribution Models and Differentiable Beam Dynamics
Ryan Roussel
rroussel@slac.stanford.edu

## Slide 2: Modern Challenges in Beam Control
Beam shaping for high efficiency PWFA
C. A. Lindstrøm, et al. Phys. Rev. Lett. 126, 014801
Wijethunga, S. A. K., et al. NIMA 1051 (2023): 168194.
Magnetized beams for hadron cooling @ EIC
Flat beams for colliders
Free electron lasers
Marinelli, A., et al. Nature communications 6.1 (2015): 6369.
Chen, P., and K. Yokoya. (1991): 91-2.
Modern accelerator technologies require precise control over high dimensional beam structure
RMS quantities  Exact beam structure

## Slide 3: Measuring 6D Beam Distributions
Cathey, Brandon, et al. PRL 121.6 (2018): 064804.
Multiple scanning slits with dipole and bunch shape monitor @ SNS (ORNL)
5D tomography with polarizable X-band TDC @ ARES (DESY)
Jaster-Merz, S., et al Proc. IPAC’22 (2022): 279-283.

## Slide 4: Progress on Measuring 6D Beam Distributions
Cathey, Brandon, et al. PRL 121.6 (2018): 064804.
Multiple scanning slits with dipole and bunch shape monitor @ SNS (ORNL)
5D tomography with polarizable X-band TDC @ ARES (DESY)
960 measurements ~ 28 hrs
Tomographic reconstruction ~ 24 hrs
5 million (!) measurements ~ 32 hrs
Jaster-Merz, S., et al Proc. IPAC’22 (2022): 279-283.

## Slide 5: Why Is This So Difficult?
Costs of detailed beam representations
Histogramming scales poorly with number of dimensions,
Reasonable resolution,
For a 6D distribution, !
Information compression
2D image
1D projection(s)
Scalar values
Often required by analysis constraints (analytical tractability, optimization simplicity, etc.)
6D distribution

## Slide 6: Example: Quadrupole Scan @ AWA
Drive beamline

## Slide 7: Using Optimization to Reconstruct Distributions
Second order
beam moments
Analytical beam dynamics model

## Slide 8: The Road to Efficient 6D Reconstructions
(1) Parameterize complex 6D beam distributions using generative ML
(2) Implement differentiable beam dynamics simulations to enable learning

## Slide 9: Machine Learning Based Beam Representations
Use a generative machine learning model to create arbitrary beam distributions
O(~1000) parameters of the neural network control the distribution of particles in 6D phase space
Learn the NN parameters  learn the beam distribution
Example: arrange particles to make the SLAC logo

## Slide 10: The Road to Efficient 6D Reconstructions
(2) Implement differentiable beam dynamics simulations to enable learning

## Slide 11: Differentiable Beam Physics Simulations
Differentiable sims keep track of derivative information during every calculation step.
Enables cheap gradient evaluations which enable optimization of >10k free parameters.
Allows us to extract information from the individual pixels of an image.
Differentiable Beam Dynamics in Bmad-X
Gonzalez-Aguilera, J., et al. Proc. IPAC 23 (2023): 1725-1729.

## Slide 12: Generative Phase Space Reconstruction (GPSR)
Roussel, Ryan, et al. PRL (2023)
Now we can use gradient descent to optimize (train) beam parameters  necessary for learning O(~1000) parameters

## Slide 13: Transverse Beam Tomography @ AWA
Drive beamline

## Slide 14: AWA Reconstruction Results
Accurate 4D reconstructions using 10 measurements!
Reconstruction (training) time < 5 mins
No prior training data needed!!
Roussel, R, et al. PRL (2023)
Accurately predicts beam distributions outside the training set
Reproduces detailed beam features
Reconstructed
4D distribution

## Slide 15: 6D Phase Space Reconstruction (Test Beam)
Logical next step, combine 4D reconstructions from quad scans with single shot longitudinal phase space diagnostics
20 simulated measurements
Fully correlated test beam

## Slide 16: Reconstruction Results (Test Beam)
Successful reconstruction with 20 measurements, ~8 min computation time
Transverse-longitudinal phase space
Transverse phase space

## Slide 17: Preliminary Experimental Results from AWA
Training data

## Slide 18: Preliminary Experimental Results from AWA
Reconstruction predictions on test data

## Slide 19: Preliminary Experimental Results from AWA
Reconstructed 6D distribution
Measurement: ~8 mins
Training: ~8 mins
Roughly 100x faster than previous demonstrations
Temporal structure likely to laser homogenization optics
Magnetization due to solenoid focusing

## Slide 20: Conclusion
Generative modeling + differentiable physics simulations (GPSR)  substantial improvements in analysis capabilities
Experimental demonstration at AWA  reconstructions + analysis in ~ 15 mins
Enables better understanding of beam distributions in experiment  better wakefield accelerators, beams for colliders/cooling, better understanding of beam physics (CSR)
See next two talks by Juan Pablo and Seongyeol!

## Slide 21: Questions?
Thanks to the team!
SLAC
Auralee Edelen
Chris Mayes
Daniel Ratner
U. Chicago
Juan Pablo Gonzalez-Aguilera
Argonne Wakefield Accelerator
Seongyeol Kim
John Power
Eric Wisniewski
Wanming Liu
Alexander Ody

## Slide 22: Backup

## Slide 23: T-Scan Results

## Slide 24: Reconstruction Results (Gaussian Beam)

## Slide 25: Reconstruction Results (EEX Beam)