## Slide 1: Automation at CERN progress with CERN’s accelerator fleet
4th ICFA Beam Dynamics Workshop on ML for Particle Accelerators, Gyeongju, Korea 06. March 2024
A. Huschauer, V. Kain, M. Schenk, F. Velotti on behalf of the extended EPA community

## Slide 2: Contents
    Efficient Particle Accelerators project transforming machine operations
    Infrastructure frameworks & building blocks
    Status & results some highlights
    Outlook & conclusions timeline

## Slide 3: Motivation
Efficiency Think Tank
Question coming up repeatedly at CERN end-of-year workshops ‘21 & ‘22
How to best exploit the accelerator complex? in terms of efficiency, reproducibility, flexibility, and performance
Efficiency Think Tank (ETT) in 2023
7 strategic recommendations

## Slide 4: Efficient Particle Accelerators
From think-tank to project
ETT Efficient Particle Accelerators (EPA) project
Approved in autumn 2023 for a 5-year period
10 strongly interlinked work packages (WP)

## Slide 5: Efficient Particle Accelerators
From think-tank to project
Infrastructure evolution
ETT recommendations
ETT Efficient Particle Accelerators (EPA) project
Approved in autumn 2023 for a 5-year period
10 strongly interlinked work packages (WP)

## Slide 6: Contents
    Efficient Particle Accelerators project transforming machine operations
    Infrastructure frameworks & building blocks
    Status & results some highlights
    Outlook & conclusions timeline

## Slide 7: Infrastructure
Frameworks & building blocks
Machine Learning Platform Deployment & inference of (ML) models
Train, store & share ML models with VC
Language agnostic
Available in control room
Acc-Py “accelerating Python”
Full integration of Python with control system
Online data acquisition, equipment access (set / get), app development, …
Python package index
Classical automation concepts
EPA: sequencer 2.0, equipment testing, efficient settings management
Sequencer: programmatic execution of tasks
High-level parameter models
AccTesting
    GeOFF Generic Optimization Framework and Frontend
    acc-geoff4ucap Framework for optimization & control via UCAP
        Facilitate implementation of control problems
        Exploit & expose features of control architecture
        Maintain uniformity across complex
    Auto-pilots & optimizers
    UCAP Unified Controls Acquisition & Processing
Virtual device service
Event-based, online data transformations
Further evolution with EPA
Enabling automation with AI / ML

## Slide 8: Infrastructure
Frameworks & building blocks
Machine Learning Platform Deployment & inference of (ML) models
Train, store & share ML models with VC
Language agnostic
Available in control room
Classical automation concepts
EPA: sequencer 2.0, equipment testing, efficient settings management
Sequencer: programmatic execution of tasks
High-level parameter models
AccTesting
    GeOFF Generic Optimization Framework and Frontend
    acc-geoff4ucap Framework for optimization & control via UCAP
    Auto-pilots & optimizers
    UCAP Unified Controls Acquisition & Processing
Virtual device service
Event-based, online data transformations
Further evolution with EPA
Enabling automation with AI / ML
        Facilitate implementation of control problems
        Exploit & expose features of control architecture
        Maintain uniformity across complex
Acc-Py “accelerating Python”
Full integration of Python with control system
Online data acquisition, equipment access (set / get), app development, …
Python package index

## Slide 9: Infrastructure
Acquire
UCAP & acc-geoff4ucap
UCAP
Framework & service to implement & run online data processing pipelines
Transform
Publish
Subscribe to data sources
Group data via EventBuilder
Process incoming data
Java or Python
GPU support
Publish results
Can be hardware “sets”
UCAP pipelines can be chained and built into hierarchies
Conceptually simple, and very powerful

## Slide 10: Infrastructure
UCAP & acc-geoff4ucap
Acquire
Transform
Publish
Subscribe to data sources
Group data via EventBuilder
Process incoming data
Java or Python
GPU support
acc-geoff4ucap
Use UCAP to implement the optimization / control loop on server
Great infrastructure to run auto-pilots continuous controllers or auto-launching optimizers
UCAP
Framework & service to implement & run online data processing pipelines
Publish results
Can be hardware “sets”
UCAP pipelines can be chained and built into hierarchies
Conceptually simple, and very powerful

## Slide 11: Contents
    Efficient Particle Accelerators project transforming machine operations
    Infrastructure frameworks & building blocks
    Status & results some highlights
    Outlook & conclusions timeline

## Slide 12: Status & results
EPA: ETT recommendations

## Slide 13: Status & results
Supercycle (SC): sequence of beam types / cycles played over and over
Programming SC is a constrained scheduling problem Constraints: some beams cannot be adjacent, respect priorities, etc.
Manually defining SC has severe impact on efficiency & OP resources Stats: SC change takes 2 - 25 min; 40 - 60 x / 24 h
Plans
  2024: template SC with placeholders to be filled in automatically
  2025: no programmed SC; schedule beams “as we go”
  Eventually: dynamic cycle length (“play beams only for time needed”)
WP1: Dynamic beam scheduling
Notes: multi-destination machines
mention google OR-tools

## Slide 14: Status & results
EPA: ETT recommendations

## Slide 15: Status & results
Auto-pilots & optimizers are all across the injector complex
2023
  Many automatic solutions (20+ problems) in place and used in commissioning & day-to-day operation
  Plenty new ones under development
Trend 2024: from on-demand to continuous control infrastructure is key (UCAP)
Until end of Run 3: implement auto-pilots for remaining control problems in standard operation
Incomplete overview of auto-pilots and optimizers

## Slide 16: Status & results
Auto-pilots: a selection
  Automatic drift compensation
  Successfully tested and tuned in MDs with controllers on UCAP
  Hybrid agent: continuous controller interleaved with optimizer when far off
  Upcoming operational test
PS Multi-Turn Extraction
ES
BOBYQA
ES
supercycle change
    Versatile objective Beam position, beam loss, …
    Generic settings & actors
    Various algorithms incl. Micado / SVD
    In 2024: PS2SPS, SPS2LHC
  Trajectory steering framework using acc-geoff4ucap
G. Trad, F. Velotti
PS EAST: fixed target beam steering
  PID regulator on UCAP
  Simple & effective
  2024: integrate with acc-geoff4ucap
  Similar controller for TL towards AD
J. McCarthy
A. Huschauer, M. Schenk, C. Uden

## Slide 17: Status & results
Auto-pilots: spill noise cancellation
2022: auto-launching numerical optimizer
  Effective for 50 Hz, but not for 100 Hz
  Phases of strong exploration
2023: continuous control & empty bucket channeling
  Adaptive Bayesian optimization (ABO) a spatio-temporal GP model
  Improvements throughout the run (UCAP GPU, EBC)
  Well within objective
  Occasional exploration spikes: use proximal biasing in 2024
P. Arrutia, V. Kain, M. Schenk, F. Velotti
SPS slow-extracted beam current has 50 Hz & 100 Hz noise originating from quadrupole power converter ripple

## Slide 18: Status & results
Reinforcement learning: a selection
Correct RF phase & voltage for uniform bunch splitting (LHC beams)
Successful sim2real & fully operational
Multi-agent (SAC) & CNN for initial guess
Next: continuous controller (UCAP)
PS
PhD project (B. Rodriguez): control LINAC3 cavities for optimal injection efficiency into LEIR
RL state based on VAE-encoded Schottky spectra
Agent trained on data-driven dynamics model
LINAC3 / LEIR
V. Kain, N. Madysa
Steer DC beams in TT20 TL using split-foil secondary emission monitors
Works well in simulations, with noise and varying emittances
Ready for sim2real test
SPS
N. Bruchon, V. Kain
Adjust fine delays of SPS injection kicker
RL agent (PPO) trained on data-driven dynamics model
Ready for sim2real test
PS to SPS
M. Remta, F. Velotti
A. Lasheen, J. Wulff

## Slide 19: Status & results
Enhanced diagnostics: ML tomoscope in LHC
Tomographic bunch-by-bunch reconstruction in the LHC using auto-encoder ensemble
Not possible without ML
Fully operational and using Machine Learning Platform (MLP)
Ready to be used in the control room to measure injection errors

## Slide 20: Status & results
EPA: ETT recommendations

## Slide 21: Status & results
WP4: Hysteresis compensation
Feed-forward correction to provide reproducible magnetic fields
  Saving cost & time
  Reproducible beams & slow-extraction spills
  Flexibility: dynamic beam scheduling
PhD project: PoC at SPS (A. Lu, V. Kain)
Progress
  First Phy-LSTM & Transformer models trained on main dipole data
  Inference and trim pipeline successfully tested in the control room
Outlook & challenges
  Generalizability & accuracy of model
  Further magnet measurements in lab and multipole modelling
A. Lu, V. Kain, V. Di Capua

## Slide 22: Status & results
EPA: ETT recommendations

## Slide 23: Status & results
WP8: Automate equipment
Define new paradigm of smart and agile equipment e.g. aware of beam parameters, machine state, etc.
automate setup, fault analysis, and recovery
Plans 2024 & 2025
  Pilot implementations of parts of a new equipment automation framework
  Example: safe auto-resets following SPS kicker vacuum interlocks
Plans 2026 – 2028 (LS3): implement entire framework
Example: auto-reset of SPS kicker following vacuum interlock
VAE for anomaly detection from vaccum pressure data
Make sure to check out Francesco’s poster!

## Slide 24: Contents
    Efficient Particle Accelerators project transforming machine operations
    Infrastructure frameworks & building blocks
    Status & results some highlights
    Outlook & conclusions timeline

## Slide 25: Outlook
EPA project timeline
EPA: time-bound project for 5 years to have improvements ready for Run 4 starting in 2029
2 phases
  Prototyping & first operational tests in Run 3
  Full implementation during LS3 and sequential commissioning in Run 4
Today
End Run 3
Start Run 4
EPA timeline

## Slide 26: Conclusions
Efficient Particle Accelerators project put in place to systematically transform how we run the accelerator complex
Work has actually started several years ago and we have seen numerous improvements
CERN infrastructure is already in very good shape
  Continuous development has been crucial
  Most building blocks are available
EPA has 5 years to address further efficiency bottlenecks through
  systematic automation of accelerator operation & equipment
  improving efficiency of operations through models
  integrating AI / ML solutions at scale
Thank you

## Slide 27: References
A. Huschauer, V. Kain, K. Papastergiou, F. Velotti, ETT report, 2023.
CERN Joint Accelerator Performance Workshop, Montreux, Switzerland, 2023.
CERN LHC Performance Workshop, Chamonix, France, 2024.
D. Anderson et al., “The AccTesting Framework: an extensible framework for accelerator commissioning and systematic testing”, ICALEPCS’13, California, 2013.
L. Cseppento, M. Buttner, “UCAP: A FRAMEWORK FOR ACCELERATOR CONTROLS DATA PROCESSING @ CERN”, ICALEPCS’21, China, 2021.
A. G. Wilson and R. P. Adams, “Gaussian Process Kernels for Pattern Discovery and Extrapolation”, PMLR 28(3):1067-1075, Georgia, 2013.
K. Iliakis et al., Longitudinal Beam Diagnostics and Phase Space Reconstruction in the LHC Using ML, 6th Inter-Experiment Machine Learning Workshop, CERN, Geneva, Switzerland, 2024.
HL-LHC commissioning long-term plan, Mar 2024.

## Slide 28
Backup

## Slide 29: Efficient Particle Accelerators project
CERN automation history
2018
    Optimizers, ML, …
    Learn models if not available
    Infrastructure: Python & frameworks
    Typically on-demand
2021 -
    Closing the loop: continuous control or auto-launch
    Infrastructure: server-based solutions
    Equipment: predictive maintenance, fault analysis, …
1980
    High-level parameter control
    Conditional sequencing of actions
Classical automation
Adding AI / ML
2006
    Reduce complexity through models LSA: high-level parameter models with hierarchies, value generation
    Sequencers, watchdogs & SW interlocks, classic control

## Slide 30: Efficient Particle Accelerators project
CERN automation history
2018
    Optimizers, ML, …
    Learn models if not available
    Infrastructure: Python & frameworks
    Typically on-demand
2021 -
    Closing the loop: continuous control or auto-launch
    Infrastructure: server-based solutions
    Equipment: predictive maintenance, fault analysis, …
1980
    High-level parameter control
    Conditional sequencing of actions
Classical automation
Adding AI / ML
2006
    Reduce complexity through models LSA: high-level parameter models with hierarchies, value generation
    Sequencers, watchdogs & SW interlocks, classic control
Key: building infrastructure to support full integration of AI / ML technologies into the control system

## Slide 31: Status & results
Hysteresis compensation
Model Predict hysteresis & eddy-current effects based on past
Integration Model deployment & integration into controls infrastructure
Data SPS B-Train (dipoles) & Lab (other multipoles)
  Provide reproducible magnetic fields for every cycle through feed-forward correction
  Challenge: 2.5 s to calculate & apply trim before next cycle starts
  PhyLSTM: physics-inspired loss function
  Transformers: powerful, but data hungry & compute-intensive (see tutorial by A. Lu)
  Challenge: achieving sub-Gauss accuracy
A. Lu, V. Kain, V. Di Capua
  OP-parasitic: abundant, but lacking variability
  extend dataset by varying supercycles
  Outlook: measure multipoles in lab
  Challenges: pre-processing & securing adequate data variability

## Slide 32: Efficient Particle Accelerators project
Work packages
Remove fixed supercycles by algorithmically & dynamically scheduling beams
Automate & standardise beam preparation in injectors and LHC filling; Reduce impact on fixed target users and LHC turn-around time. Requires: orchestration of task sequences, auto-pilots, beam quality metrics
Automate parameter optimisation & automatically contain drifts
Deterministic magnetic field control with the aim of decoupling cycles
AccTesting for “all” equipment for injectors & LHC to automate hardware commissioning
Automation of equipment setup, fault analysis, and recovery; preparing the grounds for preventive maintenance