## Slide 1: From Physics Study to Operations: The Road to Production ML-Driven Beam Loss Optimization
C. Elliott, W. Blokland, D. Brown, B. Cathey, G. Gallimore, A. Kasparian*, B. Maldonado Puente, C. Peters,
K. Rajput*, K. Ruisard, J. Rye, M. Schram*, A. Shishlo,
S. Thomas, A. Zhukov

## Slide 2
Motivation
  Spallation Neutron Source Facility
  Impact of Beam Loss on SNS
  Operator Perspective
  Automated Beam Loss Tuning (ABLT)
Beam Loss Optimization(BLO)
  DOE Grant Information
  BLO Use-Case
  Deployment Plan
  Software Integration
  CER Upgrades
Future Plans

## Slide 3: Most Intense Pulsed Neutron Source in the World
The Spallation Neutron Source (SNS)
  1.3 GeV, 2.8 MW, 60 Hz
  Normal & superconducting Linac accelerates H-
  Accumulator ring and carbon foil strip H- to p+
  1000:1 pulse compression from Linac to Target
  Neutron production (NP) for users 4600 hrs/yr
FRONT END
LINAC
HEBT
RING
RTBT
Liquid Hg Target
+
-
-
+
-
-
+
-
-
+
Electron Stripping
+
+
+
-
-
+
-
-
+
-
-
+
-
-
Waste Beam Dump

## Slide 4: SNS Design Didn’t Match Observations
Designed for 0 loss in Superconducting Linac (SCL)
  Large aperture
  High vacuum
Unexpected H- beam loss mechanisms observed
  Intrabeam stripping: inelastic scattering of H-
  IBST occurs when ϵ is small
  Reduce quad gradients from design
H−
P+
(Shishlo et.al)
https://doi.org/10.1103/PhysRevLett.108.114801
Normalized Loss
Peak Current

## Slide 5: Simulated Transmission through Warm Linac
Simulation of Each cavity Phase & Amplitude 2D Scan
We changed amplitudes and phases 14 cavities one by one
For each cavity, all downstream ones were tuned according to design
100,000 macro-particles at the MEBT entrance with design Twiss
Transmission was simulated to the end of warm linac
MEBT1
DTL1
CCL1
Simulation shows both the design and final settings have no loss.
Model isn’t accurate enough to predict losses seen
Black region is not lossless in reality, but we can explore it
(B. Cathey, A. Shishlo)

## Slide 6: How Did We Adapt?
H- beam loss activation
  DR > 1 Rem/hr : must maintain positive access control
  Longer cooldown times
Must address continuous loss, prompt loss
Mitigated through:
  Scraping and collimation
  Equipment modifications
  Hand Tuning
  Tracking faults
Trip Length
Frequency per day
Beam Power Operating Hours

## Slide 7: Operations Impact
Want loss profile that is:
  Well-below trip limits
    Minimize spurious trips
    Free up operators for other duties
  Robust to “drift”
    Due to humidity, equipment, etc.
    Reduce daily hand-tuning
  Resilient to power ramp-up in coming years (2 MW by 2027)

## Slide 8: Hand Tuning is an Art
Time-consuming nature introduces human error
Cannot be easily taught

## Slide 9: Automated Beam Loss Tuning (Pre-ML) in Python
Constraints to Run During NP
  Op. Constraints: beam current & centering on injection dump, beam size and centering on target, power on target, beam orbit and trajectory into Ring
  Safety Constraints: safe windows, step sizes from experts; save as defaults
  Terminates if violating user-defined BLM limits
  Terminate for unexplained Machine Protection System (MPS) faults
  Lock one instance of script running at one time
  Approval from ACCC to run at 60 Hz for 24 hrs (08/14/2023); No trips!
  Metric: Loss data, expected activation data (correlated to loss signal using historical survey data)
  Actuators: Shift RF cavity settings and quadrupole magnet currents
  Save explored settings & diagnostic readbacks to HDF5 file
    Current Monitors (BCM), RMS H and V beam profiles upstream of Target, Position Monitors (BPM) in the HEBT, Humidity
  Orbit correction happening in parallel
Optimize & Maintain Low Losses
Real-Time Optimization during NP – safeguards are critical!
Notes: Organize left side into “goals” and “constraints”

## Slide 10: Automated Beam Loss Tuning
(J. Rye)
Estimated Activation

## Slide 11: Data Analysis, 1D Scans
RF Phase Changing
Beam Loss Monitor
(S. Thomas)

## Slide 12
Motivation
  Spallation Neutron Source Facility
  Impact of Beam Loss on SNS
  Operator Perspective
  Automated Beam Loss Tuning (ABLT)
Beam Loss Optimization(BLO)
  DOE Grant Information
  BLO Use-Case
  Deployment Plan
  Software Integration
  CER Upgrades
Future Plans

## Slide 13: “Machine Learning for Improvement in Accelerator and Target Performance” Renewed for up to 3 years
ORNL PI: Willem Blokland and JLAB PI: Malachi Schram
This is a continuation of previous grant, and the focus is now to bring ML into operations as opposed to offline analysis
Three use-cases:
  Beam Loss Optimization: Automatically minimize beam losses in real-time
  Target Anomaly Detection: Warn for anomalies and generate reports
  Errant Beam: Predict and prevent errant beam pulses
  (K. Rajput: “Machine Learning to Improve Accelerator Operations at SNS”)
(W. Blokland)

## Slide 14: BLO Use Case
AP physics model works with one bunch, doesn’t have halo details
Loss monitors see 1 ms pulse
Lead: Alexander Zhukov
Goal: Reduce beam losses using Reinforcement Learning
Sensors: 267 Loss Monitors
Actuators: 111 RF Cavities, 335 Magnets
Approach: Use virtual accelerator and safety limits to test safety of algorithms
Metrics: Reduce tune-up time by 50% Reduce activation < 100 mRem/h
Activation (mRem/hr)
(W. Blokland)
Position Along SCL

## Slide 15: Tools
List of Tools
Tool | Description
Python | Used for Virtual Accelerator (VA) and ScanEngine
PyORBIT3 | Particle-In-Cell accelerator physics code
EPICS | Used for VA and ScanEngine
HDF5 | Scan file format
SciOptControlToolkit (Jefferson Lab) | ML Side; Specific techniques/methods to come
(A. Zhukov)

## Slide 16: Software Integration – Configuration 1
ScanEngine
SciOptControl Toolkit
Proxy Server with safe limits
Virtual
Accelerator
Safe stepping, monitoring BLMs from ABLT
Proxy
Use
Test interaction between proxy server and control policy safely using VA

## Slide 17: Software Integration – Configuration 2
ScanEngine
SciOptControl
Toolkit
PyORBIT/Virtual
Accelerator
Control policy
Virtual Accelerator
SciOptControlToolkit
Use
Bypass proxy server to scale up training

## Slide 18: Software Integration – Production Configuration
ScanEngine
SciOptControl Toolkit
Proxy Server with safe limits
SNS
Use:
In NP on accelerator network
Need to define administrative boundaries for new approvals

## Slide 19: Infrastructure Overview
ML Server
Storage
Data
Edge computer
Data compression and buffer
Real-time Model inference
Display results
Data Acquisition
Acquire data
Model inference
Inference Results
Operator
View results
Operate models
Stop / Pause
Rollback to previous model
SNS Servers
Train and test model
Store data
GitLab
GitLab
Code repository
Actions
  Verify new code
  Deploy
New Model
New Model
ORNL Servers
GitLab
Icarus
Developer
Scripts
GUIs
MLFlow
(W. Blokland)
SciOptControlToolkit
SNS / VA
Proxy Server

## Slide 20: Deliverables
Deliverable | When
VA Environment | Spring 2024
IPAC paper/poster on VA | Spring-Summer 2024
Software framework to run safe scan during production | Summer 2024
Preliminary quantitative data with comparison of different techniques for reduced number of setpoints (10 knobs, 26 BLMs) | Spring 2025
VA to include some loss modeling (From AP or empirical findings) | Spring 2025
Expansion of parameter space to full SCL | Winter 2026
Working Automated procedure that reduces loss during production | Summer 2026
Publication ML Based Adaptive Accelerator Beam Loss Tuning | Fall 2026
(A. Zhukov)

## Slide 21: Hardware Installation Progress
8 Nvidia GPUs purchased and delivered
Modifications to central equipment room to support
  (2) 208V, three-phase, 60A receptacle circuits to rack 04CER01, and new 60A 3 pole breakers to support circuits
  Near completion

## Slide 22: Moving Forward into FY24B
Compare ML techniques to find best for our usecase
Incorporate loss-modeling into Virtual Accelerator
Expand to full parameter space
Deploy working CCR tool
Clean up integration code / Running example
Proxy server integration
Test on ICS, small subset, during Accelerator Physics study (low power)
Test on ICS, small subset, at 60 Hz full power
In the next three years….

## Slide 23: Acknowledgements
BLO Team for their invaluable input and contributions,
Accelerator Physicists for their work studying beam dynamics,
ORNL, JLab, and DOE for supporting this project,
supportive management for this opportunity,
the Scientific and Local Organizing Committees for ICFA 2024.
Thank you! 정말 고마워요

## Slide 24: References
First Observation of Intrabeam Stripping of Negative Hydrogen in a Superconducting Linear Accelerator (A. Shishlo, J. Galambos, A. Aleksandrov, V. Lebedev, and M. Plum, Phys. Rev. Lett. 108, 114801 12 March 2012)
ML Physics Presentation for BLO Use Case (B. Cathey, A. Shishlo, Machine Learning Kick-off Meeting, 9 Nov 2023)
BLO Use Case Overview (S. Zhukov, Machine Learning Kick-off Meeting, 9 Nov 2023)

## Slide 25: Additional Slides
ABLT
Analysis
ScanEngine
More Physics Slides
More Details on BLO Use Case

## Slide 26: Design vs. Production Settings in RF Cavities
Cavity | Design φsynch deg | Real φsynch deg | ARF/ARF Design %
MEBT 1 | -90.0 | -100.6 | 145
MEBT 2 | -90.0 | -85.6 | 131
MEBT 3 | -90.0 | -103.5 | 132
MEBT 4 | -90.0 | -91.6 | 129
DTL 1 | -45.0 | -43.6 | 106
DTL 2 | -33.4 | -44.4 | 103
DTL 3 | -32.4 | -19.6 | 99
DTL 4 | -31.7 | -30.7 | 101
DTL 5 | -31.7 | -25.2 | 92
DTL 6 | -34.0 | -34.4 | 97
CCL 1 | -30.9 | -16.7 | 93
CCL 2 | -30.8 | -21.6 | 95
CCL 3 | -30.7 | -23.9 | 98
CCL 4 | -29.3 | -18.3 | 93
Data on Feb. 7, 2021, 1.4 MW
RF Cavities are initially designed using the model with no beam loss
Operators then change the cavity settings to minimize beam loss
These final settings can be far from the design settings
Models aren’t predicting this beam loss
(B. Cathey, A. Shishlo)

## Slide 27: Beam Halo
Beam Halo is defined as particles far outside of the main beam
  Not well defined
  Formed from space-charge self forces
Current models fail to predict its formation
  Halo Twiss can be significantly different from core Twiss
  The Beam Test Facility at SNS is currently looking into this
Horizontal phase space at the SNS Linac exit showing beam halo
A. Aleksandrov, S. Cousineau, and K. Ruisard, “Understanding beam distributions in hadron linacs in the presence of space charge”
(B. Cathey, A. Shishlo)

## Slide 28: Data In
Sensor | Type | Repeatability | Storage
Beam Loss Monitors | timeseries, 60 pulse array | Yes | Scan files on BIGMAC
Beam Position Monitors | 60 pulse array, average scalars | Yes | Files on errant-beam
Slow environmental parameters: temperature etc. | scalars |  | EPICS archiver
Input Details
(A. Zhukov)

## Slide 29: Tools
List of Tools
Tool | Description
Python | Used for VA and scanning script
PyORBIT3 | PIC accelerator physics code
EPICS | Used for VA and scanning script
HDF5 | Scan file format
ML | Specific techniques/methods to come
(A. Zhukov)

## Slide 30: Model and Dynamics
Dynamics
Do you have | Yes/No | If yes, explain | If no, what is missing | Comments
Physics model | Yes but | There are accelerator physics models | Losses are not explained by it | Might not use it
Record relevant settings | Yes | Beam configuration settings are saved | There might be other relevant events that change data | Concept/data Drift
Simulation Model | Yes | Virtual Accelerator based on PyORBIT3 (PIC code) | Can not model loss data | Will be used for testing scanning procedures
Stable | Yes | BLM and BPM data are stable |  | 
Disturbances | No? |  |  | 
How to optimize |  |  |  | 
Tuning Procedure | Yes | Manual | Smart automation not affecting production | 
(A. Zhukov)

## Slide 31: Objectives and approaches
List of objectives and approaches
Objective | Approach
Identify critical control variables for loss minimization | Online (during scan) correlation analysis
Determine the duration of scan allowing the model to learn and guide subsequent tuning | 
Determine what percentage of loss reduction is achievable | 
(A. Zhukov)

## Slide 32: Challenges
List of Challenges
Challenge | Approach | Backup
Administrative Control | Framework controlling all changes to machine independent from ML algorithm | None
Reasonable trade-offs while relaxing constraints | Revisiting limits in SCL with all parties involved | Operate within existing unnecessary tight limits
Unstable performance (especially for tuning phase) |  | 
Quantification of the results |  | 
Need to run in production for relevant data
Safe non-intrusive operations required
(A. Zhukov)

## Slide 33: BLO Overview
Kick-off
Framework development
Virtual accelerator
Objectives
Approaches
Plan
Final
ML methods comparison
Control Room Integration
Develop VA
Test with VA
??
Full scale tool running in CCR
Report
Test with AP beam
Test with production beam
??
NIM publication
Tasks
Action Items
Notes
Timeline
Year 1
Year 2
Year 3
Full parameter space
Virtual Accelerator Environment
Software framework
Technique Comparison
Year 1
Year 2
Year 3
Publication: NIM
Highlight Slide
Results
Deliverables
VA loss modeling
Working CCR tool
(S. Zhukov)