## Slide 1: TwinCAT Introduction Hands on Session
Anders Sandström
Electronics Engineer
www.europeanspallationsource.se
14 November 2016

## Slide 2: Outline
TwinCAT overview
Runtime
Engineering Tool
License system
Data Links
Control Loops (Motion)
Configuration
FB_DriveVirtual
Hands on session

## Slide 3: TwinCAT Overview
TwinCAT:
“Soft PLC” system
Runs on/under Windows systems
Two generations available:
  TwinCAT 2.x
  TwinCAT 3.x
Notes: https://download.beckhoff.com/download/document/catalog/Beckhoff_TwinCAT3_042012_e.pdf

## Slide 4: TwinCAT 3.1 XAR (Runtime)
XAR : eXtended Automation Runtime
Real time environment
PLC
Motion
..
Notes: https://download.beckhoff.com/download/document/catalog/Beckhoff_TwinCAT3_042012_e.pdf

## Slide 5: TwinCAT 3.1 XAE (Engineering tool)
XAE : eXtended Automation Engineering:
Integrated into Visual Studio®
support for the native Visual Studio® interfaces (e.g. connection to source code management systems)
IEC 61131-3 languages (with object oriented extensions), Structured Text (ST), Function Block Diagram (FBD)
C++ support (with debugger)
Integration with Matlab Simulink possible (Matlab Simulink coder)
Possibility for .NET projects in the same solution (e.g. for HMI)
Safety editor
Motion libraries (PLC-Open compliant)
…
Notes: https://download.beckhoff.com/download/document/catalog/Beckhoff_TwinCAT3_042012_e.pdf

## Slide 6: Engineering Tool: Overview
Notes: Explain different windows

## Slide 7: Software “management”
Highest level in solution explorer tree is “Solution”
A solution can contain several projects.
Project types:
  C# (non realtime)
  TwinCAT (realtime)
  C++
  ..
A TwinCAT Project can contain source code and configurations (hardware and other)

## Slide 8: Motion

## Slide 9: System

## Slide 10: Motion

## Slide 11: PLC

## Slide 12: Safety

## Slide 13: C++

## Slide 14: I/O

## Slide 15: Application Control/Status

## Slide 16: License System
Engineering tool is free
Runtime licenses are needed.
  Runtime licenses are needed for functionalities:
    PLC
    Motion
    HMI
    Connectivity
    C++
    …
  License costs are related to performance of CPU (performance classes)
1 week trial licenses can be generated (unlimited number of times).
Example:
  Our test crate needs licenses for approx. 700Eur (including Windows license and 8 axes)
Notes: Licenses also need a lot of administartion…
Trial licence convieneient since you can test evetything and then se which licences you need.
https://download.beckhoff.com/download/document/catalog/Beckhoff_TwinCAT3_042012_e.pdf

## Slide 17: Data Links
Data exchange between different modules are done through “data links”
Example:
  Digital inputs, or other I/O, can be linked to a PLC variable
  A motion axis can be linked to an amplifier, encoder and PLC program.
Pros:
  Nice way to separate hardware from software
Cons:
  Can be a lot of work to link variables
  Easy to make mistakes (link wrong variables)

## Slide 18: Motion Data Links
Link hardware to Axis
Link Axis to PLC
Hardware
Motion
PLC

## Slide 19: Motion Control Loops
Current Control Loop:
  Needed for both open and closed loop setups (however depends on actuator)
  Functionality depends on motor type (phase shift output for commutation)
  Current is related to torque via the motor KT constant for rotary motors or to a force for linear motors.
  Common sample rate range: 10-50kHz
  Type: PI controller (maybe filters, observer)
Velocity Control Loop:
  Needed for closed loop, sometimes used for open loop (frequency control)
  Common sample rate range: 1-10kHz
  Type: PI controller
Position Control Loop:
  Needed for closed loop, sometimes used for open loop (for consistency)
  Common sample rate range100-5kHz
  Type: P or PI controller (if P the stationary error will be handled by velocity PI)

## Slide 20: Motion Control Loops
P(ID)Position
SPPosition
PVPosition
OPosition
SPSpeed =FFSpeed
PVSpeed
FFI
+
+
+
-
-
+
+
+
PI(D)Speed
Speed Control
Position Control
SPPosition Position setpoint
OPosition Position offset
PVPosition Actual position
SPSpeed Speed Setpoint
FFspeed Speed feed forward
PVSpeed Actual speed
PI(D)I
Process
Current Control
Mech., motor, feedback

## Slide 21: Control Loop Execution Options
Act. position
Position setp.
Act. position
Velocity setp.
Act. position
Torque setp.
CSP-Mode
Cyclic Sync. Position
CSV-Mode
Cyclic Sync. Velocity
Control:
Pos.
Velo.
Torque
Control:
Velo.
Torque
- Trajectory gen.
- No control
-Trajectory gen.
-Position cont.
-Trajectory gen.
-Position cont.
-Velocity cont.
Control:
Torque
Amplifier
Level
Controller: No loops needed
Drive: All control loops
Controller: Position loop
Drive: Velocity and current loop
Controller: Position, velocity loop
Drive: Current loop
CST-Mode
Cyclic Sync. Torque
Notes: Also position interface.. Where traj is made in card! Good for open loop..

## Slide 22: One more alternative…
Act. position
Position target position.
Positioning Interface
Control:
Trajectory gen.
Pos.
Velo.
Torque
- No control
Amplifier
Level
Controller: No loops needed
Drive: All control loops and trajectory generator
Useful for open loop
stepper or for use when encoder is connected to local terminal.
Notes: Also position interface.. Where traj is made in card! Good for open loop..
No need for axis

## Slide 23: Configuration
Motion settings are made in Solution Explorer under “Motion” and in the actual I/O terminal.
Notes: When running BLDC many settings are automatic. Steppers need some settings

## Slide 24: Important Configurations
I/O card (important parameters start at CoE 0x8000):
Maximum current
Motor Voltage
Steps/rev
(Encoder resolution)
(Controller parameters)
(Modes)
Motion Axis (Settings for Controller):
Scale factors
Dynamics (acceleration, deceleration, jerk)
Velocities (max, manual, referencing)
Control parameter(s)
Notes: When running BLDC many settings are automatic. Steppers need some settings

## Slide 25: Feed Forward and Trajectory
P(ID)Position
PI(D)Speed
PI(D)I (torque)
Process
+
+
Already known changes can be fed forward. The error for the controller to handle will be less. Scaling of velocity feed forward is made through the “Reference speed” parameter in the TwinCAT motion axis.

## Slide 26: Feed Forward
Target position
Actual position
Position Controller output
Time
Position / Output
Trajectory generator set-point
Feed Forward output (to speed PID)
26
Time
Position / Output
No Feed Forward
Feed Forward
Already known changes can be fed forward to increase performance.
The error for the controller to handle will be smaller.
Feed Forward handles
main part of the control
Position controller
only handles small
deviations

## Slide 27: FB_DriveVirtual
Function block that handles most common use cases:
  Absolute Positioning
  Relative Positioning
  Constant Velocity
  Homing/Referencing Procedures
  Jog
Implements EPCIS motor record functionalities

## Slide 28: FB_DriveVirtual Operation
bEnable: Amplifier On/Off
nCommand: Defines commands
  0 = Jog
  1 = Constant Velocity
  2 = Relative Positioning
  3 = Absolute Positioning
  10 = Homing/Referencing procedures
nCmdData: Parameter to nCommand
  Example: For nCommand = 10, the nCmdData specifies which procedure to use.
fPosition: Target position
fVelocity: Target velocity
bExecute (Execute new command on rising edge)

## Slide 29: FB_DriveVirtual Example
Absolute positioning to a target position of 100 with a target velocity of 200.
bEnable = 1 (Amplifier On)
nCommand = 3 (Absolute Positioning)
nCmdData = 0 (not used for nCommand =3)
fPosition = 100
fVelocity =200
bExecute = 0
bExecute = 1 (Positive Edge)
Note: EPICS motor record model 3 driver is utilizing FB_DriveVirtual in the same way.
Notes: This is also how the motor record driver runs motion

## Slide 30: Hands on Session
www.europeanspallationsource.se
14 November 2016

## Slide 31: Hardware: Test Crates
19’’- 6HU – subcrate, depth 175mm
Different configurations for 1 or 2 axes
Standardized set of IOs per axis
Mechanics included
For both OS versions (W7/TwinCAT and Linux/Open Source)

## Slide 32: Hardware: CX5130 CPU
Embedded PC with Intel® Atom™ processor, 1.75 GHz, 2 cores (TC3: 40)
Flash memory slot for CFast card
Integrated 1-second UPS (1 MB persistent memory on CFast card)
Windows Embedded Standard 7 64 bit
3 network ports (2 RJ45 and 1 dedicated EtherCAT)
4 USB ports
DVI connection
Diagnostic LEDs (TwinCAT)
TwinCAT 3.1 Runtime installed
Licences (not all crates)

## Slide 33: Hardware: EL7037 Drive Card
2 phase stepper drive
24V, 1.5A
Incremental Encoder (TTL)
2 Inputs
Distributed clock
Modes:
  Open Loop (step counter)
  Closed Loop with encoder
  Vector Control (closed loop with current control)
Supported Control Modes:
  Cyclic Synchronous Position
  Cyclic Synchronous Velocity
  Positioning Interface

## Slide 34: Hardware: EL5101 Incremental Encoder
Differential Incremental Encoder Interface (A, A/, B, B/, C, C/)
1 Input
Distributed clock
Latch, Gate functionalities (can be used as inputs)

## Slide 35: Hardware: EL1018, EL2808 Digital Inputs
EL1018:
8 inputs
24V
10 micro seconds filter
EL2808:
8 Outputs
24V, 0.5A

## Slide 36: Power Concept

## Slide 37: Tasks
Get familiar with hardware
Signal testing
Commission one axis in open loop
Commission one axis in closed loop
Test debug HMI (visualization FB_DriveViz..)
More detailed instructions will be available in the lab.
GOOD LUCK!