## Slide 1
Transition to Phoebus at the Karlsruhe Institute of Technology
Edmund Blomley
Copyright M. Breig

## Slide 2: Outline
KIT accelerators
Current environment
Custom systems
Transition to Phoebus

## Slide 3: Location: Karlsruhe – Germany
OpenStreetMap.org

## Slide 4: Karlsruhe Research Accelerator (KARA)
KIT synchrotron light source & accelerator test facility
  until 2015 known as “ANKA“
Circumference: 110.4 m
Ramped storage ring: 0.5 - 2.5 GeV
Mostly “stable“ IOCs & panels
One week per month:
  Beam physics experiments and tests
  Very variable in energy, filing pattern, bunch current and operational condition
Image: U. Herberger
1 Hz injection at 0.5 GeV
accumulation for 30-45 minutes
energy ramp up to 2.5 GeV
beam decay for 23 hours
Default user operation

## Slide 5: Far-Infrared Linac and Test Experiment
50 MeV linear electron accelerator
Goal: Ultra short electron pulses (1-300 fs)
Panels and IOCs much more fluid
Overlap in panels, IOC support and general controls infrastructure
But separate network, building, operators and users

## Slide 6: Current Setup

## Slide 7: Controls Environment
EPICS 7
  IOCs mostly on virtual machines
(Historically) quite a few complex EPICS applications run in Java
  Example: Orbit correction
Recently more and more Python
  Including Python SoftIOC
Ubuntu LTS for all servers and terminals
Code repository: historically Subversion
  Migration to GitLab ongoing, using CI for automation
IT orchestration: Salt Project

## Slide 8: Control System Studio
Transition to EPICS started around 2012
  Control System Studio was chosen as the main GUI
Required to build our own CSS flavour
  Site specific settings
  Custom plugins
    Archiving system
    Save and restore system
    Alternative EPICS Java library (Jackie)
Building was quite complex, so did not update base version of CSS regularly
  Current CSS base version 4.1

## Slide 9: Software and Panel Distribution
Python Launcher
Office Binaries
Accelerator Binaries
KARA Panels
Shared Panels
FLUTE Panels
Python Launcher
FLUTE CSS
Office Binaries
Accelerator Binaries
Dev
Main
Archive
Alarm
Layouts
Custom
Dev
Main
Archive
Alarm
Custom
Layouts
download
download
include
include
start
KARA CSS
start

## Slide 10: Panels

## Slide 11: Panels

## Slide 12: Custom Tools

## Slide 13: Archiver
NoSQL Cassandra cluster
High data throughput for writing
CSS integration via custom JSON protocol
  Also Python module
Central archive configuration
  Monitor or scan
  Compression or no compression
  …
Making data available of 12+ years of operation

## Slide 14: Alarming
Due to very variable operational conditions for KARA we require a “dynamic“ alarm system
Certain states should only be an alarm depending on the operation state
  Example – injection kicker:
    If not on during injection -> ALARM
    If not off during ramping/operation -> ALARM
IOC independent alarm configuration
  Multiple configurations for one record, based on “status PV“ (operation state)
  Without additional effort also possible for embedded devices

## Slide 15: Alarming
EPICS Alarming
JAVA Alarming
CSS Alarming
Layer 1
Layer 2
Layer 3
Change record files
+
Restart IOC
Change XML files
+
Restart Java application
Run script to update alarm table
High risk during operation
Low risk during operation. Might confuse operator
No risk during operation

## Slide 16: Alarming
Centralised alarm configuration
Dynamic alarm state switching
Embedded and native IOCs managed in the same format
More flexible
  Complex summaries
Integrate non-EPICS alarms
  Ping alarm
Centralised alarm configuration
  Keeping alarms synchronised to IOC development
  Philosophy shift over time
Each alarm creates additional PV
  Panel integration?
Custom software layer
  Bugs
  Adds Java to the mix
  Scaling
  Maintenance
Pros
Cons

## Slide 17: Alarm Status Panel
Summary alarms
Also used for the launcher

## Slide 18: Save and Restore
Around 2013-2014 looking for a save and restore system
Also “track“ any operator change to machine parameters
  “So, what were all the changes made during last shift?”
View, compare and restore operator changes over any period of time
Set labels and defaults for groups of PVs
 Yet another custom solution with another (sql) database and external configuration

## Slide 19: Save and Restore
Custom CSS integration
Lots of custom code
Maintenance overhead, yet another external configuration
CSS Widget
CSS View

## Slide 20: Transition to Phoebus

## Slide 21: Transition to Phoebus
Use opportunity to re-evaluate current features
Try to rely on less custom code
Try to get necessary adjustments to Phoebus upstream from the beginning
Dockerize as much as possible
Use opportunity to add long-wanted features
  Channel Finder
  Highly available network storage for panels (but also autosave, layouts, etc.)

## Slide 22: Contributions to Phoebus Upstream
Support for alternative Java channel access library (merged)
  EPICS Jackie, can be used via jackie:// instead of ca://
  (Based on experience with lots of Java applications)
Support for JSON-Archive-Access-Protocol (merged)
  for Cassandra PV Archiver
Improvements to the menu bar in macOS (yet to be submitted)
Support for loading Mementos/layouts via URLs (planned)

## Slide 23: ChannelFinder and Alarm Server
Run in high availability Docker setup
Use more features of the Phoebus alarm server instead of custom Java server
  Summary alarms
ChannelFinder makes use of already existing infrastructure
  Each IOC already exports PV lists, filtered by some keywords
  Does not require additional IOC integration (no RecCaster)
  Meta data from IOC deployment
Add authentication
  Resources will be available in the office versions
  Added for ChannelFinder -> ElasticSearch
  tbd for alarm logger -> ElasticSearch

## Slide 24: Cross-Plattform-Builds for Native Launcher
jpackage allows to build native launcher
  but can only built for platform it is being used with
Core features of jpackage re-implemented in Python
Use GitLab CI to build for all platforms
  Using Linux Docker images
Limitations compared to jpackage:
  Slightly larger builds
  Currently not possible to create installer (but might be possible with external tools)
At the moment available only internally on our GitLab
  but can be shared if interest exists

## Slide 25: Next Steps
Panel transition
  Tests so far look promising, as only visual effects (and file handling) was done with JavaScript/Rules
Considerations for replacement of SNR system by using archiving data
  Current system cannot be used with Phoebus
  Use archiving interface and labeled timestamps instead
  Integrate into Phoebus upstream
Evaluation for alarming system
  Current system can still be used
  Remove additional alarm PVs, instead adjusting EPICS record alarm fields dynamically (using Python SoftIOC instead of Java)