## Slide 1: PV Browser - A Web Based EPICS PV Information Query System
Yuliang Zhang, Kangjia Xue
CSNS@IHEP
2024 Spring EPICS Collaboration Meeting, Pohang

## Slide 2: Brief Introduction of CSNS Operation and CSNS-II
25/50kW
80/100kW
100kW
100/125kW
140kW
140/160kW
CSNS is operating at 160kW beam power since March 2024
Total number of PVs accelerator only is about 100,000
Beam power ramp history
Beam time and availability

## Slide 3: Brief Introduction of CSNS Operation and CSNS-II
Beam power will be upgraded from 160kW to 500kW
Total number of PVs accelerator only will be 200,000+
SSC, 80MeV->300MeV
NEW：9 neutron beam line, 1 muon and 1 proton line
Parameters
CSNS
CSNS-II
Beam Power（KW）
Rep-Rate（Hz）
Beam Energy（GeV）
Avg Current (µA)
Linac Energy(MeV)
Linac Pk Current (mA)
Linac RF Frequency（MHz）
Linac Beam Width(µS）
New Injection System

## Slide 4: Accelerator Control System Upgrade Towards CSNS-II
EPICS V3 and V7 mixed control system
Total number of V3 and V7 IOCs will be more than 200

## Slide 5: Information we care about PV
Live Value
EPICS
PV
Historical Value
Put Log
Owner
Location
IP Address
Alarm State
Number of PV

## Slide 6: Information we care about PV
There are many tools to collect these information in EPICS community
Browsing these PV related information via web pages is more convenient

## Slide 7: Design of PV Browser
Front end：Vue.js framework +PrimeVue component library
Backend：Node.js and community existing tools

## Slide 8: PV List
Directory service tool ChannelFinder and EPICS record synchronizer tool RecSync
Web pages get PV record data from ChannelFinder service and ElasticSearch directly
PV list module

## Slide 9: PV List
PV List main page
List Data
Hist Data
Putlog
Network
PV name list, IOC name list, IOC IP list and PV detailed information can be showed in the main page
IOC List

## Slide 10: PV Live Data
PV Web Socket tool PVWS was adopted as the backend
Web page subscribes the PV live data and alarm state
PV Live data
PV live data module

## Slide 11: PV Historical Data
The EPICS Archiver Appliance supports data retrieval in multiple formats/MIME types. PV browser calls the in-built web service to show the historical data
PV Historical Data

## Slide 12: PV Putlog
Usually, CaPutLog module and iocLogServer were used to collect the PV put log , the Put log was stored in separated local files, it is hard to read
The content of iocLogServer log file

## Slide 13: PV Putlog
CaPutLog module and Logstash were adopted, the put log was saved into ElasticSearch
Web page gets PV put log from ElesticSearch
PV put log page
PV Put log module

## Slide 14: PV Alarm State
Pheobus kafka based alarm system was used
Web page get the active alarms directly from kafka
Active alarm page
The Phoebus kafka alarm system deployed at CSNS

## Slide 15: PV Alarm State
Alarm history page
Web page gets alarm history from the Phoebus alarm system in-built RESTful API

## Slide 16: IOC Status
IOC Status page
IOC status module
A python application periodically get the 1st PV of each IOC from ElasticSearch, and save to MongoDB
Get the value of these PVs via PVWS, if these PVs are all alive, then the IOCs are all alive

## Slide 17: IOC Status
From this page, more detailed PV information can be acquired
This page is useful after the long shutdown of the accelerator
IOC Status page

## Slide 18: IOC Network Information
The IOC detailed network information can also be queried
Operators can quickly get the related switch information
The detailed IOC network information

## Slide 19: IOC Network Information
List all the IP addresses used for EPICS IOCs, then we can go to the each of the IOC for the detailed information

## Slide 20: Deployment of PV Browser at CSNS
Proxy server Nginx was adopted to deploy the PV Browser
The system was deployed at CSNS accelerator in 2022. Now, it is frequently used by the operator
Accelerator Network
Campus Network

## Slide 21
Thank you for your attention!