## Slide 1: epics-containers
Pohang, April 2024
Supervised by Giles Knap & James O'Hea
Beamline Controls – Diamond Light Source

## Slide 2: epics-containers?
Applying modern industry practices for software delivery to EPICS IOCs
  ​Continuous Integration:
Kubernetes:​
Helm Charts:​
Repositories:
  Package IOC software and execute it in a lightweight virtual environment​
  Centrally orchestrates all IOCs at a facility​
  Deploy IOCs into Kubernetes with version management​
  Source and container repositories manage all the above assets
  Source repositories automatically build assets from source when updated
Containers:

## Slide 3
  IOCs are decoupled from the OS
    No modifying support modules to suit facility infrastructure
    Allows us to use upstream support modules with no need for local forks
    Develop and test anywhere
    Protection from many security vulnerabilities
  Simple server setup: any Linux + container runtime only.
    Very easy server OS upgrades
  Remove maintenance of internal management tools
  Kubernetes provides (not just for IOCs):
    Shared software deployment and management
    Shared Logging and monitoring
    Shared resource management: Disk / CPU / Memory
    Connect to IOC and interact with its shell
    IOC debugging
    Monitor IOC status
    Just Google it when things go wrong
Why?

## Slide 4: How?
/epics/
epics-base/
lib/
dbd/
bin/
configure/
support/
ADSimDetector
...
ioc.yaml
make a detector ...
make some plugins ...
Generic IOC Container Image
IOC Instance Description
Generic IOC Source Repo
Beamline IOC Instance Repo
Continuous integration
Continuous integration
values.yaml
image: image-URI
Running Container Instance
st.cmd
ioc.db
/epics/
ioc/
lib/
dbd/
bin/
configure/ ...
Notes: Container images are built by layering on top of existing images. EPICS base and essential tools are compiled into one image in what we call our Generic IOC image.
We mentioned continious integration - every published generic ioc image has a version number . When we release an image we tag it with a version number. In github and gitlab this causes Ci to build the source, publish the results and tag it with the same version number. At diamond we use githubactions for open source assets and gitlab CI for in diamond specific/ private assets.

## Slide 5
  ec – edge containers CLI for developers
    Runs outside the container
      Deploying, monitoring and managing IOC Instances
      Also used by Continuous Integration
      CLI tool is a wrapper around kubectl, Docker/podman, Helm and git - simplifies Bash Scripts
  ibek – IOC builder for EPICS and Kubernetes
    Runs inside the container at build time
      Helpers for building Support and Generic IOC in the container environment
    Runs inside the container at runtime startup
      Makes IOC instance startup script and database from a YAML description
Supporting Tools

## Slide 6: How to make an IOC Instance?
A helm chart values override file for the beamline helm chart. The only required field is the URL of the
Generic IOC to use.
An ibek IOC YAML file listing the support entities that we want to
instantiate for this IOC instance.
2. Deploy the IOC instance:
  Tag and push the beamline repo
  ec deploy bl45p-ea-ioc-01 2023.11.1
1. Create a beamline repo
  Using copier template
  add a subfolder to `services`
  create new IOC Instance config

## Slide 7: edge-containers-cli in action

## Slide 8: How to make a Generic IOC?
To make a new generic IOC add the additional support modules required to the template Dockerfile
2. Deploy Generic IOC to your container registry:
  Tag and push the generic IOC repo
  CI builds image
1. Create a Generic IOC repo
  using Copier template on GitHub
  edit Dockerfile and ReadMe

## Slide 9: How to Add a new Support Module
Install.sh example for ADSimDetector. Most install.sh would look identical to this but
You can add custom steps as
Needed.
2. Add a new install.sh file:
  Use the new support in your Generic IOC Dockerfile
1. Add a folder in the ibek-support repo
  Shared ibek-support on GitHub
  Or private ibek-support per facility

## Slide 10
Example of install.sh for ADAravis support module

## Slide 11: Need for Developer Containers
  Types of changes:
  Changing IOC instance
    Changing EPICS DB records
    Making changes to the IOC instance
  Changing the Generic IOC
    Altering how the Generic IOC container is built
    Changing EPICS version
    Adding new support module
  Changing the dependencies
    Sometimes you need to alter the support module used by Generic IOC
    New release of the support module
    Updating and publishing the Generic IOC
    Updating and publishing the IOC instance
Order of decreasing frequency of change but increasing complexity

## Slide 12: BL46p test rig "beamline in a box" and beamline K8S cluster
Pandabox
2 GigE cameras, 1 is detector and other is diagnostic camera
Delta Tau turbo clipper motion board + motor encoder and decoder
Kubernetes cluster on beamline IO3 – Cluster per beamline
However, BL46p's cluster is on Pollux – a namespace on a shared central cluster

## Slide 13: Containerising device on beamline: oxcs700
Cryostream device in IO3
  epics-modules does not have published support for oxcs700
  Took EPICS support and "de-dls-ify" to make an as generic as possible
  Added to ibek-support
  Created a generic IOC for device
  Testing in the near future

## Slide 14: The future: MXBridge and DLS wide
MX beamline 'out in the field' deployed at APS, Chicago during the Diamond-II upgrade dark period
  Early rollout of key components of Diamond-II beamline software stack
  Directly applicable for new flagship beamline K04 and I03, IO4 at later stage
  At its peak collecting 5,000 samples per day (K04 to peak with 10,000 samples per day with multi-sample pins)
  MXBrigde will test the future architecture for Diamond II beamlines

## Slide 15: Thanks for listening
  Thanks to Giles Knap for the slides and other materials
  For more information see
  https://github.com/epics-containers
    Tutorials
    Documentation
    Templates
    Source code
    Growing number of Generic IOC images