## Slide 1: Portable Channel Access Server for Node.js
Lin Wang
wanglin@ihep.ac.cn
Controls Group, Accelerator System Division, CSNS
Dongguan Campus of IHEP (Institute of High Energy Physics)
EPICS Collaboration Meeting 2024
Apr 15 – 18, 2024, hosted by the Pohang Accelerator Laboratory

## Slide 2: Content
（1）Scenario
（2）Design
（3）Implementation
（4）Usage examples
（5）Issues and use cases
（6）Summary

## Slide 3: Scenario
node-epics-pcas: Portable Channel Access Server for Node.js
Motivation #1
  EPICS has excellent support for C++, Java and Python.
  EPICS has very little support for JavaScript or Node.js.
  JavaScript and Node.js are very popular in web development.
  I am interested in developing EPICS-related tools for Node.js.
Motivation #2
  As a high-level application developer, starting an IOC is not very convenient for me.
  Although there is already pcaspy, I am not familiar with Python.
  If PVs can be published in Node.js environment, it is convenient.
Why?

## Slide 4: Design
FFI (Foreign Function Interface) is used to talk to the shared libraries of PCAS
  libca, libcas, libCom, libgdd
Which FFI library to use?
  node-addon-api
    https://www.npmjs.com/package/node-addon-api
    Learning curve is deep
    Does not support callback
  SWIG (Simplified Wrapper and Interface Generator)
    https://swig.org/
    Support for JavaScript is not as good as Python
    Mailing list support is too slow (~ 1 week)
  koffi
    https://www.npmjs.com/package/koffi
    Fast and easy-to-use C FFI module for Node.js
    Well maintained, well documented, quick response on GitHub issue tracker

## Slide 5: Design
Borrows idea and implementation from pcaspy
  https://pypi.org/project/pcaspy
  Portable Channel Access Server in Python
Most of the logic has been moved from the scripting language to C++
Wraps PCAS C++ shared library and provide C interfaces for Node.js
  libca, libcas, libCom, libgdd
Uses koffi in Node.js to interact with the C interfaces.
Provides APIs in node-epics-pcas for Node.js applications.

## Slide 6: File structure
wrapper.h and wrapper.cpp files
  Wrapper of PCAS C++ code which provide C interface for Node.js
clibs folder
  Prebuilt shared libraries: libca, libcas, libCom, libgdd
  Built from EPICS base 3.15.9 together with wrapper.h / wrapper.cpp
channel.js file
  Interacts with the C interface and provides APIs for Node.js applications
aitTypes.js file
  Architecture Independent Type (AIT) definitions in PCAS
alarm.js file
  EPICS alarm status and severity definitions

## Slide 7: All C++ classes in the wrapper
class SimpleServer: public caServer
  The server instance of PCAS
class SimplePV: public casPV
  PV instance for the server tool
class PVInfo
  PV info associated with the PV instance
class Driver
  Interfaces for Node.js to operate the parameter library
class Data
  PV value and status in parameter library
class Value
  Data structure for PV value field
All C++ classes in the PCAS server tool

## Slide 8: APIs for Node.js applications
createServer()
  Create the PCAS server
getParam()
  Get value from the parameter library
setParam()
  Set value to the parameter library
setParamStatus()
  Set alarm and severity to the parameter library
updatePVs()
  Post event to monitor clients when value or alarm status changes
setDebugLevel()
  Set debug level (0, 1 or 2) to print more information
Supported PV fields

## Slide 9: Usage examples
A dummy PV
Dummy scalar PVs
Dummy array PVs

## Slide 10: Usage examples
Read data from Node.js
Write data to Node.js

## Slide 11: Usage examples
Raise alarm automatically
Raise alarm manually

## Slide 12: Issues
Memory leak problem exists.
Currently it is not clear what the root cause is.
A memory leak test
  Running the usage example to publish Archiver Appliance status as PVs
  Running for 24 hours
  Linux virtual machine with 8GB memory
  Memory usage rose from 0.7% to 2.5%
Due to the memory leak issue, node-epics-pcas is not recommended for production use.
It can be used to publish PVs for test purpose.
Use cases

## Slide 13: Summary
node-epics-pcas is an EPICS Channel Access server for Node.js with FFI implementation.
The FFI package in use is koffi.
The implementation is very similar to the pcaspy package.
Github and npm package links
  https://github.com/wanglin86769/node-epics-pcas
  https://www.npmjs.com/package/node-epics-pcas
Development team
  Design & Implementation: Lin Wang wanglin@ihep.ac.cn
  Line Manager: Yuliang Zhang zhangyl@ihep.ac.cn

## Slide 14
Thanks for your attention!