## Slide 1: Status of the RAON Heavy Ion Accelerator
Dong-O Jeon, Ji-Ho Jang, Hyunchang Jin*, Hyung Jin Kim, Jeongil Heo,
Bum Sik Park, Jangwon Kwon, Yujung Ahn, Chul Jin Choi, Eun Hun Lim,
Sangyoon Bae, Kyung Tae Seol, Yoochul Jung, Youngkwon Kim, Hyojae Jang,
Heetae Kim, Ju Wan Kim, Joonsun Kang, Hyungjoo Son, Chang Seok Seo, Yeon Sei Chung
IBS/IRIS
*KBSI
ICABU 2024.11.

## Slide 2: The RAON Facility
Campus Area: 952,066 m2

## Slide 3: Accelerator Systems
SCL32
ISOL
SCL31

## Slide 4: Accelerator Systems Construction Phase 1 & 2
Injector
ISOL
IF Separator
KoBRA
SCL3
SCL3
High energy Experiment Hall
Low energy
Experiment Hall
Phase 1 (2012~2022)
Injector, SCL3, ISOL
All the experiment systems including IF separator system
Phase 2 (~2030)
SCL2 (high energy linac)
Injector
Very Low energy Experiment Hall
SCL2
SCL3
4

## Slide 5: Accelerator Systems Low Energy Superconducting Linac (SCL3)
SSPA(60kW*2EA)
Cryomodule(CM) & Warm section is assembled in the clean booth at tunnel
Total Particle counts < 30 counts / 10min (size > 0.5um)
Warm section
CM
CM
CM
Beam commissioning started in Oct, 2022
5
SCL3

## Slide 6: The RAON Injector
[ RAON injector ]
- RAON injector: 14.5 GHz ECR IS (10keV/u), LEBT (charge selection, matching),
RFQ (507 keV/u, 98% transmission) , MEBT (matching)
- Injector beam commissioning:
Ion | Argon | Neon | Oxygen | Helium | Proton
A (Q) | 40 (8, 9, 11) | 20 (4) | 16 (6) | 4 (2) | 1(1)
Current [A] | 50, 30, 50 | 40 | 40 | 50 | 50 ~ 160
[ Beam Diagnostics in RAON injector ]

## Slide 7: Beam Commissioning
Measurements for commissioning
Emittance (X and Y) : Allison scanners, wirescanners, quad scan methods
Cavity RF set-point (phase scan, BPM)
Beam energy (phase scan, TOF with BPMs)
Beam current, transmission (ACCT, FC)
Orbit correction (BPM / Wirescanner & dipole steerer)
Beam transverse profile (wirescanner)
Beam longitudinal profiles (Fast Faraday Cup)
Transverse matching (wirescanner)
Physics applications for commissioning
BIPAM (Beam Input Parameters And Matching)
CAPS (Cavity Amplitude and Phase Scan)
Orbit correction application
Emittance data analysis & wirescanner data analysis
7

## Slide 8: LEBT beam parameter measurements
Beam parameter measurement (Allison scanners, wirescanners)
- using emittance data or beam sizes of wirescanners
controlling beam optics
Emittance measurement (Allison scanner, BIPAM, quad scan)
Beams: Ar9+, Ar8+, O6+, Ne4+, He2+, proton
BIPAM: beam emittance & parameters
Beam emittance
(Allison scanner)
 | X | Y
Allison | 0.048 | 0.067
Quad Scan | 0.041 | 0.038
emittance comparison
Quad scan
(beam emittance)

## Slide 9: LEBT beam measurements for various beams
- By using the Allison data and wirescanner data, we established beam matching to RFQ.
- Beam dynamics: using TRACK or DYNAC codes
Initial result of Allison scanner Ne4+
Allison result after adjusting quadrupoles
for Ne4+
TRACK results after beam matching to RFQ

## Slide 10: Wire-scanner and TRACK in LEBT for various beams
- We compared WS data with TRACK simulation in LEBT
* TRACK input: calculated from Allison data
* In general, TRACK simulations and WS data are in good agreement
with each other.
Ne4+
Ar9+
He2+
Ar8+
J.H. Jang

## Slide 11: LEBT wire-scanner measurements for various beams
O6+ 48uA
injector transmission: 90%
LEBT
RFQ
Beam parameters are measured using BIPAM for various beams.
Beam optics is controlled with measured beam parameters.
Matching can be performed.
H+ 160uA
LEBT transmission: 75%
LEBT
RFQ
LEBT
RFQ
Ar8+ 50uA
injector transmission: 95%
X beam size
Y beam size
11

## Slide 12: Matching to RFQ
Matching Ar8+ beam to RFQ improves beam quality in MEBT.
Beam profiles are almost Gaussian.
MEBT wirescanners
12

## Slide 13: RFQ RF set-point
- RFQ transmission: (ACCT in LEBT and ACCT in MEBT)
* RFQ transmission is larger than 90%.
* We found low RFQ transmission for Ne beams
 We can improve it by using slit in LEBT
 | Ar9+ | Ar8+ | Ne4+
Transmission | 93.4% | 95.4% | 85.7%
Set value | 51.5 kW | 62.9 kW | 67.4 kW
RFQ
MEBT
RFQ set-point for Ar9+
RFQ set-point for Ne4+
RFQ set-point for Ar8+

## Slide 14: Off-axis injection affects RFQ output beam
ex=0.086 mm-mrad
ey=0.064 mm-mrad
ex=0.114 mm-mrad
ey=0.068 mm-mrad
ex=0.098 mm-mrad
ey=0.146 mm-mrad
X kick
Y kick
reference
Jeon et al, NIM A 1052, 168250 (2023)
On-axis injection to the RFQ is crucial: Off-axis injection increases output beam rms emittances and beam tails.
14

## Slide 15: MEBT beam emittance
MEBT beam parameter measurements:
using wirescanner data
measure the initial beam emittances & parameters
matching to SCL3
BIPAM method and quad scan show consistent results.
quad scan technique takes rather long time
BIPAM requires one scan per wirescanners
X plane
Y plane
Quad scan
 | ex mm-mrad | ey mm-mrad
BIPAM | 0.068 | 0.044
Quad Scan | 0.064 | 0.049
emittance comparison
WS data
BIPAM

## Slide 16: MEBT Beam profile Exp. vs Simulation
- Adjust RFQ output beam parameters
by using WS results in MEBT.
- Compare TRACK simulation and 3 WS data
* Different results between TRACK simulation
and WS data  Adjust RFQ output beam
rms beam size through MEBT
Ar9+ in MEBT
Ne4+ in MEBT
He2+ in MEBT
Ar8+ in MEBT
J.H. Jang

## Slide 17: Ar8+ beam in Injector and SCL3
LEBT
RFQ
Ar8+ 45uA
injector transmission: 95%
MEBT
SCL3(QWR)
ex=0.091 mm-mrad
ey=0.063 mm-mrad
(BIPAM)
ex=0.059 mm-mrad
ey=0.033 mm-mrad
(BIPAM)
17
X beam size
Y beam size
X beam size
Y beam size

## Slide 18: RAON Superconducting Linac
- RAON superconducting linac: SCL3(low energy), SCL2(high energy, 2nd phase)
- Low energy superconducting linac (SCL3):
* 2 types of cavities: QWR (4K), HWR (2K)
* Normal conducting quadrupole doublet for transverse focusing
* Large aperture diameter for small beam loss: 40 mm

## Slide 19: SCL3 Diagnostics and Phase Scan
For RF set-point, phase scan technique is used to set the RF set-point.
19
cryomodule
quadrupole
beam box

## Slide 20: Beam Commissioning of SCL3
First Beam commissioning with 40Ar+9 beam: 1Hz, 100 sec
- Sep. 2022: Start cool-down
- Oct. 2022: Cool down to 4.5K finished
- Oct. 2022: Beam commissioning with initial 5 cavities of QWR finished
- Dec. 2022: QWR beam commissioning finished
- Jan. 2023: Cool down to 2K finished
- May 2023: SCL3 beam commissioning finished
* 10 cavities (out of 124) were not used due to control issues, cold leak, etc.
* Accelerating fields: QWR < 5 MV/m (design 6.1 MV/m), HWR < 4 MV/m (design 6.6 MV/m)
- June 2023: KoBRA beam test (May 30 ~ June 2)
Second Beam commissioning with 40Ar+8 beam: 1Hz, 100 sec
- March 2024: Cooled down to 2K
- April 29, 2024: SCL3 beam commissioning started
* 8 cavities are excluded for similar reasons
* Accelerating fields: QWR < 5 MV/m (design 6.1 MV/m), HWR < 5 MV/m (design 6.6 MV/m)

## Slide 21: 2023 Ar9+ beam commissioning
3 QWR cavities were turned off.
7 HWR cavities were turned off.
RF set-points of near-by cavities were adjusted to minimize beam loss.
Cavities were set using phase scan:
beam energy: 17.39 MeV/u
Beam transmission: 64%
Beam phase jitters were big in 2023.
21

## Slide 22: 2024 Ar8+ beam commissioning
3 QWR cavities were turned off.
5 HWR cavities were turned off.
RF set-points of near-by cavities were adjusted to minimize beam loss.
Cavities were set using phase scan:
beam energy: 18.53 MeV/u
Beam transmission improved: 93%.
Energy discrepancy observed (phase scan vs dipole) → BPM calibration is needed and check against dipole will be performed.
22

## Slide 23: BPM phase jitters improved
Cavity RF set-points were obtained using phase scan technique (2 BPMs).
In 2024 BPM phase jitters were reduced compared with the 2023 run.
Beam phase jitter is still large and tighter LLRF control is necessary.
Last HWR cavity (2024)
Last HWR cavity (2023)
23

## Slide 24: Beam Loss and RF control in SCL3
Beam transmission through SCL3:
QWR orbit correction reduced beam loss during HWR commissioning.
Beam transmission: 64% in 2023  93% in 2024.
RF control of SCL3 cavities continues only several minutes.
RF powers  coupler temperature rising  cavity frequency shift  slow tuners moves, but we lose RF control of some cavity. (It is why we use smaller amplitudes): Need to improve couplers and tuners
Beam transmission (2023)
Beam transmission (2024)

## Slide 25: Beam Loss & Longitudinal Acceptance
- Longitudinal Acceptance decrease induces beam loss.
- Estimated beam loss through the Error Analysis.
- To increase beam transmission, we need to turn on more cavities.
[ Longitudinal
Acceptance ]
[ All cavity ON ]
[ Beam Loss
(Error Analysis) ]
[ 8 cavities OFF ]
[ 8 OFF  QWR3 ON ]
[ 8 OFF  QWR3,12 ON ]
Ji-Ho Jang
25

## Slide 26: Stripped Ar+18 beam to the NDPS (neutron facility) 2024.06.12.
40Ar 빔 (NDPS 표적 위치)
중성자 빔
감마선
Preliminary
26

## Slide 27: First Rare Isotope Beam Acceleration
- RI beam (25Na5+) acceleration through SCL3 (July 19, 2024)
* The beam is generated by the ISOL facility,
* Accelerated by the SCL3 and transported to the KoBRA.
* All plots in this page are provided by the experimental system team in IRIS.
[ Separation of 25Na5+ beams from impurities and the measured value of the life-time ]

## Slide 28: Summary
Superconducting linac (SCL3) beam commissioning has been conducted:
We have made significant progresses.
Beam commissioning with Ar9+ beam was in 2023.
Beam commissioning with Ar8+ beam conducted in 2024.
Beam was sent to KoBRA for user service and to NDPS.
Beam transmission improved from 64% (2023) to 93% (2024).
Beam phase jitter is reduced due to tighter LLRF control.
Injector beam commissioning has been conducted: Ar9+, Ar8+, O6+, Ne4+, He2+, proton beams.
Issues:
superconducting cavity stability issues.
HWR cavities run at 76%, QWR cavities at 82%.
BPM calibration is needed to do Time-of-Flight measurement.
Beam energy inconsistency between phase scans and dipole scans
28

## Slide 29: Summary
Experiment systems commissioning & user service in 2024
Ar8+ beam to KoBRA for user service
Stripped Ar18+ beam to NDPS for experiment system commissioning
Na5+ Rare Isotope beam from the ISOL to KoBRA in 2024
RI beam is planned for user service in 2025:
High energy SCL2 development
R&D underway to prototype SSR1 and SSR2.
Timely completion of the R&D is crucial.
Thanks for your attention!!
29

## Slide 30: Accelerator Systems SRF Test Facility & Cavity Tests
30
SRF Test Facility: 3 Vert. Test pits (3 cavities per pit), 3 Hor. Test bunkers
Test all the RAON cavities: 22 QWR (82.25 MHz), 102 HWR (162.5 MHz) and SSR1,2 (325 MHz)
QWR
HWR
30