## Slide 1
Overview and Results of the “Intercomparison” reported at SATIF
Hideo Hirayamaa,b
aHigh Energy Accelerator Research Organization
bNuclear Regulation Authority

## Slide 2: Introduction
“Intercomparison” of computational codes were conducted from SATIF-3 through SATIF-16 (excluding SATIF-11).
Unlike “benchmarks,” which are compared with experimental data, “intercomparisons” aim to compare differences among computational codes using identical calculation conditions (such as source, material composition, and conversion factors for dose, etc.).
Two types of intercomparison initiatives were conducted within SATIF.
Both were “collaborative efforts by SATIF participants” in which participants submitted results obtained using their respective codes in response to “proposed challenges” issued by the organizing committee, and the results of the inter-code comparisons were reported at SATIF.
This presentation will introduce the details of these two types of intercomparisons and the results obtained.

## Slide 3: Differences between “Benchmark” and “Intercomparison”
“Shielding benchmark calculations” involve comparing results obtained via various calculation methods and codes against “true values”—which are derived from high-quality experimental data characterized by clearly defined source conditions and shielding specifications (composition, density, and dimensions) and sufficient accuracy for meaningful comparison.
  Since there is a target “true value,” it is likely that various “improvements” are attempted—while comparing results against that value—in order to achieve an outcome closer to it.
  This process can sometimes lead to improvements in the “models” or “data” used in the computational code.
Experimental results suitable for benchmark calculations are limited, as they require facilities capable of conducting the experiments and measurement systems capable of high-precision measurement.

## Slide 4: Differences between “Benchmark” and “Intercomparison”
The objective of an intercomparison is to examine how “calculation methods” and “reaction models/data” influence the results with using same information of material data, mixture compositions and ratios, and dose calculation methods.
Such comparisons can be conducted regardless of the availability of measured data.
If discrepancies arise between computational codes, it is not possible to determine which represents the "correct information," but it is possible to show the extent to which the codes differ in their treatment of the phenomenon in question.
Two types of intercomparison activities were conducted under SATIF and reported at the meeting.
  Intercomparison of medium energy neutron attenuation in iron and concrete
  Intercomparison of particle production

## Slide 5: Intercomparison of medium energy neutron attenuation in iron and concrete
This intercomparison was initiated as part of the action “Agree on definitions of attenuation length and source term parameters,” which was added at SATIF-2.
This proposal was made by a Japanese group with the aim of understanding the behavior of the “neutron attenuation coefficient” in the intermediate energy range of 1 GeV and below, by comparing results across different calculation codes.
  “Neutron attenuation coefficient” is a parameter critical to shielding calculations for high-energy accelerators at the time.
In the energy range above several hundred MeV, the attenuation of neutrons in matter becomes nearly constant regardless of energy; this conclusion was drawn based on the fact that the inelastic scattering cross-section of neutrons in matter remains approximately constant for neutrons with energies above 100 MeV.

## Slide 6
Comparison of neutron attenuation lengths in concrete (Paterson and Thomas, “Accelerator Shielding”)
Inelastic neutron cross section
(Paterson and Thomas, “Accelerator Shielding”)

## Slide 7: Intercomparison of medium energy neutron attenuation in iron and concrete
Results from SATIF-3 revealed that differences between codes in the intermediate energy range were smaller than anticipated, indicating the importance of comparisons at higher incident energies, including neutron spectra.
In subsequent SATIF exercises, comparisons were made based on calculations involving neutron energies of 20 MeV and above; the incident neutron energy was increased for each problem (reaching 10 GeV in the final Problem 7), and the shielding thickness was increased up to 12 m for concrete.
Starting with SATIF-4, a problem was also added in which the distributed secondary neutrons provided by the organizers were treated as incident neutrons.

## Slide 8
Problem at SATIF-3 (Problem 1)
Problem at SATIF-9 and 10 (Problem 7)

## Slide 9
Participating organizations, codes, etc. to intercomparison of medium energy neutron attenuation in iron and concrete

## Slide 14: Semi-benchmark comparison at SATIF-9
As the new problems, the comparison with the experimental results of AGS shielding experiments presented by H. Nakashima et al. was added.
  Proton (2.83 and 24 GeV)
  Target Material : Mercury
  Shielding Material : Steel and Concrete
  Geometry : Slab Geometry
  Neutron Reaction Rate
    209Bi(n,4n)206Bi
    209Bi(n,6n)204Bi
  Use reaction cross section provided from organizer
Concrete shield
Steel shield
Cave
Mercury target
Proton beam

## Slide 17: Future Themes
0 effects for iron presented PHITS must be checked by other codes.
It is necessary to compare various produced secondary particles from small target to understand the reason of difference of dose at high energy region.
Study the reason for the large difference in the attenuation length and dose between codes.
Study the reason of difference between measured results and calculated ones by various codes and the reason of the different tendency of C/E values between codes.

## Slide 18: Future Themes (SATIF-10)
Λ0 effects for iron presented PHITS must be checked by other codes.
It is necessary to compare various produced secondary particles from small target to understand the reason of difference of dose at high energy region.
Study the reason for the large difference in the attenuation length and dose between codes.
Study the reason of difference between measured results and calculated ones by various codes and the reason of the different tendency of C/E values between codes.

## Slide 19
500 cm
10 GeV proton
Target
Target
(a) Al : length 40cm, diameter 4.0cm and density 2.7g/cm3
(b) Cu : length 16cm, diameter 1.6cm and density 8.63 g/cm3
(c) Au : length 10cm, diameter 1.0cm and density 19.3 g/cm3
Intercomparison problems of particle production (SATIF-15 and 16)
Incident particle
Pencil beam of protons with 10 GeV.

## Slide 20
Participating organizations, codes, etc. to intercomparison of particle production

## Slide 21
Comparison of total particle fluence number above 20 MeV

## Slide 22
0 degree neutron from 10 GeV proton

## Slide 23
150 degrees proton from 10 GeV proton

## Slide 24
150 degrees π+ from 10 GeV proton

## Slide 25
150 degrees π- from 10 GeV proton

## Slide 26
0 degree photon from 10 GeV proton

## Slide 27: Future action (SATIF-16)
It is desired to check models especially for spectrum of neutron and proton and angular distributions by code developers and reflect to this comparison.
Good experimental results at 0 degree and large angle will be useful to found the reason of differences between codes.
What intercomparison will be useful to understand the differences between codes ?
We want to hear everyone’s opinions.

## Slide 28: Summary
The intercomparison reported at SATIF was a joint achievement of the organizing group and the participants.
This activity made possible only within the framework of SATIF.
  Communicate intercomparison issues to code developers and users who are interested.
  Report and discuss at SATIF as the joint activities.
Both “benchmarking” (comparison with experimental results) and “intercomparison” (comparison among computational codes) are crucial for the advancement of computational codes.
It is hoped that necessary intercomparison tasks will continue to be agreed upon within SATIF and that the results will be reported there.