## Slide 1: RP studies and operational experience from the decommissioning of the CNGS target area
EDMS 3536520
A. Devienne, C. Ahdida, E. Nowak, C. Saury, S. Boucly, D. Estellon, M. Tirronen, R. Charousset, F. Aberle and P. Bertreix
SATIF-17 (20-22 October 2026)

## Slide 2: Content
Introduction
Characterization
Benchmark
Feedback
Conclusion

## Slide 3: Introduction
CNGS & Target Area Decommissioning

## Slide 4: Introduction
732 km
Gran Sasso (Italy)
Detectors: OPERA & ICARUS
Beam p+ 400 GeV/c
The CNGS experiment (2006-2012) aimed at detecting muon-to-tau neutrino oscillations with an intense muon-neutrino beam generated at CERN directed over 732 km towards the Gran Sasso National Laboratory in Italy.
Year | Mode | Protons on target (pot/year)
2006 | Commissioning | 0.08E+19
2007 | Commissioning | 0.08E+19
2008 | Physics | 1.78E+19
2009 | Physics | 3.52E+19
2010 | Physics | 4.04E+19
2011 | Physics | 4.84E+19
2012 | Physics | 3.90E+19
TOTAL |  | 1.82E+20
Beam intensities
Beam line description
Target Area (TCC4)

## Slide 5: Introduction
Motivations of CNGS Target Area Decommissioning (2025-2026, 12 MCHF):
  Extension of the AWAKE experiment after LS3
  Re-use of standard shielding blocks for other CERN facilities (400 m³)
  Minimize CERN on-site radioactive storage (VLLW 81 m³, LILW 102 m³)
January 2026
October 2026
November 2025

## Slide 6: Characterization
Studies & validation

## Slide 7: Characterization – studies
Scoring residual dose rate and activities
FLUKA Model
Identified past contributors to the current FLUKA model: A. Ferrari, M. Lorenzo, L. Sarchiapone, S. Roesler, H. Vincke, C. Ahdida, E. Nowak
C. Ahdida et al. (2023) 10.1080/00295639.2023.2204183
User routine (magfld.f) generating a toroidal magnetic field
Detailed CSG model with CNGS beam line components, supports, shielding and concrete tunnel floor/walls
Residual dose rate after 11 years of cooling (December 2023) with all components
Residual dose rate in the empty tunnel (April 2026) (using ASSIGNMAT card to assign a different material at decay)
FLUKA v4.0-x

## Slide 8: Characterization – validation
FLUKA + Actiwiz 3 simulations vs results from Gamma Spectrometry main radionuclides
Material composition (concrete):
  XRF measurements
  Sampling of concrete
  Gamma Spectrometry
Results of the XRF for the concrete composition of the shielding, tunnel walls and floor
Results of the Actiwiz and Gamma spectrometry for the concrete floor

## Slide 9: Benchmark
Target, Horn & Empty tunnel

## Slide 10: Benchmark – Target
Source: EDMS 3408902
Video overview of the handling, survey, cutting and packing of CNGS target station

## Slide 11: Benchmark – Target
10 mSv/h (AD-6 & AD-t)
Cool-down time for benchmark: January 2026
Downstream:
  RP Survey performed with an AD-6 (Automess 6150AD) on a robot
  Ratio RP Survey / FLUKA ~1.2 (at 10 cm and 40 cm)
Contact
10 cm
Residual dose rate at different distances from the downstream face. Averaged on X=[-5;5], Y[15;20]
40 cm
Target
Side view of the residual dose rate at the target location. Averaged on X=[-5;5]
FLUKA v4.5-x
Beam
Side view

## Slide 12: Benchmark – Target
Lateral:
Beam
Residual dose rate lateral target (@5cm). Averaged on Y=[-10;10], X=[32;38]
downstream
middle
upstream
3 mSv/h (AD-6 & AD-t)
5 mSv/h (AD-6 & AD-t)
8 mSv/h (AD-6 & AD-t)
Cool-down time for benchmark: January 2026
(lateral downstream)
(lateral middle)
(lateral upstream)
Measurement at 10 cm laterally from the target station on the TCC4 corridor side at 3 locations (upstream, middle, downstream).
downstream
middle
upstream
Residual dose rate from center along beam axis. Averaged on X=[30;40], Y[20;30]
Top view of the residual dose rate at the target location. Averaged on Y=[-5;5]
Top view

## Slide 13: Benchmark – Horn
RP Survey:
  Using an AD-t (Automess 6112AD)
  Upstream, downstream and laterally (both corridor and wall sides) at 3 distances (“contact”, 10cm, 40cm)
Ratio RP Survey / FLUKA:
  Up to a factor of 2
Horn
Downstream
Upstream
Residual dose rate upstream and downstream of the Horn. Averaged on X=[-5;5], Y[-5;5]
Top view
Horn
11.5 mSv/h (AD-6 & AD-t)
Wall
corridor
Wall side
Corridor side
Cool-down time for benchmark: July 2026
Residual dose rate laterally of the Horn. Averaged on Y[-5;5]
40-cm
Possible causes (under investigation):
  Simplified geometry / materials
  Distances during survey
Implications:
  Extra dose at removal (+0.5 p.mSv)
  Additional shielding for on-road transport

## Slide 14: Benchmark – Horn
  Residual dose rate around truck containing the horn in its container with an additional 12 mm Pb-equivalent layer
  Bin size Z=20cm, X=20 cm, averaged in Y=[-10;10] - Scaled with RP survey (factor 2)
  Top view at beam level
Horn container and Truck in FLUKA for on road transport

## Slide 15: Benchmark – Empty Tunnel
RP Survey (09/2026):
  Measurement with 3 AD-6 (Automess 6150AD) mounted on mechanical arm with 3 distances (“contact”, 40cm, 100cm)
  Identification of areas >50 µSv/h at 40 cm
Good agreement with FLUKA simulation (activities still ongoing)
Cool-down time for benchmark: September 2026
Empty tunnel floor below the target & horn
Empty tunnel floor below the reflector
Residual dose rate along the beam axis at 40 cm from the floor. Averaged on X=[-10;10], Y[-140;-100]
Horn
Reflector
Top view

## Slide 16: Feedback
Planning & Contamination

## Slide 17: Feedback – Work and Dose Planning
Strategy:
  No safety factor used for dose estimates  early detection in case of deviation
  Safety margin of 20% in the planning  currently with +1 month behind schedule after 10 months.
  Presentation to an ALARA committee as per CERN procedure (>5 p.mSv or >1mSv)  ensure optimization measures.
Lessons learnt:
  Collective dose estimate went from 14 p.mSv (initial) to 26 p.mSv (current)  major review in July 2026
  Safety factors could have been used in critical activities for which hard limits apply (ex: on-road transport or max individual dose)
  Foresee slots in the planning for backup options (ex: removal of the Horn)
Chart: Additional collective dose (+12.5 p.mSv)
| Activities not considered in the initial scope | Operational difficulties
Additional Collective Dose | 6.5 | 6
Actual collective dose
Estimated collective dose
WDP (done in October 2025)
WDP (updated in July 2026)
Major revision of dose estimates

## Slide 18: Feedback – Contamination
Items contaminated:
  136 (currently)  Marble, Concrete, Iron shielding and Aluminium beam line components facing the beam. Mainly associated with degradation of the material (rust, dust, sweat).
Limits applied:
  > 1 Bq/cm2 (unidentified β/γ) or > 0.1 Bq/cm2 (unidentified α).
  For identified radionuclides > 1 CS (values derived from Swiss legislation)
  If after cleaning or decontamination still above the limits  packaged or contamination fixed.
Main actions:
  The most radioactive items were wrapped or placed in dedicated containers.
  The Helium Tanks (Aluminium) were cut and decontaminated (ASPIGEL).
  Contamination fixed on concrete blocks < 600 µSv/h at contact (CONTAFIX),
Target
TBID
Reflector (wrapped)
Helium Tank
(decontaminated)
Fix contamination (spray) vs. decontamination (gel) on concrete

## Slide 19: Conclusion

## Slide 20: Conclusion
The CNGS Target Area is being decommissioned (2025-2026) for the extension of the AWAKE experiment.
Characterization studies were done in preparation of the activity. Current collective dose estimate is 26 p.mSv (14 p.mSv initially).
Benchmark results on residual dose rates show an agreement between RP survey and FLUKA generally within a factor of 2 (mainly underestimation).
Operational activities carried out by a specialized nuclear dismantling contractor: a lot of lessons learnt!
After the decommissioning of the Target Area, it will only remain from CNGS the 1-km decay tube and the hadron stop chamber (200 m³ of iron…)