## Slide 1: Deflecting cavity status & experimental plan at eLABs
Geunwoo Kim
24. 10. 11.

## Slide 2: Contents
1. Transverse deflecting cavity (TCAV)
CST
Modeling
Field distribution for Astra
MAD-X
Preparation
Current status
2. Simulation
3. Longitudinal phase space (LPS), briefly

## Slide 3: 1. Transverse deflecting cavity (TCAV)
E0
x’
Screen
TCAV kicks the beam to the transverse plane.
by Panofsky-Wenzel Theorem
  Gradient Ez is major kick component for deflecting.
  TM mode is dominant than TE mode.
We can measure the longitudinal beam distribution.
RF
deflecting
cavity
Beam
<e-labs deflecting cavity shape>
Coupler cells
Active cells

## Slide 4: 1. Transverse deflecting cavity (TCAV)
Main feature
HEM11 mode (similar to TM11 mode)
  : Composed of TE11 and TM11 modes
  Uses both E and B fields for kicks.
  Capable of achieving high shunt impedance.
  ∴ Therefore, achieving high transverse kick components.
6 cells
ΔΦ = 4π
<E-field distribution>
z
Compared to SCLA TCAV, rsh is about a factor of 14.
 | SCLA TCAV | E-labs TCAV
Mode | TM11 | HEM11
Shunt Impedance(rsh) | 2.1 MΩ/m | 28.7 MΩ/m
Structure | Linear and Circular | Iris-loaded
<SCLA TCAV, TM11 mode>

## Slide 5: 1. Transverse deflecting cavity (TCAV)
Main feature
Iris-loaded structure
Why don’t we use a uniform cavity?
  Phase velocity > c in a uniform waveguide.
   Particle cannot exceed the speed of light ( ve ~ c, ve < c).

## Slide 6: 1. Transverse deflecting cavity (TCAV)
Main feature
Iris-loaded structure
  Disk-loaded or “slow-wave” structure
  Control is necessary to synchronize with a beam.
   Deaccelerating
2/3π mode (ΔΦ = 2π for three cells)
  High efficiency (high shunt impedance)

## Slide 7: 1. Transverse deflecting cavity (TCAV)
The primary goal of my research
* Investigation of the longitudinal phase space (LPS) using TCAV.
Before the experiment, we need to confirm TCAV’s resolution by simulation.
1. Resolution is one of the crucial parameters. (whether it can have fs scale resolution)
2. So far, there are no measured results or simulation results.
MAD-X, Astra is suitable for obtaining the beam parameter.
  * 2D field distribution of TCAV should be measured using CST.
σy0: RMS beam size on the screen
βd: β at TCAV entrance
βc: β on screen
ΔΨy: Phase advance between TCAV and screen
Φrf: RF phase from the zero crossing
σz: RMS bunch length
krf: wavenumber of field

## Slide 8: Contents
1. Transverse deflecting cavity (TCAV)
3. Longitudinal phase space (LPS), briefly
CST
Modeling
Field distribution for Astra
MAD-X
Preparation
Current status
2. Simulation

## Slide 9: 2. Simulation (CST)
Modeling & Field distribution
0. Remodeling in my own for understanding the structure
Eigenmode solver
  To check whether the geometry is same or not.
  HEM11 mode (2.856 GHz, Mode 5)
Frequency-domain solver
d
< field distribution example in Astra>

## Slide 10: 2. Simulation (CST)
Extra) Comparison simulation results with reference results.
- boundary condition: Et=0
- Cell per maximum wavelength: Automatic

## Slide 11: 2. Simulation (MAD-X)
<e-labs equipment layout>
Courtesy of PhD. Sung
Of course, it is inaccurate!
~ 2.76 m
2.8 m
Screen
~ 0.465 m
Preparation
The Methodical Accelerator Design code (MAD)
e-labs layout with distance
Checking the equipment layout
Familiar with the simulations

## Slide 12: 2. Simulation (MAD-X)
<e-labs equipment layout>
Courtesy of PhD. Sung
2.8 m
Screen
~ 0.465 m
Preparation
Initial condition βx0, βy0, αx0, and αy0 were given right after booster cavity.
Deflecting voltage V⊥ : 2.7 MV/  1 MV; P = 0.137 MW
MAD-X simulation start point

## Slide 13: 2. Simulation (MAD-X)
Current status
Study how to use MAD-X.
Insert TCAV to the beamline.
Taking βd
Simulation begins at 5.0 m
<Initial beamline>
<Revised beamline>
TCAV
1. Space between quad
0.21 → 0.3 [m]
0.19 → 0.3 [m]
2. Adding TCAV
3. β Optimization point
s = 2 → 3.7 m

## Slide 14: Contents
1. Transverse deflecting cavity (TCAV)
CST
Modeling
Field distribution for Astra
MAD-X
Preparation
Current status
2. Simulation
3. Longitudinal phase space (LPS), briefly

## Slide 15: 3. Longitudinal phase space (LPS)
Tomography method
Iterative Reconstruction Method

## Slide 16: Summary and plans
Understanding TCAV Geometry and Operational Principles
Complete Re-modeling of TCAV
  Performed using CST simulation to analyze field distribution
  Comparison between reference results and my results. (Still different, but insignificant)
Inserting TCAV to the initial beamline and obtaining β by using MAD-X.
Enhanced proficiency in MAD-X, including ASTRA simulations
Focused study on Longitudinal Phase Space (LPS)
Simulations are being finalized to ensure before TCAV's deployment at PAL