## Slide 1: Deflecting cavity status & experimental plan at eLABs
Geunwoo Kim
24. 11. 08.

## Slide 2: Contents
0. Review
How to design TCAV in ASTRA
Matching process for elabs TCAV.
Optimization elabs beamline
TCAV resolution calculation

## Slide 3: 0. Review
Main feature
HEM11 mode (similar to TM11 mode; TE + TM)
  Possible to get high deflecting component.
Iris-loaded structure (a.k.a slow-wave structure)
  To deaccelerate phase velocity under .
2/3π mode (ΔΦ = 2π for three cells)
  Increasing rsh → VT ↑ ()
<e-labs deflecting cavity shape>
Coupler cells
Active cells
6 active cells (2/3π mode)
ΔΦ = 4π
<E-field distribution>
z
y

## Slide 4: 0. Review
Kick direction
  Ey and Hx were measured w.r.t z direction.
  Beam will be kicked onto y direction. (E+B)
Ey
Hx
<Ref.>
To simulate TCAV into elabs beamline,
need to know how to define TCAV in ASTRA

## Slide 5: 1. Milestone to get resolution by simulation
Definition TCAV in ASTRA
Scaling TCAV to elabs
Simulation
(MAD-X, ASTRA)
Resolution
calculation
Notes: 하나 빠지면 파일 자체를 못찾아버림

## Slide 6: 1. How to design TCAV in ASTRA
3D field map components are required.
Transform CST data → 3D field map format
Store total 12 data
  Both Re and Im field components.
  If you are missing just single component….
Position
Data
Field(Fx, Fy, Fz)
Re
Fx
Im
Fx
Re
Fy
Im
Fy
Re
Fz
Im
Fz
<CST 3D data format>
Position
data
x
y
z
#
of posi.
x y z
<ASTRA 3D field map format>
Field data
x
y
Nz(1)
Nz(2)
Nz(n)
Notes: 하나 빠지면 파일 자체를 못찾아버림

## Slide 7: 1. How to design TCAV in ASTRA
Assign 3D field map data into Astra code.
  Re and Im fields should be distinguished.
Combine both cavities into a single module.
6. Run
Module 1
Cavity 1
Re(field)
Cavity 2
Im(field)
Control scaling, phase Φ
# of particles: 1,000

## Slide 8: 2. Scaling process for elabs TCAV
Initial VT = 155.6 MV
  PAL-XFEL TCAV VT = 20 MV @ 21 MW
  elabs TCAV VT = 1 MV @ 0.137 MW
  Scaling is required
The design process for elabs's TCAV procedure is complete.
 | E-labs TCAV
Beam energy | 70 MeV
Operating freq. | 2856 MHz
Freq. mode | HEM110
Phase shift a cell | 120 deg
Shunt Impedance | 28.7 MΩ/m
Input Power | 137 kW
Deflecting voltage | 1 MV
Cavity length | ~ 0.5 m

## Slide 9: 3. Optimization elabs beamline
② σoff
TCAV OFF, drift region
TCAV ON
* Temporal resolution
Not
cavity length
① Beam energy
② Beam size at screen without kick.
③ Deflection factor
Tunable parameters
More input power is required for high VT ()
  VT = 2 MV for P = 0.549 MW (∵ VT = 2.7 MV/)
2. Need beam size σoff = 0.1 mm at the screen.
MAD-X and ASTRA are suitable for optimization.

## Slide 10: 3. Optimization elabs beamline
<e-labs equipment layout, unit: m>
~ 0.5 m
Screen
9.7
Initial twiss parameters obtained from ASTRA.
βx0 = 16.10165;
βy0 = 15.87806;
αx0 = -2.508242;
αy0 = -2.470562;
MAD-X simulation
  Matching both beamlines
  Definition method is different.
  Optimization quadruple strengths
  Obtain optimized β, α
D
D
Q1
Q2
MAD-X
ASTRA
Optimization point

## Slide 11: 4. TCAV Resolution calculation
3. ASTRA simulation
Transverse emittance
εx = 0.4653, εy = 0.4614
σrms,x = 53.30 μm
σrms,y = 52.83 μm
Target: 100 um
Result: σrms,y = 52.83 μm
 σt,res = 412.45 fs for VT = 1 MV.
Quadruple region
Screen

## Slide 12: Summary and plans
0. Be sure to check example files in addition to the manuals.
Simulation(MAD-X, ASTRA) code for elabs including TCAV was completed.
Resolution calculation was done. (σt,res= 412.45 fs)
But, it needs to check the simulation results.
Considering the other simulation conditions.
Drawing deflecting voltage w.r.t phase.
Study on Longitudinal Phase Space (LPS)