## Slide 1: First Lasing of A Cavity based XFEL .
1st Hard X-ray Self-seeded FEL workshop, PAL-XFEL, Pohang
Patrick Rauer on behalf of the CBXFEL@EuXFEL team

## Slide 2: The CBXFEL @EuXFEL Team

## Slide 3: The CBXFEL @EuXFEL Team
Winfried Decking
Dirk Lipka
Patrick Rauer
Matthias Scholz
Marc Guetg
Daniel Thoden
Frank Mayet
Torsten Wohlenberg
Lukas Müller
Jörg Roßbach
Immo Bahns Sara Casalbuoni Massimiliano Di Felice Martin Dommach Bertram Friedrich Jan Grünert Wolfgang Freund Ivars Kapic | Suren Karabekyan Andreas Koch Daniele La Civita Liubov Samoylova Harald Sinn Maurizio Vannoni Allesandro Silenzi Jia Liu Naresh Kujala

## Slide 4: Cavity Based X-ray FELs
SASE vs. CBXFEL
CBXFEL
  Small Bandwidth
  Very high peak spectral density
  ~full pulse coherence (3D)
  Nearly transform limited
Possible use cases
  Time resolved Inelastic (Hard) X-ray Scattering (IXS + RIXS)
  Nuclear Resonance Spectroscopy
  High peak power applications
  Moving closer to optical lasers —> Development potential (X-ray frequency comb etc.)

## Slide 5: Cavity Based X-ray FELs
Longitudinal matching: Matching between electron bunch repetition and photon pulse round trip time
  Normal conducting linac: 100 Hz repetition rate ↔ >1E6m optical path length (orbital XFELO?)
  EuXFEL/LCLS-II/Shine: electron bunch repetition rate ~0.1 - 4.5 MHz↔ 66-2800 m optical path length
Transverse matching between electron bunches and photon pulses after at each repetition
  µm -scale electron and photon pulses ← Tens of nrad angular resolution for 100m optical path length
The Challenge of Electron-Photon Matching
Burst Mode: No Steady State

## Slide 6: A CBXFEL Demonstrator for the European XFEL
Proof-of-concept experiment at the end of SASE1 tunnel

## Slide 7: A CBXFEL Demonstrator for the European XFEL
37 cm
Radiators
Last 4 SASE Undulators
Aligned to 10 µm
X-Ray Cavity
For demo experiment as simple as possible
Crystal in backscattering geometry (no wavelength tunability  7keV)
Mirrors for guidance and focusing
Retro-reflector to reduce sensitivity to angular errors (nrad tolerance)
Return Beam in same vacuum pipe as SASE/electron beam
Length matched to 2.2 MHz and adjustable with sub-µm precision – while keeping nrad angular reproducibility!
Accelerator
High repetition rate (2.2 MHz)
High energy (14 GeV)
Long. and trans. ultra stable (6 fs, 1 µm)
Diagnostics
Spectrometer
Gas Monitor
Diode
Imagers
Lasing of a Cavity Based X-ray Source
Patrick Rauer, Immo Bahns, …, Harald Sinn (submitted)

## Slide 8: A CBXFEL Demonstrator for the European XFEL
Step by step tracking through individual components using pre-defined positions on screen.
Transverse scanning of KB apertures to maximize transmission
Experimental Realization: Alignment using YAG:Ce
YAG:Ce
YAG:Ce

## Slide 9: A CBXFEL Demonstrator for the European XFEL
Final alignment by maximizing cavity effiency (cold-cavity ringdown): ∆Θ~100 nrad
time consecutive bursts
Experimental Realization: Alignment using Intra-Cavity Photodiode
Grating
Photodiode
100 bunches going through cavity | ring down (6 cycles after opt.)
Cavity Reflectivity ~ 75%

## Slide 10: A CBXFEL Demonstrator for the European XFEL
time consecutive bursts tuning of cavity length
Experimental Realization: Matching Cavity Length
100 bunches going through cavity | ring down (6 cycles)
Saturation of Diode

## Slide 11: A CBXFEL Demonstrator for the European XFEL
Experimental Realization: Spectrum
Spectrometer

## Slide 12: A CBXFEL Demonstrator for the European XFEL
Experimental Realization: Alignment using Intra-Cavity Photodiode
Heat load limits output power

## Slide 13: A CBXFEL Demonstrator for the European XFEL
What’s Next?
Reproduce results (should be faster, as we have the longitudinal distance and a proven method)
Better characterize the radiation: Time domain measurement, wavefront characterization, ...
„Cryogenic“ Cooling (~70K)
77K with high gain: 1mJ transmitted
77K with low gain: 100µJ but stable

## Slide 14: Thank You!

## Slide 15: Backup

## Slide 17: RetroReflector
Surface curvature to achieve focussing
All three mirrors at 90°  Retroreflector:
   Decoupling from outer vibrations

## Slide 18: Outcoupling
Using “short” (10fs) electron bunches
  Regular operation mode of EUXFEL

## Slide 19: Phase Locked CBXFEL
Also see:
M. Singleton et al., Instruments 8.1 (2023): 2

## Slide 20: The Problem of Heat Load
The Problem of Heat Load

## Slide 21: The Problem of Heat Load
Heating at full pulse energy much too high
  Does the CBXFEL reach a stable state at lower pulse energies in fully coupled simulation?
mJ pulse
Saturated CBXFEL  ~10 mJ pulse energy incident on crystal at 2 MHz rate
  Disturbing optical stability (heat bump and long-term vibrations)
  Disturbing the crystal spectral reflectivity

## Slide 22: Thermal Response
No stable operation
Periodically reoccurring intense pulses
Interesting for experimental setup

## Slide 23: Thermal Response
No stable operation
Periodically reoccurring intense pulses
Interesting for experimental setup

## Slide 24: Thermal Response
Increasing cavity losses (grating scheme)
Simulation results | 
Transmitted (grating) | 
Sat. pulse energy | 0.16(1) mJ
Spectral Q density | ~30 µJ/THz
Brilliance | 1.9(2)*1033
Transmitted (cryst) | 
Sat. pulse energy | 0.15(2) mJ
Spectral Q density | ~4 µJ/THz
Brilliance | 1.7(4)*1033
SASE | 
Sat. pulse energy | ~3 mJ
Spectral Q density | ~0.5 µJ/THz
Brilliance | ~5*1033
Stable operation can be achieved (with reduced pulse energy)
Reducing FEL gain

## Slide 25: Thermal Response with Thermoelasticity
Thermoelastic Response

## Slide 26: Thermal Response (with thermoelasticity)

## Slide 27: Thermal Response with Thermoelasticity

## Slide 28: Outcoupling
Cavity/mirror based + electron beam based + cavity dump

## Slide 29: Cavity Based X-ray FELs
Outcoupling (No claim on completeness)
By X-ray Optics (akin optical lasers)
  Thin crystals (down to single µm!) [XFELO]
  Diffractive grating | crystal beam splitter [X+X]
  “Holy” crystal [XRAFEL]
Kolodiej et al., J. Appl. Cryst. 49 (2016), 1240–1244

## Slide 30: Cavity Based X-ray FELs
Outcoupling (No claim on completeness)
By Electron Phase Space Distribution [XRAFEL]
  Short electron bunches ()

## Slide 31: Cavity Based X-ray FELs
Outcoupling (No claim on completeness)
By Electron Phase Space Distribution [XRAFEL]
  Short electron bunches ()
  Use chirped (frequency-shift)/compressed electron beam (increased bandwidth)
Tang et al., PRAB 25 (2022), 08070

## Slide 32: Cavity Based X-ray FELs
Outcoupling (No claim on completeness)
By Electron Phase Space Distribution [XRAFEL]
  Short electron bunches ()
  Use chirped/compressed electron beam
  Use microbunch rotation + afterburner
Margraf et al., Proc. of IPAC2020, WEVIR03

## Slide 33: Cavity Based X-ray FELs
Outcoupling (No claim on completeness)
Cavity dump (single shot, close to 100% outcoupling)
  Single shot increased electron chirp [XRAFEL]
  Pulsed crystal heating by external laser [X+X]
  Passive crystal heating [X+X]

## Slide 34: Wavelength tunability for XFELOs
  At XFELOs: Wavelength fixed by Bragg Angle ƟB
  Problem for wavelength tuning: ƟB needs to be the same for all crystals (assuming same reflection order), while also keeping the total path lengths stable —> For cavities with nCrystal<=4, we need huge translational travel ranges or have very limited tunability
  Idea: Extent to six mirrors and opening to all three dimensions
Yuri Shyd‘ko, Feasibility of X-Ray Cavities for Free Electron Laser Oscillators, ICFA Beam Dynamics Newsletter, vol. 60, 2013.
Feasibility of X-Ray Cavities for Free Electron Laser Oscillators
Yuri Shyd’ko, IFCA Beam Dynamics Newsletter 60, 71-83 (2013)
Notes: Ich versichere, dass ich die Disputation selbstständig ohne die Unterstützung Dritter absolviere und keine unerlaubten Hilfsmittel verwende. Mir ist bewusst dass, sollte während der Disputation ein Täuschungsversuch festgestellt werden, die Prüfung sofort abgebrochen und als „nicht bestanden“ bewertet wird.“

## Slide 35: Wavelength tunability for XFELOs
  Six Mirror cavity:
  Crystals C1(')/C3(') in x-z plane, with fixed spaxing Hx in x, but same z and y
  Crystal C2(') with tunable offsets Hy in y and Hz in z and fixed offset Hx/2 in x
  Same angle ƟB for all crystals if (= rotation around x;y-axis of crystal Ci): , , ,,
Notes: Ich versichere, dass ich die Disputation selbstständig ohne die Unterstützung Dritter absolviere und keine unerlaubten Hilfsmittel verwende. Mir ist bewusst dass, sollte während der Disputation ein Täuschungsversuch festgestellt werden, die Prüfung sofort abgebrochen und als „nicht bestanden“ bewertet wird.“

## Slide 36: Wavelength tunability for XFELOs
  Six Mirror cavity:
  When changing ƟB, offset Hy in y and Hz in z for crystal C2 and C2' need to be changed. Also, in order to keep the total cavity length LC, the z-position of all downstream Crystals C1-3 need to be changed by ΔL: , ,
  All offsets scale proportional with Hx: The smaller the Hx, the smaller the necessary range in other offsets
Notes: Ich versichere, dass ich die Disputation selbstständig ohne die Unterstützung Dritter absolviere und keine unerlaubten Hilfsmittel verwende. Mir ist bewusst dass, sollte während der Disputation ein Täuschungsversuch festgestellt werden, die Prüfung sofort abgebrochen und als „nicht bestanden“ bewertet wird.“

## Slide 37: Wavelength tunability for XFELOs
  Import note: The angle for
Notes: Ich versichere, dass ich die Disputation selbstständig ohne die Unterstützung Dritter absolviere und keine unerlaubten Hilfsmittel verwende. Mir ist bewusst dass, sollte während der Disputation ein Täuschungsversuch festgestellt werden, die Prüfung sofort abgebrochen und als „nicht bestanden“ bewertet wird.“

## Slide 38: CBXFEL – fixed wavelength
If tunability too mechanically demanding
Fixed photon energies [eV] |  | Reflection order |  |  | 
 |  | C<400> | C<111> | C<333> | C<444>
Cavity geometry | 4 mirrors°) | 8950 | 4250 | 12770 | 17000
 | 3 mirrors °) | 8027. | 3467 | 10428 | 13900
 | 2 mirrors °) | 6952 | 3010 | 9030 | 12040
 | 6 mirrors °) | 7200-12100 | 3100-5250 | 9350-15745 | 12470-21000
Fixed photon energies [eV] |  | Reflection order |  |  | 
 |  | C<400> | C<111> | C<333> | C<444>
Cavity geometry |  | 8950 | 4250 | 12770 | 17000
 |  | 8027. | 3467 | 10428 | 13900
 |  | 6952 | 3010 | 9030 | 12040
 |  | 7200-12100 | 3100-5250 | 9350-15745 | 12470-21000

## Slide 39: A Cavity Based X-ray FEL Demonstrator for the European XFEL
Start-2-End Modeling of a CBXFEL: Three Fully Coupled Submodules
FEL Process
X-ray Propagation
X-ray Crystal Interaction

## Slide 40: A Cavity Based X-ray FEL Demonstrator for the European XFEL
Start-2-End Modeling of a CBXFEL: Four Submodules
FEL Process
X-ray Propagation
X-ray Crystal Interaction
Electron Dynamics
  Based on Start-2-End Simulations by I. Zagarodnov et al.
Igor Zagorodnov et al., Accelerator beam dynamics at the European X-ray Free Electron Laser, PRAB (2019)
Simulation parameters | 
Electron Energy | 16 GeV
Bunch Charge | 250 pC
FODO | 32 m

## Slide 41: A Cavity Based X-ray FEL Demonstrator for the European XFEL
Start-2-End Modeling of a CBXFEL: Three Fully Coupled Submodules (+1)
FEL Process
  Using Genesis-1.3 (V4)
    Well known and benchmarked
    Parallelized and fast
    Many tunable parameters and adjustable errors
X-ray Propagation
  Self-written parallel X-ray Cavity Propagator (pXCP)
    Based on Fourier Optics
    Very fast on (Maxwell) Cluster
    Very versatile (adjustable optics and error sources)
X-ray Crystal Interaction
  X-ray reflection based on (two beam) dynamic diffraction
  Crystal thermal response using COMSOL Multiphysics®

## Slide 42: Numerical Framework
Benchmark
Genesis-1.3
  Good agreement with analytic approximation (M.Xie)
pXCP
  Square Beam
  Gaussian Beam approximation
  Ocelot
  Transverse gaussian resonator modes
X-ray diffraction
  Strained crystal with V.A. Bushuev
Thermal Response
  Room temperature analytic response

## Slide 43: Cavity Based X-ray FELs
Some Semantics: XFELO vs XRAFEL
XFELO (X-ray Free Electron Laser Oscillator)
XRAFEL (X-ray Regenerative Amplifier FEL)
Low gain device ()
  Saturation after > hundreds of roundtrips
Output determined by cavity characteristics
Less power, more stable + monochromatic
Major advantage: Very close to optical laser oscillators  Huge development potential (frequency comb XFELO, …)
Intermediate to high gain device ( to )
  Saturation after 5 to some tens of roundtrips
Output determined by (seeded!) FEL process
More power, less stable
Major advantage(s): Easier to realize and can make use of developments in high gain FEL physics

## Slide 44: X-ray Diffraction
nBeam diffraction

## Slide 45: Background on thermal response
Heatload distribution + advantage of low T + boundary scattering + reduced + size of heat source + diamond probs

## Slide 46: X-ray crystal interaction
(approximation)
strained crystal:
Heat absorption

## Slide 47: A Cavity Based X-ray FEL Demonstrator at the European XFEL
The Problem of Heat Load  Low Crystal Temperatures
Thermal strain versus excess energy:
Severely increased heat transport at low
  Lowered due to boundary scattering
Dynamic elasticity mostly determined by strain directly after absorption (~no benefit of cooling)
small

## Slide 48: Nanoscale Thermal Conductivity
Boundary Scattering
Increase of phonon mean free path at low T
  Phonons can reach the crystal boundary without scattering
  Reflection can occur specularly (no impact on thermal conductivity in radial direction) or diffusively (same as point defect)
  A 100% diffusive scattering is assumed

## Slide 49: Nanoscale Thermal Conductivity
Using First-Principles Program ALMABTE
  Mode resolved scattering time/length
  Additional shape dependent boundary scattering term

## Slide 50: Nanoscale Thermal Conductivity
Using First-Principles Program ALMABTE
  Mode resolved scattering time/length
  Additional shape dependent boundary scattering term