## Slide 1
Comparison same bunch and fresh bunch self-seeding at PAL
MyungHoon Cho, Chang-Kyu Sung, Chi Hyun Shim, Gyujin Kim, Yeong Jin Suh, Donghyun Na, Haeryong Yang, Kook-Jin Moon, Seongyeol Kim, Hoon Heo
2025-10-16

## Slide 2
self-seeding crystal
Fresh Slice and Self-Seeding Scheme
Combining self-seeding and fresh slice schemes
Transverse deflection using a corrugated plate (dechirper).
Forward Bragg Diffraction for self-seeding.

## Slide 3
Fresh Slice and Self-Seeding Scheme
LCLS already demonstrated the fresh slice self-seeding.
Shorten FEL duration was measured by X-TCAV.
Proceedings of NAPAC, TUB3CO03 (2016)
APPLIED PHYSICS LETTERS 110, 154101 (2017)

## Slide 4
Hard X-ray Self-Seeding at PAL
Picture of self-seeding section
Gyujin Kim
Control
Sunghoon Kwon
Laser Heater
4 X 5 mm size Diamond crystals
100 μm [100] orientation
30 μm [110] orientation
Since installed the self-Seeding monochromator in 2018, many efforts are dedicated to operate in stable and to generate high intensity.

## Slide 5
Hard X-ray Self-Seeding at PAL
Some features of PAL-XFEL.
Mechanical collimator at BC1 (operational up to 60 Hz)
- eliminating head and tail horn of the electron beam.
- unwanted head part (high emittance and high current) can be eliminated.
- it help to make a flat current profile and low energy chirp.
Electron beam matching at acceleration and undulators
Efficient laser heater
- required laser heater energy :
6 uJ for SASE
> 40 uJ for SS
head
tail
lasing part
Slice emittance at L1
energy
time

## Slide 6
Parameter | Value
h | 500 µm
p | 500 µm
t | 250 µm
a | variable
b | variable
length | 1 m
Dechirper Structure
Positioned before undulators.
- Two flat and corrugated plates (dechirper)
Donghyun Na
Install, Vacuum
Yeong Jin Suh
Install, Vacuum

## Slide 7
Elegant Simulation at just after dechirper
Parameters - b=450 um
- beam energy = 4.2 GeV
Beam position measurement after performing dechirper
To calculate deflection, Bane’s model is used
PRAB 19 084401 (2016)
Electron Beam Deflection
To confirm deflection, we compared electron beam position after the dechirper.
Numerical model of deflection and tracking simulation has well agreement with BPM measurement.
 Good Dechirper alignment
Head
Tail
y
Undulator on-axis line (lasing)
Particle distribution by simulation (elegant)
DECH OFF
DECH ON

## Slide 8
Alignment of the local Electron Beam
Using vertical deflection, specific slice section should be aligned at the undulator axis.
C factor parameter is used.
The center of mass (COM) or value of BPM will be a target of position feedback.
C factor scan (FEL intensity)

## Slide 9
Fresh Slice FEL
Overlapping the seed and e-beam head slice is done by the Chicane at the Self-Seeding section.
 Resulting FEL durations is shorten.
overlap
Fresh slice (2.47 keV)
SASE (2.47 keV)
18.05 fs (RMS)
9.19 fs (RMS)
NIMA 1076 170458 (2025)
 Chicane scan shows FEL duration.
8 units
13 units

## Slide 10
Self-seeding FEL
Hard X-ray Self-Seeding is possible at with 100 m crystal, with 30 m crystal.
We tested with 100 m crystal at .
SASE FEL beam duration : 29.74 fs
We assume FEL beam duration 29.74 fs at SS.
Self-seeding intensity : 759

## Slide 11
Fresh slice SS FEL duration : 18.1 fs
SS FEL duration : 29.7 fs
Fresh Slice Self-seeding FEL
C factor scan at 9 keV
head
tail
Delay scan at SS FEL
Fresh Slice Self-Seeding is performed at
Fresh slice FEL : C factor 1.8 for the head, 0.4 for the tail.
Fresh slice SS : shorten duration compared SS.
Optimal delay is different between the SS and the fresh slice SS.  we may try with 30 um crystal in future.

## Slide 12
Fresh Slice Self-seeding FEL
1ST
2ND
1ST
2ND
2 stage undulator taper.
Intensity : 355

## Slide 13
Electron Beam Phase Space Measurement
PAL-XFEL try to measure a phase space of e-beam using the dechiper.
Below is an example of the soft x-ray beam line measurement at the dump screen.
For hard X-ray, the dechirper plate should be rotated to 90 deg.
deconvolution method
numerical analysis
FEL duration : 19.4 fs (FWHM)
Intensity : 144

## Slide 14
1. Fresh slice self-seeding was successfully demonstrated at 9 keV.
2. Flat top current profile is good to predict the gap between the electron beam and the dechirper plate.
3. The deflection C factor was used to control a targeted local part of electron beam.
4. The obtained fresh slice SS duration was 18 fs, which was 60 % of SS duration 30 fs.
The averaged power is still 78% of SS power.
 we need further activity to increase a peak power.
Summary

## Slide 15
Future work
1. Fresh slice optimization at 5 keV, 7 keV, 9 keV, and higher.
After making 2.5 keV with 1 mJ intensity, FEL intensity was not satisfied at higher photon energy.
2. Self-seeding at low photon energy
Using crystal for 3.5 keV FEL, optimizing fresh slice self-seeding.
3. Matching optimal delay of self-seeding and fresh slice.
Ex) 20 fs delay of fresh slice, 40 fs of maximum self-seeding intensity.
Finding different crystal orientation (shorter wakefield period).
Fresh slice with longer electron beam.
4. Electron beam diagnostics using new dechirper at hard x-ray line.
Measuring electron beam phase space will give confidence to our activity.