## Slide 1
20250110 Group Meeting
20250110 Group Meeting
10, Jan 2025
Minseo Jeong

## Slide 2
2
20250110 Group Meeting
Outline
Laser System of PAL-eLabs
Experiment Progress
GPT Simulation Code

## Slide 3
Laser System of PAL-eLabs
20250110 Group Meeting
3
Photogun laser: Used to generate electron bunches by photoelectron effect
Pump laser: Used in pump-probe spectroscopy (scheme used to measure ultrafast phenomena)

## Slide 4
Oscillator
Compressor
Amplifier
Stretcher
THG/FHG
Photo-
cathode
Spatial/
temporal shaping
Vacuum pipe
CPA
Laser System of PAL-eLabs
20250110 Group Meeting
4

## Slide 5
Laser System of PAL-eLabs
20250110 Group Meeting
5
Material | Ti-Sapphire laser(800nm)
Pulse energy | 7mJ(IR) / >500μJ(UV)
Oscillator repetition rate | 79.333MHz
Pulse repetition rate | 120Hz
Spot size | 100μm(FWHM, variable)
Pulse duration | ~150fs
Wavelength on the photocathode | 266nm

## Slide 6
Ultrafast Electron Diffraction(UED)
20250110 Group Meeting
6
Pump-probe imaging technique based on optical pump-probe spectroscopy and electron diffraction caused by ultrafast electron
D. Filippetto et al. Rev. Mod. Phys. (2022).

## Slide 7
Experiment Progress
20250110 Group Meeting
7

## Slide 8
GPT Simulation Code
20250110 Group Meeting
8
General Particle Tracer(GPT): Beam simulation code which tracks charged particles in electromagnetic field

## Slide 9
GPT Simulation Code
20250110 Group Meeting
9
Batch file: A file that contains instructions to run GPT
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 10
GPT Simulation Code
20250110 Group Meeting
10
Plotting Graph

## Slide 11
GPT Simulation Code
20250110 Group Meeting
11
Plotting field profile: By positioning a line of on-axis particles using setstartline at t=0

## Slide 12
GPT Simulation Code
20250110 Group Meeting
11
Bunch charge | 75fC
Initial pulse length | 26fs(rms)
Beam size | 100μm(FWHM)

## Slide 13
GPT Simulation Code
20250110 Group Meeting
11
Cavity frequency | 2.856GHz
Gun gradient | 82.84MV/m(max)
UV pump pulse duration | ~150fs
Solenoid 1 position | 0.196m
Solenoid 1 strength | 0.180T(max)
Solenoid 2 position | 1.26m
Solenoid 2 strength | 0.0959T(max)
Aperture position | 0.55m
Aperture diameter | 400μm
Detector position | 5.00m

## Slide 14
GPT Simulation Code
20250110 Group Meeting
12
Plot of energy of electron beam

## Slide 15
GPT Simulation Code
20250110 Group Meeting
13
Plot of beam size(rms)

## Slide 16
GPT Simulation Code
20250110 Group Meeting
14
Field plot by ASTRA

## Slide 17
GPT Simulation Code
20250110 Group Meeting
15
Changing the phase to φ=2°

## Slide 18
GPT Simulation Code
20250110 Group Meeting
16
Changing the phase to φ=-2°

## Slide 19
GPT Simulation Code
20250110 Group Meeting
17
Plot of emittance of electron bunch

## Slide 20
Future Plan
20250110 Group Meeting
18
Generating multiple dataset for training of ML
Coding the source code for ML
Participating in UED experiment

## Slide 21
Thank you!
20250110 Group Meeting

## Slide 22
GPT Simulation Code
-PAL-eLabs UED Facility Setup
20250110 Group Meeting
20

## Slide 23
GPT Simulation Code
-PAL-eLabs UED Facility Setup
20250110 Group Meeting
21